EDEWG Change Request #065

This EDEWG Change Request can be found on the PUC website at http://www.puc.state.pa.us/electric/electric_edewg_download.aspx

| Requester’s Name: Ernie Mathie | EDC/EGS Name: FirstEnergy | Phone # : 330-384-5757 |
| --- | --- | --- |
| Date of Request: 05/7/10 | Affected EDI Transaction Set #(s): 814ER, 814C, 867HIU, 867HU | E-Mail Address: mathiee@firstenergycorp.com |
| Requested Priority (emergency/high/low): High | Requested Implementation Date: 08/10 | Status: Implemented in v3.1.1D/v1.1D |

Brief Explanation (This will be copied into the description in the Change Control Summary Spreadsheet):  Add REF loops for Loss Factor and Service Voltage to 814 enrollment response, 814 change, 867 historical usage, and 867 historical interval usage.  Loss Factors will be numeric values that vary by rate class as set forth in the Electric Generation Supplier Coordination Tariff reflecting system line losses associated with delivering usage.  kWh usage is multiplied by this factor to determine the actual kwh’s that need to be generated to serve the customer.  Service Voltage is the line voltage an account is served at and will be either alpha or numeric.  For example, most residential accounts will have a service voltage of secondary but larger commercial/industrial accounts could be served at a transmission level such as 34.5kV.

These changes would be for FirstEnergy only and should be indicated as such on the respective pages and lines.

Detail Explanation  (Exactly what change is required? To which EDEWG Standards? Why?):

814 Enrollment Response:  add REF*LF*Loss Factor and REF*SV*Service Voltage under the N1*MQ loop

814 Change Request:  add REF*LF*Loss Factor and REF*SV*Service Voltage under the N1*MQ loop

814 Change Request:  in REF*TD under N1*MQ add REFLF for Change Loss Factor and REFSV for Change Service Voltage

867 Historical Usage & 867 Historical Interval Usage:  in PTD*FG add REF*LF for Loss Factor and REF*SV for Service Voltage

Added recommended updates to IG…

p.2 – REFLF addition to 814E and 814C

p.3 – REFSV addition to 814E and 814C

p.4 – REFTD updates for 814C

p.5 - REFLF addition to 867s

p.6 – REFSV addition to 867s

For Change Control Manager Use Only:

| Date of EDEWG Discussion: 5/13/10 | Expected Implementation Date: 8/31/10 |  |
| --- | --- | --- |

EDEWG Discussion and Resolution:

5/10/10-Brandon Siegel:  Reviewed change, entered into Change Control log, and assigned #065.  Placed on agenda for 5/13 EDEWG meeting.

5/13/10-Brandon Siegel:  EDEWG discussed and approved CC65 which will be incorporated into the next revision of the PA EDI Implementation Guidelines.

7/22/2010-Brandon Siegel:  Upon request, added the below samples for how these segments will be incorporated into the IGs.

Priority Classifications

| Emergency Priority | Implemented within 10 days or otherwise directed by EDEWG |
| --- | --- |
| High Priority | Changes / Enhancements implemented with 30 days. The next release, or as otherwise directed by EDEWG |
| Low Priority | Changes / Enhancements implemented no earlier than 90 days, Future Release, or as otherwise directed by EDEWG |

Please submit this form via e-mail to both the PUC at annmarino@state.pa.us and to the

Change Control Manager, Brandon Siegel at brandon.siegel@ista-na.com

Your request will be evaluated and prioritized at an upcoming EDEWG meeting or conference call.

## Segment:	REF Reference Identification (LF=Loss Factor)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | Request: CE Accept Response: All other Accept Responses: Reject Response: | Not Used Required for First Energy Companies Optional for others Not Used Not Used |
| --- | --- | --- | --- |
| NJ Use: |  | Same as PA; JCP&L only |
| DE Use: |  | Not Used |
| MD Use: |  | Not Used |
| Example: |  | REF*LF*2 |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | LF |  | Load Planning Number |
|  | Loss Factor |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |

## Segment:	REF Reference Identification (SV=Service Voltage)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | Request: CE Accept Response: All other Accept Responses: Reject Response: | Not Used Required for First Energy Companies Optional for others Not Used Not Used |
| --- | --- | --- | --- |
| NJ Use: |  | Not Used |
| DE Use: |  | Not Used |
| MD Use: |  | Not Used |
| Example: |  | REF*SV*SECONDARY |

Data Element Summary

Ref.	Data

Des.	Element	Name	X12 Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | SV |  | Service Charge Number |
|  | Service Voltage |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |

PRIMARY

SECONDARY

Actual service voltage transmission value (Ex:  34.5kV)

## Segment:	REF Reference Identification (TD=Reason for Change –Meter Level)

Position:	130

Loop:	NM1

Level:	Detail

Usage:	Optional

Max Use:	>1

Purpose:	To specify identifying information

Syntax Notes:	At least one of REF02 or REF03 is required.

If either C04003 or C04004 is present, then the other is required.

If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	REF04 contains data relating to the value cited in REF02.

Comments:

| UIG Notes: |  | This convention of the REF segment is used for Account Maintenance and Update transactions, to convey meter-level and entity relationship change reason codes. The codes used in REF02 are maintained by the UIG. The first portion of the code identifies the segment that contains the data that has been changed; the remaining portion of the code identifies the relevant code qualifier for the data that has been changed. The changed data will appear in the appropriate element of the identified segment. For example, REF02 code of REFVR indicates that data in the REF segment that is identified by the qualifier VR (i.e. Meter Installer) has been changed to the value now shown in REF02 of the REF*VR segment. |
| --- | --- | --- |
| PA Use: |  | Request: Response: | Required if change is at a meter level Optional |
| NJ Use: |  | Same as PA |
| DE Use: |  | Same as PA |
| MD Use: |  | Same as PA |
| Example: |  | REF*TD*REFRB |

Data Element Summary

Ref.	Data

Des.	Element	Name	Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | TD |  | Reason for Change |
|  | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |
|  | NM1MA |  | Meter Addition |
|  | NM1MQ |  | Change Metering Location |
|  | Change of Meter Attributes: Meter Constant (REF*4P), Number of Dials (REF*IX), Meter Type (REF*MT) and Consumption Provided on 867 (REF*TU) |
|  | NM1MR |  | Meter Removal |
|  | NM1MX REFLF |  | Meter Exchange Change Load Factor |
|  | REFLO |  | Change Load Profile |
|  | REFNH |  | Change Utility Rate Class or Tariff |
|  | REFPR |  | Change Unit Pricing Category Under a Rate Code |
|  | REFRB REFSV |  | Change ESP Rate Change Service Voltage |
|  | REFTZ |  | Change Meter Cycle |
|  | REF03 | 352 | Description | X | AN 1/80 |
|  | A free-form description to clarify the related data elements and their content |

## Segment:      	REF Reference Identification (LF=Load Factor)

Position:	030

Loop:	PTD

Level:	Detail

Usage:	Optional

Max Use:	20

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | Optional; provided by First Energy Operating Companies |
| --- | --- | --- |
| NJ Use: |  | Not Used |
| DE Use: |  | Not Used |
| MD Use: |  | Not Used |
| Example: |  | REF*LF*2 |

Data Element Summary

Ref.	Data

Des.	Element	Name	Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | LF |  | Load Factor |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |

## Segment:      	REF Reference Identification (SV=Service Voltage)

Position:	030

Loop:	PTD

Level:	Detail

Usage:	Optional

Max Use:	20

Purpose:	To specify identifying information

Syntax Notes:	1	At least one of REF02 or REF03 is required.

2	If either C04003 or C04004 is present, then the other is required.

3	If either C04005 or C04006 is present, then the other is required.

Semantic Notes:	1	REF04 contains data relating to the value cited in REF02.

Comments:

| PA Use: |  | Optional; provided by First Energy Operating Companies |
| --- | --- | --- |
| NJ Use: |  | Not Used |
| DE Use: |  | Not Used |
| MD Use: |  | Not Used |
| Example: |  | REF*SV*SECONDARY |

Data Element Summary

Ref.	Data

Des.	Element	Name	Attributes

| Must Use | REF01 | 128 | Reference Identification Qualifier | M | ID 2/3 |
| --- | --- | --- | --- | --- | --- |
|  | Code qualifying the Reference Identification |
|  | SV |  | Service Voltage |
| Must Use | REF02 | 127 | Reference Identification | X | AN 1/30 |
|  | Reference information as defined for a particular Transaction Set or as specified by the Reference Identification Qualifier |

PRIMARY

SECONDARY

Actual service voltage transmission value (Ex:  34.5kV)