|  | PENNSYLVANIA PUBLIC UTILITY COMMISSION Harrisburg, PA. 17105-3265 |  |
| --- | --- | --- |

|  | Public Meeting held May 28, 2009 |
| --- | --- |
| Commissioners Present: |  |

| James H. Cawley, Chairman |  |
| --- | --- |
| Tyrone J. Christy, Vice Chairman |  |
| Kim Pizzingrilli |  |
| Wayne E. Gardner |  |
| Robert F. Powelson |  |
| Implementation of the Alternative Energy Portfolio Standards Act of 2004: Standards for the Participation of Demand Side Management Resources – Technical Reference Manual Update | Docket No. M-00051865 |

ORDER

BY THE COMMISSION:

In implementing the Alternative Energy Portfolio Standards Act, 73 P.S. §§ 1648.1 – 1648.8, this Commission had previously adopted an Energy-Efficiency and DSM Rules for Pennsylvania’s Alternative Energy Portfolio Standard, Technical Reference Manual (“TRM”).  In adopting the original version of the TRM, this Commission directed the Bureau of Conservation, Economics and Energy Planning (“CEEP”) to oversee the implementation, maintenance and periodic updating of the TRM.  Additionally, in the Energy Efficiency and Conservation Program Implementation Order, this Commission adopted the TRM as a component of the Energy Efficiency and Conservation (“EE&C”) Program evaluation process.  In that Implementation Order, this Commission also noted that “as the TRM was initially created to fulfill requirements of the AEPS Act, it will need to be updated and expanded to fulfill the requirements of the EE&C provisions of Act 129.”  Soon after the adoption of the EE&C Program Implementation Order, Commission staff initiated a collaborative process to review and update the TRM with the purpose of supporting both the AEPS Act and the Act 129 EE&C program.  With this Order, the Commission adopts the 2009 version of the TRM as contained in the Annex to this Order.

BACKGROUND

On February 20, 2009, this Commission issued a Secretarial Letter seeking comments on a proposed TRM update.  Comments were due March 12, 2009, with reply comments due March 27, 2009.  Commission staff also held a TRM Working Group meeting with interested stakeholders On March 24, 2009, to discuss the proposed TRM and filed comments.  At that meeting, Commission staff extended the reply comment period to March 30, 2009.

The following parties filed comments to the proposed TRM update:  Duquesne Light Co. (“Duquesne”), Elster Integrated Solutions (“Elster”), The Energy Association of Pennsylvania (“EAPA”), Lawrence E. Spielvogel, Inc. (“Spielvogel”), PECO Energy Co. (“PECO”), Positive Energy, Inc. (“Positive Energy”), PPL Electric Utilities Corp. (“PPL”), UGI Utilities, Inc. – Gas Division, UGI Penn Natural Gas, Inc. and UGI Central Penn Gas, Inc. (collectively, “UGI”), and West Penn Power Co. d/b/a Allegheny Power (“Allegheny”).

The following parties participated in the March 24, 2009, TRM Working Group meeting:  Clean Power Markets, Duquesne, the E Cubed Co., Elster, EAPA, EnerNOC, Inc. (“EnerNOC”), First Energy Corp. (“First Energy”), Honeywell Corp. (“Honeywell”), MCR Group (“MCR”), PECO, Pennsylvania Department of Environmental Protection (“DEP”), PPL, Regulatory Connection, and UGI.

The following parties filed reply comments:  Duquesne, EAPA, EnerNOC, First Energy, Keystone Energy Efficiency Alliance (“KEEA”), PA Home Energy, PECO, Positive Energy, PPL, Allegheny.  The Commission would like to thank all of those who participated in this process.

DISCUSSION

Below, we will discuss the more significant changes and updates being made to the TRM.  Minor administrative changes will not be discussed.

A.	Dual Purpose of TRM

As noted above, the EE&C Program Implementation Order entered January 16, 2009 indicated that the Commission will utilize the TRM for the EE&C Program evaluation process requirements.  A process was initiated to expand and update the TRM to fulfill the requirements of the EE&C provisions of Act 129 as well as the requirements of the AEPS Act.  The expanded and updated TRM will be used for implementation of Act 129 and continued use for the purpose of identifying demand side management and energy efficiency (“DSM/EE”) alternative energy credit amounts for AEPS Act compliance.

We have received several comments noting that some of the draft TRM language is confusing because it relates only to either the AEPS Act or the EE&C provisions of Act 129. Comments recommend employing a means that will identify elements of the TRM that are specific to Act 129 or the AEPS Act.  In addition, we have received suggestions that the TRM include a section with definitions to aid in clarifying the elements that are specific to the AEPS Act or Act 129.

The Commission agrees that the TRM needs to indicate its dual purpose for use with the EE&C provisions of Act 129 and the AEPS Act such that it clearly indicates which elements are solely related to the AEPS Act.  As such, we have shaded those elements in the TRM that apply solely to the AEPS Act.  All non-shaded areas are applicable to both the EE&C provisions of Act 129 and the AEPS Act.

The Commission also agrees that the addition of a definitions section to the TRM would be helpful to clarify words and terms used and to identify their applicability to the AEPS Act, the EE&C provisions of Act 129, or both.  A small definitions section has been added to the TRM.

B.	Changes to Individual Measures

In this section we will address individual standard measures identified in the TRM or proposed by commenters.

1.	Energy Star Savings vs. Sales-Weighted Average

Lawrence Berkeley National Laboratory (“LBNL”) recommended adjusting the Energy Star appliance savings based on existing Federal standards as the baseline to savings adjusted for current sales-weighted average efficiencies based on the most recent Association of Home Appliance Manufacturers (“AHAM”) information.  The tables provided by LBNL that use AHAM information significantly reduced the savings estimates for refrigerators, freezers, dishwashers, room air conditioners, and residential clothes washers.

EAPA, First Energy, PECO and Duquesne recommend savings calculations based on Federal standards.  Allegheny recommends that information from industry resources and manufacturers regarding each appliance be used to determine the deemed energy savings.

The Commission will use Energy Star appliance savings based on current Federal standards for this revision of the TRM.  We note that the TRM contains deemed energy savings, EDCs are free to utilize approved custom measures for appliance replacements, as Allegheny suggests.

In addition, several commenters noted that there are updated ratings for Energy Star appliances that are not incorporated in the TRM.  These updates pertain to water heaters, heat pumps, dishwashers and clothes washers.  We have updated these ratings in Tables 7 and 10 to reflect the latest Energy Star ratings.

Finally, PECO and KEEA noted a need to allow the use of software that meets a national standard for savings’ calculations.  We agree with these comments and have incorporated language in the TRM under Residential New Construction to allow for any recognized software that meets national standards when implementing Home Performance with Energy Star.  Similarly, we have revised the language under Home Performance with Energy Star noting that software that meets national standards for savings’ calculations of whole-house approaches such as Home Performance must be used.  References for three standards are provided.

2.	Energy Star Lighting – Compact Fluorescent Lighting

LBNL recommended a reduction in the hours of use for compact fluorescent lighting (“CFL”) from 3.4 hrs/day to 2.0 hrs/day.  LBNL also recommended a reduction in the measured lifetime for CFLs, as well as a downward adjustment over time in the net-to-gross ratios of screw-in CFLs to account for the impacts of the Energy Independence and Security Act of 2007 (“EISA”).

Both EAPA and PECO recommend against adopting LBNL’s proposed changes.  They disagree with LBNL’s recommendation to reduce TRM hours of use because, the recommendation is not based on data gathered in Pennsylvania.  PECO points out that LBNL recommended a net-to-gross adjustment that is more aggressive than and inconsistent with the EISA schedule. PECO stated that the Commission should adopt net-to-gross methodology that is more reasonable and Pennsylvania specific.

The Commission rejects LBNL’s recommendations to reduce the TRM hours of use for CFLs to 2.0 hrs/day.  However, the commission will reduce the TRM hours of use for CFLs to 3.0 hrs/day based on information from the U.S. Department of Energy, Energy Star Calculator as of March 16, 2009.

The Commission agrees with EAPA and PECO that LBNL’s recommended net-to-gross ratio adjustment for screw-in CFLs is inconsistent with the EISA schedule and declines to follow LBNL’s recommendation.  However, the Commission believes that implementation of EISA requirements for standard incandescent light bulbs needs to be accounted for in energy savings EDCs claim from CFL distribution measures.  The EISA requires phasing out, over several years, the manufacturing and importation of incandescent bulbs in their current configuration by imposing new performance standards with prescribed wattage limitations.  For example, under the new standards the lumens produced from a currently available 100 watt bulb must be produced by a bulb with a maximum wattage of 72 watts.  The phased implementation begins January 1, 2012, when 100W incandescent bulbs can no longer be manufactured or imported for sale; the 75W bulb is restricted beginning January 2013; with the 60W and 40W bulbs follow in January 2014.  While the EISA prohibits the manufacture and importation of existing incandescent bulbs, it does not prohibit the sale of the phased out bulbs in stock.  The Commission recognizes that depletion of incandescent bulb existing stock will take some time and has decided to use a depletion time of five months following the effective date of a new standard established in EISA.

Therefore, the Commission directs EDCs to adjust the calculated energy savings claimed from CFL measures to reflect implementation of the EISA incandescent light bulb standards.  Specifically, the amount of energy savings reflected in the table is reduced in accordance with the new maximum wattages established by the EISA with a five month delay to account for the depletion of existing incandescent bulb stocks.  For example, if an EDC distributes 26W CFLs to replace 100W incandescent bulbs in 2010, the energy savings calculations would use 74 watts saved per bulb until June 1, 2012, but only 46 watts saved for the remaining time of the CFL measure life.

3.	LED Traffic Signals

The draft TRM included Table 16: Traffic Signals.  PECO commented that the Equivalent Full Load Hours in Table 16 were calculated using inappropriate variables and recommended removal of the table or replacement with a new table provided by PECO.  PECO’s proposed Table 16 compared incandescent and LED traffic signals.  EAPA and PPL supported the inclusion of PECO’s proposed table for traffic signals.  In its reply comments, PECO included a revised and more complete Table 16.  The Commission agrees that LED traffic light signals should be included in the TRM and has included PECO’s revised Table 16 in the TRM.

4.	Large Scale Data Analysis

Positive Energy request that the Commission include Large Scale Data Analysis (“LSDA”) as part of the revised TRM or at least allow LSDA to be used as a custom measure.  Duquesne, PECO and PPL commented that LSDA is not an appropriate measure for inclusion in the TRM.  In its reply comments, Positive Energy clarified that the Commission should accept LSDA as an appropriate evaluation, measurement and verification (“EM&V”) technique and that the TRM acknowledge the use of LSDA as such.

The Commission agrees with comments that oppose inclusion of LSDA in the TRM and recognizes Positive Energy for submitting reply comments to clarify their request.  The Commission agrees that LSDA can be considered one of many techniques that evaluators may use to measure efficiency gains.  However, the Commission does not believe that the TRM is the appropriate place to address specific EM&V measures unrelated to standard measures and will decline to include LSDA in the TRM.

5.	Smart Meters

Elster suggested that smart meters be used to collect data for use in the TRM. PECO commented that since the Commission has not issued its proposed smart meter rules, Elster’s suggestion is pre-mature.  The Commission acknowledges that special metering may be necessary to validate certain custom measures.  However, the Commission agrees with PECO and believes that smart meter issues should be addressed in the Commission’s Smart Meter Procurement and Installation plans proceeding at Docket No. M-2009-2092655.

6.	Natural Gas Fuel Switching

UGI and PECO support measures that count energy and demand savings when electric equipment is removed and replaced with equipment that uses natural gas.  PECO suggested that the Commission tentatively approve fuel switching as a potential TRM measure, pending the establishment and report of a fuel-switching sub-group.

First Energy does not support fuel switching and notes that there are many issues related to fuel switching that must be considered.  PPL suggests that fuel switching should be considered a custom measure and not included in the TRM.  EAPA supports convening a sub-group to examine the fuel switching issue and the possibility of including it in the TRM in subsequent years.

The Commission recognizes that fuel switching is a complicated topic that will require additional time and effort to fully address.  As the TRM will provide vital guidance to EDCs in developing their EE&C plans, which are due to be filed by July 1, 2009, there is not enough time to convene a working group to address all the related issues, fuel switching will not be included in this TRM. The Commission will convene a fuel switching working group in the near future to identify, research and address issues related fuel switching.  Depending on the outcome of this working group, fuel switching may be incorporated into a future version of the TRM.

7.	Additional Measures Not Included

The Commission received several comments about measures not contained in the TRM.  These comments fall into two general categories, potential standard measures not currently included in the TRM and custom measures.  We will address each general category.

PECO and Duquesne provided comments on several potential standard measures that may qualify for deemed savings calculations for future TRM updates.  These standard measures include street lighting, outdoor lighting, and home and office electronics.  Duquesne mentioned the potential for residential TVs, TV set-top boxes, DVDs and desktop computers.

The Commission fully intends to add new standard measures to the TRM as commonly accepted savings calculations become available.  We will consider such recommendations in our regular TRM update process.  Some of the specific equipment mentioned by PECO and Duquesne may be good candidates for additions to future versions of the TRM as more information becomes available.

The second general category of comments pertaining to measures not included in the TRM refers to custom measures.  EAPA commented that the TRM was missing many energy and demand savings measures such as rates and tariffs involving peak load management; e.g. time-of-use, critical peak pricing, direct load control and curtailment/interruptible load tariffs.  EAPA also noted the absence of measures for whole house/building EE&C projects.  Duquesne commented on the absence of residential retrofit measures, such as insulation, duct work, infiltration reduction and whole house performance.  Also noted by Duquesne was the absence of commercial measures such as refrigeration and commercial building retro-commissioning.

We will adopt the general approach proposed by PECO and PPL that for the purposes of the Act 129 EE&C program, custom measures should be outside of the scope of the TRM.  As noted by PPL, the TRM is intended only for standard measures that warrant standard energy efficiency calculation methods and assumptions.  More complex measures, that involve unique variables and/or whose results are measured directly, should be treated as custom measures.  Examples noted above, including residential whole house or building EE&C projects, retrofit projects, or pricing programs designed for peak demand-savings, are all considered custom measures.  The absence of these measures in the TRM should in no way discourage EDCs from proposing such measures in their EE&C plans.  The Commission fully expects that a sizeable proportion of the residential programs and perhaps a majority of the commercial and industrial programs will be based on custom measures.  The determination of energy and demand savings for EE&C program custom measures will be based on the EM&V protocols as determined by the Commission, versus the deemed savings contained in the TRM for standard measures.

Consistent with our determination to use the TRM only for standard measures, we will make several modifications to the TRM.  First, we will remove the section entitled “Blue Line Innovations-Power Cost Monitor” including Table 14 noting the reductions in electricity consumption associated with the installation of in home energy monitoring devices.  Such devices should be considered as custom measures and their savings determined through EM&V protocols.  Second, we will delete Table 15, Lighting Verification Summary as commercial and industrial lighting applications will be considered as custom measures whose savings will be determined by EM&V protocols.  Finally, we will delete Table 17 entitled Prescriptive Lighting for Commercial Customers as such applications will be considered as custom measures.

In addition, the Commission determined, based on comments and further analysis, that Table 4, “Applicable to Building Completions from January 2001 through March 2003” on page 16, and Table 6, “Energy Star Homes- REMRate User Defined Reference Homes,” on pages 19-20 of the January 2009 draft TRM are not applicable and have been eliminated from the TRM. The worksheet on page 42 is also not applicable and has been eliminated.

C.	Baseline Estimates for Measure Burnout vs. Early Retirement

The version of the TRM issued for comment noted under the heading of “Baseline Estimates” that for most efficiency measures the change in energy usage values are based on the energy use of standard new products versus new high efficiency products.  Several parties, including EAPA, PPL, PECO, Allegheny, LBNL and First Energy noted that EDC programs will likely promote the early retirement of functioning appliances or technology for which a different baseline estimate is more appropriate.

Commenters generally recommended that in the case of early retirement or retrofit measures, EDCs should use as the baseline, the estimated energy use of the existing, in place equipment.  This is in contrast with using a standard, predetermined energy use baseline for all high-efficiency refrigerator installations, regardless of the actual energy use of the refrigerator being replaced.  These commenters also recommended that this baseline be applied for a period not to exceed the remaining useful life of the equipment being replaced.

While commenters agreed on this approach for baseline estimates for early retirement or retrofit measures, there were different proposals for determining the useful life of the existing equipment.  PPL does not agree that the exact age of the appliance (as determined by the purchase date) needs to be obtained, verified or recorded to determine the specific remaining useful life to calculate savings.  PPL recommends that the TRM should assume a standard remaining life for appliances, such as eight years.  Also noting the cost and difficulty of determining the remaining useful life of equipment, First Energy suggests adopting an assumed five years of remaining useful life in the TRM, absent any other supported alterative.

Allegheny provides a different approach based on a program that their affiliate in Maryland is currently implementing.  In the Maryland program, data about the existing equipment is collected by a recycling contractor who verifies the working condition of the equipment, collects the nameplate data and provides an estimate of the energy saved by replacing the old unit.

The Commission agrees with the general comments that in the case of retrofit measures where existing, in-place equipment is replaced, EDCs should use, as the baseline, the estimated energy use of the existing in-place equipment for the remaining useful life of the existing equipment.  During this period, the energy savings would be the difference between the usage of the existing, in-place equipment, and the usage of the new high-efficiency equipment.  Once the remaining useful life of the existing equipment would have expired, the newly installed high-efficiency equipment is likely to have additional years of useful life.  For this remaining useful life of the new high-efficiency equipment, the energy savings will be the difference in energy savings from new standard equipment and the new high-efficiency equipment.  For example, if an EDC replaces an existing refrigerator that has a remaining useful life of five-years, with a new high-efficiency refrigerator that has a measure life of 15-years, then the energy savings credited during the first five-years will be the difference between the usage of the existing refrigerator and the new high-efficiency refrigerator.  For the remaining ten-years, the energy savings will be the difference between a new standard refrigerator and the new high-efficiency refrigerator.

However, we do not agree with the comments of PPL and First Energy, who recommended that we adopt a standard useful life of existing equipment, such as five or eight years.  The remaining useful life of equipment is likely to vary considerably by the type of equipment (refrigerator, freezer, HVAC) and perhaps by EDC service territory.  Initially, EDCs should adopt the general approach noted by Allegheny, where equipment-specific data is collected for the existing equipment and used to calculate the energy savings for the remaining useful life of that equipment.  At such time as EDCs have compiled sufficient experience and have sufficient data available to be able to calculate average life expectances for specific types of equipment in their service territory          (i.e. refrigerators, freezers), then they can request that the commission approve a standard useful life of x years for future use in lieu of determining useful life and energy savings on a case-by-case basis.  This approach supports the development of a useful life standard based on actual research findings consistent with the overall approach of the TRM.

We point out at this time that the measure lives of the programs as noted in Appendix A of the TRM are not to exceed fifteen years for calculations of the TRC test.  Actual useful lives of measures may be used when calculating energy savings for meeting annual energy reduction targets under the AEPS Act implementation procedures.  An asterisk will be placed next to each measure with a useful life greater than fifteen years indicating that fifteen years is the maximum number of years that can be used for the TRC test calculations, but the actual useful life may be used for AEPS Act purposes.

D.	Documented Savings for Standard Measures

Allegheny requests assurance that EDCs will not be limited to exclusive reliance on the TRM.  Allegheny noted that where EDCs implement alternative, well-documented methods to measure savings, the Commission should consider the measurement methods and add language to that effect in the TRM.

The Commission envisions two general cases where EDCs may implement measures that are not in the TRM or use the TRM values to calculate energy savings.  The first case is when custom measures are used, in which case alternative measurement methods are required to arrive at verifiable energy savings that are unique to the specific application.  The second case is where an EDC may install a standard measure that is contained in the TRM but does not wish to use the deemed energy savings values contained in the TRM.  In these cases, the EDC may use alternative, well-documented, measurements that are more robust to arrive at the energy savings.   The alternative measurement methods used will be subject to review and approval by the Commission to ensure their accuracy.  We will include language to this effect in the TRM.

E.	Weather Adjustments

The Commission received comments from numerous parties regarding the weather adjustments contained in the TRM.  For example, EAPA and PECO noted that some tables contain calculations that are inappropriately applied to measures that are not climate sensitive.  Several other commenters, such as LBNL, noted that the method used to adjust HVAC and thermal-envelope savings for climates that differ from Pennsylvania are overly simplistic.   PECO commented that the Equivalent Full-Load Hours (“EFLHs”) do not correlate with the Energy Star values.

We will adopt the position advocated by PECO and use the EFLHs provided by the U.S. Department of Energy’s Energy Star Calculator for the following seven cities in Pennsylvania:  Allentown, Erie, Harrisburg, Philadelphia, Pittsburgh, Scranton and Williamsport.  These Energy Star values will be applied to Table 3, Residential Electric HVAC; Table 10, Room Air Conditioners; and Tables 25 and 27, Commercial and Industrial HVAC, Heat Pumps and Electric Chillers.  We will also remove climate zone references in Table 16, Traffic Signals, and Table 23, Motors, as these applications are not affected by climate zone variations.

F.	Net-to-Gross Ratio Adjustments to Savings

A common consideration for determining the cost benefit of energy efficiency programs is whether to make adjustments to gross energy savings through the use of a net-to-gross (“NTG”) ratio.  The NTG ratio adjusts the cost-effectiveness results so that they only reflect those energy efficiency gains that are attributed to and are a direct result of the energy efficiency program in question.  The NTG ratio gives evaluators an estimate of savings achieved as a direct result of program expenditures by removing savings that would have occurred even absent a conservation program.

Three common factors addressed through the NTG ratio are free-riders, take-back effect, and spillover effect sometimes referred to as free-drivers.   The concept of free-riders consists of customers that may take advantage of rebates or cost savings measures available through conservation programs even though they would have installed the energy efficient measure on their own.  Take-back effect occurs when customers displace any reduction in energy bills by increasing their total energy use for comfort or convenience.  Spillover is the opposite of the free-rider effect, it occurs when customers adopt efficiency measures because they are influenced by program-related information and marketing efforts, without actually participating in the program.  Net-to-gross ratio adjustments for free-riders and take-back effects result in the reduction of claimed energy savings, whereas, spillover effects result in additions to claimed energy savings.

Most of the comments relating to NTG ratios suggested that during the first year, plans assume a NTG ratio of one, or zero, as all NTG related adjustments cancel each other out.  None of the commenters cited any studies or research that would support these assumptions.  However, it was noted that New Jersey handled the NTG ratio issue by assuming a NTG ratio of one.  The commenters also suggested that the Commission form a working group to examine this issue and look at ways to identify appropriate NTG ratios to be applied in future years.

Net-to-gross ratio adjustments are likely to be influenced by program or measure-specific applications.  The degree to which free-rider, take-back and spillover effects are present in a program is best determined by research conducted at the program-participant level.  This research comes at a cost that increases total program costs.  In addition, if adjustments are made through NTG ratios that result in reductions to claimed savings due to free-rider and take-back effects that are not cancelled out by spillover effects, then EDCs must implement additional energy efficiency measures to meet the mandated reduction targets.  While the deployment of additional reduction measures may produce incremental reductions in the cost of wholesale power, to the benefit of all customers whether they participate or not, it may be difficult to measure and correlate the wholesale power market changes to the additional energy efficiency measures.

The Commission does not necessarily agree that assuming a NTG ratio of one is correct.  However, due to the short time period to finalize the TRM prior to the EE&C plan filing deadline, we will initially assume a NTG ratio of one.  As the NTG ratio will also be a factor in the total resource cost test adopted by this Commission, we will establish a process for developing future NTG ratios in that proceeding.

G.	Future TRM Updates

We received numerous comments on the importance of updating the TRM on an annual basis.  The updates need to be finalized soon enough for use with the next year EE&C plans consistent the Commission’s EE&C program Implementation Order.  All the comments supported a draft TRM update by June 1 each year with the final revision by December 31 for use effective June 1 of the following year.

The Commission received no alternative suggestions.  We agree with the importance of a set timetable for TRM updates and direct that the Bureau of Conservation, Economics, and Energy Planning enlist whatever resources are necessary to produce a final revised TRM by December 31 of each year; to be used by EDCs as the basis for deemed energy savings in subsequent EE&C plan compliance years.

CONCLUSION

This Order represents the initial step in establishing a comprehensive TRM with a purpose of supporting both the AEPS Act and the EE&C provision of Act 129.  We extend our thanks to all who provided comments and participated in the stakeholder meeting.  THEREFORE,

IT IS ORDERED:

1.  That the 2009 Technical Reference Manual contained in the Annex to this Order is adopted and replaces the prior version of the Technical Reference Manual as of the entry date of this Order.

2.  That a copy of this Order and Annex shall be served upon the Office of Consumer Advocate, the Office of Small Business Advocate, the Office of Trial Staff, all jurisdictional electric distribution companies, all licensed electric generation suppliers, and the Pennsylvania Department of Environmental Protection.

3.  That the Secretary shall deposit a notice of this Order and Annex with the Legislative Reference Bureau for publication in the Pennsylvania Bulletin.

4.  That this Order and Annex be published on the Commission’s website.

5.  That a fuel-switching working group is established to identify, research and address issues related to including fuel-switching measures in a future Technical Reference Manual.  This working group shall provide a report to the Commission, with recommendations, by June 1, 2010.

BY THE COMMISSION

James J. McNulty

Secretary

(SEAL)

ORDER ADOPTED:  May 28, 2009

ORDER ENTERED:  June 1, 2009

Annex

Technical Reference Manual (TRM)

for

Pennsylvania Act 129

Energy Efficiency and Conservation Program

and

Act 213

Alternative Energy Portfolio Standards

Pennsylvania Public Utility Commission

May 2009

Table of Contents

Introduction ........................................................................................................... 1

Purpose .......................................................................................................................................1

Definitions 	1

General Framework	1

Algorithms	2

Data and Input Values	3

Baseline Estimates	3

Resource Savings in Current and Future Program Years	4

Prospective Application of the TRM	4

Electric Resource Savings	4

Post-Implementation Review	5

Adjustments to Energy and Resource Savings	5

Coincidence with Electric System Peak	5

Measure Retention and Persistence of Savings	5

Interaction of Energy Savings	5

Calculation of the Value of Resource Savings	6

Transmission and Distribution System Losses	6

Measure Lives	6

Custom Measures	6

Impact of Weather 	7

Algorithms for Energy Efficient Measures	7

Residential Electric HVAC	8

Algorithms	8

Central Air Conditioner (A/C) & Air Source Heat Pump (ASHP)	8

Ground Source Heat Pumps (GSHP)	9

GSHP Desuperheater	9

Furnace High Efficiency Fan	9

Residential New Construction	16

Algorithms	16

Insulation Up-Grades, Efficient Windows, Air Sealing, Efficient HVAC Equipment, and Duct Sealing 	16

Lighting and Appliances	17

Ventilation Equipment	17

ENERGY STAR Products	20

ENERGY STAR Appliances	20

Algorithms	20

ENERGY STAR Refrigerators	20

ENERGY STAR Clothes Washers	20

ENERGY STAR Dishwashers	20

ENERGY STAR Dehumidifiers	20

ENERGY STAR Room Air Conditioners	21

ENERGY STAR Freezer	21

Residential ENERGY STAR Lighting	24

Algorithms	24

ENERGY STAR CFL Bulbs	24

ENERGY STAR Torchieres	24

ENERGY STAR Indoor Fixture	24

ENERGY STAR Outdoor Fixture	25

Ceiling Fan with ENERGY STAR Light Fixture 	25

ENERGY STAR Windows	26

Algorithms	26

ENERGY STAR Audit	29

Algorithms	29

Refrigerator/Freezer Retirement	29

Algorithms	29

Home Performance with ENERGY STAR	31

HomeCheck Software Example	31

Lighting	34

Commercial and Industrial Energy Efficient Construction	35

C&I Electric	35

Baselines and Code Changes	35

Lighting Equipment	35

Prescriptive Lighting	37

Lighting Controls	39

20% Lighting Power Density (LPD) Reduction	41

Fluorescent Lighting Fixture	42

Motors	44

HVAC Systems	45

Electric Chillers	48

Variable Frequency Drives	49

Air Compressors with Variable Frequency Drives	51

Demand Response Programs	53

Commercial and Industrial Applications	53

Residential Applications	54

Algorithms	54

Direct Load Control (Air Conditioning Cycling and Pool Pump Load Control)	54

Appendix A - Measure Lives…………………………………………………... 55

Pennsylvania Technical Reference Manual

# Introduction

The Technical Reference Manual (TRM) was developed to measure the resource savings from standard energy efficiency measures.  The savings’ algorithms use measured and customer data as input values in industry-accepted algorithms.  The data and input values for the algorithms come from AEPS application forms, standard values including Energy Star standards, or data gathered by Electric Distribution Companies (EDCs).  The standard input values are based on the best available measured or industry data.

The standard values for most commercial and industrial (C&I) measures are supported by end- use metering for key parameters for a sample of facilities and circuits, based on the metered data from past applications in other states.  These C&I standard values are based on five years of data for most measures and two years of data for lighting.

Some electric input values were derived from a review of literature from various industry organizations, equipment manufacturers, and suppliers.  These input values are updated to reflect changes in code, federal standards and recent program evaluations.

## Purpose

The TRM was developed for the purpose of estimating annual energy savings for a selection of energy efficient technologies and measures.  The TRM provides guidance to the Administrator responsible for awarding Alternative Energy Credits (AECs). The revised TRM serves a dual purpose of being used to determine compliance with the Alternative Energy Portfolio Standards (AEPS) Act, 73 P.S. §§ 1648.1-1648.8, and the energy efficiency and conservation requirements of Act 129 of 2008, 66 Pa.C.S. § 2806.1.  The TRM will continue to be updated on an annual basis to reflect the addition of technologies and measures as needed to remain relevant and useful.

Resource savings to be measured include electric energy (kWh) and capacity (kW) savings.  The algorithms in this document focus on the determination of the per unit savings for the energy efficiency and demand response measures.

Definitions

The TRM is designed for use with both the AEPS Act and Act 129; however, it contains words and terms that apply only to the AEPS or only to Act 129.  The following definitions are provided to identify words and terms that are specific for implementation of the AEPS:

- Administrator/Program Administrator – The Credit Administrator of the AEPS program that receives and processes, and approves AEPS Credit applications.

- AEPS application forms – application forms submitted to qualify and register alternative energy facilities for alternative energy credits.

- Application worksheets – part of the AEPS application forms.

- Alternative Energy Credits (AECs) – A tradable instrument used to establish, verify, and measure compliance with the AEPS.  One credit is earned for each 1000kWh of electricity generated (or saved from energy efficiency or conservation measures) at a qualified alternative energy facility.

For the Act 129 program, EDCs may, as an alternative to using the energy savings’ values for standard measures contained in the TRM, submit documentation of alternative measurement methods to support different energy savings’ values.  The alternative measurement methods are subject to review and approval by the Commission to ensure their accuracy.

## General Framework

In general, energy and demand savings will be measured using measured and customer data as input values in algorithms in the TRM, and information from the AEPS application forms, worksheets and field tools.

Three systems will work together to ensure accurate data on a given measure:

- The application form that the customer or customer’s agent submits with basic information.

- Application worksheets and field tools with more detailed, site-specific data, input values and calculations.

- Algorithms that rely on standard or site-specific input values based on measured data.  Parts or all of the algorithms may ultimately be implemented within the tracking system, application forms and worksheets and field tools.

## Algorithms

The algorithms that have been developed to calculate the energy and or demand savings are driven by a change in efficiency level for the installed measure compared to a baseline level of efficiency.  This change in efficiency is reflected in both demand and energy savings for electric measures and energy savings for gas.  The following are the basic algorithms.

Electric Demand Savings = (kW = kWbaseline - kWenergy efficient measure

Electric Energy Savings = (kW X EFLH

Electric Peak Coincident Demand Savings = (kW X Coincidence Factor

Where:

EFLH = Equivalent Full Load Hours of operation for the installed measure.

Other resource savings will be calculated as appropriate.

Specific algorithms for each of the measures may incorporate additional factors to reflect specific conditions associated with a measure.  This may include factors to account for coincidence of multiple installations or interaction between different measures.

## Data and Input Values

The input values and algorithms are based on the best available and applicable data.  The input values for the algorithms come from the AEPS application forms, EDC data gathering, or from standard values based on measured or industry data.

Many input values, including site-specific data, come directly from the AEPS application forms, EDC data gathering, worksheets and field tools.  Site-specific data on the AEPS application forms and EDC data gathering are used for measures with important variations in one or more input values (e.g., delta watts, efficiency level, capacity, etc.).

Standard input values are based on the best available measured or industry data, including metered data, measured data from other state evaluations (applied prospectively), field data, and standards from industry associations.  The standard values for most commercial and industrial measures are supported by end-use metering for key parameters for a sample of facilities and circuits.  These standard values are based on five years of metered data for most measures.  Data that were metered over that time period are from measures that were installed over an eight-year period.  Many input values are based on program evaluations of New Jersey’s Clean Energy Programs or similar programs in the northeast region.

For the standard input assumptions for which metered or measured data were not available, the input values (e.g., delta watts, delta efficiency, equipment capacity, operating hours, coincidence factors) were based on the best available industry data or standards.  These input values were based on a review of literature from various industry organizations, equipment manufacturers and suppliers.

## Baseline Estimates

For all new construction and any replacement of non-working equipment appliance, the (kW and (kWh values are based on the vintage efficiency of the items being replaced versus new high-efficiency products.   The approach used for the replacement measures encourages residential and business consumers to replace working inefficient equipment and appliances with new high-efficiency products rather than taking no action to upgrade or only replacing them with new standard-efficiency products.  The baseline estimates used in the TRM are documented in baseline studies or other market information.  Baselines will be updated to reflect changing codes, practices and market transformation effects.

## Resource Savings in Current and Future Program Years

A E Cs and energy efficiency and demand response reduction savings will apply in equal annual amounts corresponding to either PJM planning years or calendar years beginning with the year deemed appropriate by the Administrator, and lasting for the approved life of the measure for AEPS Credits.  Energy efficiency and demand response savings associated with Act 129 can claim savings for up to fifteen years.

## Prospective Application of the TRM

The TRM will be applied prospectively.  The input values are from the AEPS application forms and EDC data gathering and standard input values (based on measured data including metered data and evaluation results).  The TRM will be updated annually based on new information and available data and then applied prospectively for future program years. Updates will not alter the number of AEPS Credits, once awarded, by the Administrator, nor will it alter any energy savings or demand reductions already in service and within measure life..

## Electric Resource Savings

Algorithms have been developed to determine the electric energy and coincident peak demand savings.

Annual electric energy savings are calculated and then allocated separately by season (summer and winter) and time of day (on-peak and off-peak).  Summer coincident peak demand savings are calculated using a demand savings algorithm for each measure that includes a coincidence factor.  Application of this coincidence factor converts the demand savings of the measure, which may not occur at time of system peak, to demand savings that is expected to occur during the Summer On-Peak period.

Table 1: Periods for Energy Savings and Coincident Peak Demand Savings

|  | Energy Savings | Coincident Peak Demand Savings |
| --- | --- | --- |
| Summer | May through September | June through September |
| Winter | October through April | NA |
| On Peak (Monday - Friday) | 8:00 a.m. to 8:00 p.m. | 12:00 p.m. to 8:00 p.m. |
| Off Peak (Weekends and Holidays) | 8:00 p.m. to 8:00 a.m. | NA |

The time periods for energy savings and coincident peak demand savings were chosen to best fit the Act 129 requirement, which reflects the seasonal avoided cost patterns for electric energy and capacity that were used for the energy efficiency program cost effectiveness purposes.  For energy, the summer period May through September was selected based on the pattern of avoided costs for energy at the PJM level.  In order to keep the complexity of the process for calculating energy savings’ benefits to a reasonable level by using two time periods, the knee periods for spring and fall were split approximately evenly between the summer and winter periods.

For capacity, the summer period June through September was selected to match the period of time required to measure the 100 highest hours of demand.  This period also correlates with the highest avoided costs’ time period for capacity.  The experience in PJM has been that nearly all of the 100 highest hours of an EDC’s peak demand occur during these four months.  Coincidence factors are used to determine the impact of energy efficiency measures on peak demand.

## Post-Implementation Review

The Administrator will review AEPS application forms and tracking systems for all measures and conduct field inspections on a sample of installations.  For some programs and jobs (e.g., custom, large process, large and complex comprehensive design), post-installation review and on-site verification of a sample of AEPS application forms and installations will be used to ensure the reliability of site-specific savings’ estimates.

## Adjustments to Energy and Resource Savings

### Coincidence with Electric System Peak

Coincidence factors are used to reflect the portion of the connected load savings or generation that is coincident with the electric system peak.

### Measure Retention and Persistence of Savings

The combined effect of measure retention and persistence is the ability of installed measures to maintain the initial level of energy savings or generation over the measure life.  Measure retention and persistence effects were accounted for in the metered data that were based on C&I installations over an eight-year period.  As a result, some algorithms incorporate retention and persistence effects in the other input values.  For other measures, if the measure is subject to a reduction in savings or generation over time, the reduction in retention or persistence is accounted for using factors in the calculation of resource savings (e.g., in-service rates for residential lighting measures).

### Interaction of Energy Savings

Interaction of energy savings is accounted for as appropriate.  For all other measures, interaction of energy savings is zero.

For Residential New Construction, the interaction of energy savings is accounted for in the home energy rating tool that compares the efficient building to the baseline or reference building and calculates savings.

For Commercial and Industrial Efficient Construction, the energy savings for lighting is increased by an amount specified in the algorithm to account for HVAC interaction.

For commercial and industrial custom measures, interaction where relevant is accounted for in the site-specific analysis.

## Calculation of the Value of Resource Savings

The calculation of the value of the resources saved is not part of the TRM.  The TRM is limited to the determination of the per unit resource savings in physical terms.

In order to calculate the value of the energy savings for reporting and other purposes, the energy savings are determined at the customer level and then increased by the amount of the transmission and distribution losses to reflect the energy savings at the system level.  The energy savings at the system level are then multiplied by the appropriate avoided costs to calculate the value of the benefits.

System Savings = (Savings at Customer) X (T&D Loss Factor)

Value of Resource Savings = (System Savings) X (System Avoided Costs ) + (Value of Other Resource Savings)

The value of the benefits for a particular measure will also include other resource savings where appropriate.  Maintenance savings will be estimated in annual dollars levelized over the life of the measure.

## Transmission and Distribution System Losses

The TRM calculates the energy savings at the customer level.  These savings need to be increased by the amount of transmission and distribution system losses in order to determine the energy savings at the system level.  The electric loss factor multiplied by the savings calculated from the algorithms will result in savings at the supply level.

The electric loss factor applied to savings at the customer meter is 1.11 for both energy and demand.  The electric system loss factor was developed to be applicable to statewide programs.  Therefore, average system losses at the margin based on PJM data were utilized.  This reflects a mix of different losses that occur related to delivery at different voltage levels.  The 1.11 factor used for both energy and capacity is a weighted average loss factor. These electric loss factors reflect losses at the margin.

## Measure Lives

Measure lives are provided in Appendix A for informational purposes and for use in other applications such as reporting lifetime savings or in benefit cost studies that span more than one year.  For the purpose of calculating the total Resources Cost Test for Act 129, measures cannot claim savings for more than 15 years.

## Custom Measures

Custom measures are considered too complex or unique to be included in the list of standard measures provided in the TRM.  Also included are measures that may involve metered data, but require additional assumptions to arrive at a ‘typical’ level of savings as opposed to an exact measurement. The qualification for and availability of AEPS Credits and energy efficiency and demand response savings are determined on a case-by-case basis.

An AEPS application must be submitted, containing adequate documentation fully describing the energy efficiency measures installed or proposed and an explanation of how the installed facilities qualify for A E Cs. The AEPS application must include a proposed evaluation plan by which the Administrator may evaluate the effectiveness of the energy efficiency measures provided by the installed facilities. All assumptions should be identified, explained and supported by documentation, where possible.  The applicant may propose incorporating tracking and evaluation measures using existing data streams currently in use provided that they permit the Administrator to evaluate the program using the reported data.

To the extent possible, the energy efficiency measures identified in the AEPS application should be verified by the meter readings submitted to the Administrator.

Impact of Weather

To account for weather differences within Pennsylvania Equivalent FullLoad Hours (ELFH) were taken from the US Department of Energy’s Energy Star Calculator that provides ELFH values for seven Pennsylvania cities:  Allentown, Erie, Harrisburg, Philadelphia, Pittsburgh, Scranton, and Williamsport.  These cities provide a representative sample of the various climate and utility regions in Pennsylvania.

## Algorithms for Energy Efficient Measures

The following pages present measure-specific algorithms.

# Residential Electric HVAC

## Algorithms

The measurement plan for residential high-efficiency cooling and heating equipment is based on algorithms that determine a central air conditioner’s or heat pump’s cooling/heating energy use and peak demand.  Input data is based both on fixed assumptions and data supplied from the high efficiency equipment AEPS application form or EDC data gathering.  The algorithms also include the calculation of additional energy and demand savings due to the required proper sizing of high-efficiency units.

The savings will be allocated to summer/winter and on-peak/off-peak time periods based on load shapes from measured data and industry sources.  The allocation factors are documented below in the input value table.

The algorithms applicable for this program measure the energy savings directly related to the more efficient hardware installation.  Estimates of energy savings due to the proper sizing of the equipment are also included.

The following is an explanation of the algorithms used and the nature and source of all required input data.

#### Algorithms

### Central Air Conditioner (A/C) and Air Source Heat Pump (ASHP)

Cooling Energy Consumption and Peak Demand Savings – Central A/C and ASHP (High Efficiency Equipment Only)

# Energy Impact (kWh) = CAPY/1000 X (1/SEERb – 1/SEERq ) X EFLH

Peak Demand Impact (kW) = CAPY/1000 X (1/EERb – 1/EERq ) X CF

Heating Energy Savings – ASHP

Energy Impact (kWh) = CAPY/1000 X (1/HSPFb  - 1/HSPFq ) X EFLH

Cooling Energy Consumption and Demand Savings  – Central A/C and ASHP (Proper Sizing)

Energy Impact (kWh) =  (CAPY/(SEERq X 1000)) X EFLH X PSF

Peak Demand Impact (kW) = ((CAPY/(EERq X 1000)) X CF) X PSF

Cooling Energy Consumption and Demand Savings  – Central A/C and ASHP (QIV)

Energy Impact (kWh) = (((CAPY/(1000 X SEERq)) X EFLH) X (1-PSF) X QIF

Peak Demand Impact (kW) = ((CAPY/(1000 X EERq)) X CF) X (1-PSF) X QIF

Cooling Energy Consumption and Demand Savings  – Central A/C and ASHP (Maintenance)

Energy Impact (kWh) =  ((CAPY/(1000 X SEERm)) X EFLH) X MF

Peak Demand Impact (kW) = ((CAPY/(1000 X EERm)) X CF) X MF

Cooling Energy Consumption and Demand Savings– Central A/C and ASHP    (Duct Sealing)

Energy Impact (kWh) = (CAPY/(1000 X SEERq)) X EFLH X DuctSF

Peak Demand Impact (kW) = ((CAPY/(1000 X EERq)) X CF) X DuctSF

### Ground Source Heat Pumps (GSHP)

# Cooling Energy (kWh) Savings = CAPY/1000 X (1/SEERb – (1/(EERg X GSER))) X EFLH

Heating Energy (kWh) Savings = CAPY/1000 X (1/HSPFb – (1/(COPg X GSOP))) X EFLH

Peak Demand Impact (kW) = CAPY/1000 X (1/EERb – (1/(EERg X GSPK))) X CF

### GSHP Desuperheater

Energy (kWh) Savings = EDSH

Peak Demand Impact (kW) = PDSH

### Furnace High Efficiency Fan

Heating Energy (kWh) Savings = ((Capyt X EFLHHT)/100,000 BTU/therm) X HFS

Cooling Energy (kWh) Savings = CFS

#### Definition of Terms

CAPY = The cooling capacity (output in Btuh) of the central air conditioner or heat pump being installed.  This data is obtained from the AEPS Application Form based on the model number or from EDC data gathering.

SEERb = The Seasonal Energy Efficiency Ratio of the Baseline Unit.

SEERq = The Seasonal Energy Efficiency Ratio of the qualifying unit being installed. This data is obtained from the AEPS Application Form or EDC’s data gathering based on the model number.

SEERm = The Seasonal Energy Efficiency Ratio of the Unit receiving maintenance

EERb = The Energy Efficiency Ratio of the Baseline Unit.

EERq = The Energy Efficiency Ratio of the unit being installed. This data is obtained from the AEPS Application Form or EDC data gathering based on the model number.

EERg = The EER of the ground source heat pump being installed.  Note that EERs of GSHPs are measured differently than EERs of air source heat pumps (focusing on entering water temperatures rather than ambient air temperatures).  The equivalent SEER of a GSHP can be estimated by multiplying EERg by 1.02.

GSER = The factor to determine the SEER of a GSHP based on its EERg.

EFLH = The Equivalent Full Load Hours of operation for the average unit.

ESF = The Energy Sizing Factor or the assumed saving due to proper sizing and proper installation.

PSF = The Proper Sizing Factor or the assumed savings due to proper sizing of cooling equipment.

QIF = The Quality Installation factor or assumed savings due to a verified quality installation of cooling equipment.

MF = The Maintenance Factor or assumed savings due to completing recommended maintenance on installed cooling equipment.

DuctSF = The Duct Sealing Factor or the assumed savings due to proper sealing of all cooling ducts.

CF = The coincidence factor which equates the installed unit’s connected load to its demand at time of system peak.

DSF = The Demand Sizing Factor or the assumed peak-demand capacity saved due to proper sizing and proper installation.

HSPFb = The Heating Seasonal Performance Factor of the Baseline Unit.

HSPFq = The Heating Seasonal Performance Factor of the unit being installed. This data is obtained from the AEPS Application Form or EDC’s data gathering.

COPg = Coefficient of Performance.  This is a measure of the efficiency of a heat pump.

GSOP = The factor to determine the HSPF of a GSHP based on its COPg.

GSPK = The factor to convert EERg to the equivalent EER of an air conditioner to enable comparisons to the baseline unit.

EDSH = Assumed savings per desuperheater.

PDSH = Assumed peak-demand savings per desuperheater.

Capyq = Output capacity of the qualifying heating unit in BTUs/hour.

EFLHHT = The Equivalent Full Load Hours of operation for the average heating unit.

HFS = Heating fan savings,

CFS = Cooling fan savings.

The 1000 used in the denominator is used to convert watts to kilowatts.

A summary of the input values and their data sources follows:

Table 2: Residential Electric HVAC

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| CAPY | Variable |  | AEPS Application; EDC Data Gathering |
| SEERb | Fixed | Baseline = 13 | 1 |
| SEERq | Variable |  | AEPS Application; EDC Data Gathering |
| SEERm | Fixed | 10 | 15 |
| EERb | Fixed | Baseline = 11.3 | 2 |
| EERq | Fixed | = (11.3/13) X SEERq | 2 |
| EERg | Variable |  | AEPS Application; EDC’s Data Gathering |
| EERm | Fixed | 8.69 | 19 |
| GSER | Fixed | 1.02 | 3 |
| EFLH | Fixed | Allentown Cooling = 784 Hours Allentown Heating = 2,492 Hours Erie Cooling = 482 Hours Erie Heating = 2,901 Hours Harrisburg Cooling = 929 Hours Harrisburg Heating = 2,371 Hours Philadelphia Cooling = 1,032 Hours Philadelphia Heating = 2,328 Hours Pittsburgh Cooling = 737 Hours Pittsburgh Heating = 2,380 Hours Scranton Cooling = 621 Hours Scranton Heating = 2,532 Hours Williamsport Cooling = 659 Hours Williamsport Heating = 2,502 | 4 |
| ESF | Fixed | 2.9% | 5 |
| PSF | Fixed | 5% | 14 |
| QIF | Fixed | 9.2% | 4 |
| MF | Fixed | 10% | 20 |
| DuctSF | Fixed | 18% | 14 |
| CF | Fixed | 70% | 6 |
| DSF | Fixed | 2.9% | 7 |
| HSPFb | Fixed | Baseline = 7.7 | 8 |
| HSPFq | Variable |  | AEPS Application; EDC’s Data Gathering |
| COPg | Variable |  | AEPS Application; EDC’s Data Gathering |
| GSOP | Fixed | 3.413 | 9 |
| GSPK | Fixed | 0.8416 | 10 |
| EDSH | Fixed | 1842 kWh | 11 |
| PDSH | Fixed | 0.34 kW | 12 |
| Cooling - CAC Time Period Allocation Factors | Fixed | Summer/On-Peak 64.9% Summer/Off-Peak 35.1% Winter/On-Peak 0% Winter/Off-Peak 0% | 13 |
| Cooling – ASHP Time Period Allocation Factors | Fixed | Summer/On-Peak 59.8% Summer/Off-Peak 40.2% Winter/On-Peak 0% Winter/Off-Peak 0% | 13 |
| Cooling – GSHP Time Period Allocation Factors | Fixed | Summer/On-Peak 51.7% Summer/Off-Peak 48.3% Winter/On-Peak 0% Winter/Off-Peak 0% | 13 |
| Heating – ASHP & GSHP Time Period Allocation Factors | Fixed | Summer/On-Peak 0.0% Summer/Off-Peak 0.0% Winter/On-Peak 47.9% Winter/Off-Peak 52.1% | 13 |
| GSHP Desuperheater Time Period Allocation Factors | Fixed | Summer/On-Peak 4.5% Summer/Off-Peak 4.2% Winter/On-Peak 43.7% Winter/Off-Peak 47.6% | 13 |
| Capyq | Variable |  | AEPS Application; EDC’s Data Gathering |
| EFLHHFS | Fixed | Allentown Heating = 2,492 Hours Erie Heating = 2,901 Hours Harrisburg Heating = 2,371 Hours Philadelphia Heating = 2,328 Hours Pittsburgh Heating = 2,380 Hours Scranton Heating = 2,532 Hours Williamsport Heating = 2,502 | 4 |
| HFS | Fixed | 0.5 kWh | 17 |
| CFS | Fixed | 105 kWh | 18 |

Sources:

- Federal Register, Vol. 66, No. 14, Monday, January 22, 2001/Rules and Regulations, p. 7170-7200.

- Average EER for SEER 13 units.

- VEIC estimate.  Extrapolation of manufacturer data.

- US Department of Energy, Energy Star Calculator.  Accessed 3/16/2009.

- Xenergy, “New Jersey Residential HVAC Baseline Study”, (Xenergy, Washington, D.C., November 16, 2001).

- Based on an analysis of six different utilities by Proctor Engineering.

- Xenergy, “New Jersey Residential HVAC Baseline Study”, (Xenergy, Washington, D.C., November 16, 2001).

- Federal Register, Vol. 66, No. 14, Monday, January 22, 2001/Rules and Regulations, p. 7170-7200.

- Engineering calculation, HSPF/COP=3.413.

- VEIC Estimate.  Extrapolation of manufacturer data.

- VEIC estimate, based on PEPCo assumptions.

- VEIC estimate, based on PEPCo assumptions.

- Time period allocation factors used in cost-effectiveness analysis.

- Northeast Energy Efficiency Partnerships, Inc., “Benefits of HVAC Contractor Training”, (February 2006): Appendix C Benefits of HVAC Contractor Training: Field Research Results 03-STAC-01.

- Minimum Federal Standard for new Central Air Conditioners between 1990 and 2006.

- NJ utility analysis of heating customers, annual gas heating usage.

- Scott Pigg (Energy Center of Wisconsin), “Electricity Use by New Furnaces:  A Wisconsin Field Study”, Technical Report 230-1, October 2003.

- Ibid., p. 34.  ARI charts suggest there are about 20% more full load cooling hours in NJ than southern WI.  Thus, average cooling savings in NJ are estimated at 95 to 115.

- The same EER to SEER ratio used for SEER 13 units applied to SEER 10 units.  EERm = (11.3/13) * 10.

- VEIC estimate. Conservatively assumes less savings than for QIV because of the retrofit context.

# Residential New Construction

## Algorithms

### Insulation Up-Grades, Efficient Windows, Air Sealing, Efficient HVAC Equipment and Duct Sealing

Energy savings due to improvements in Residential New Construction will be a direct output of accredited Home Energy Ratings (HERS) software that meets the applicable Mortgage Industry National Home Energy Rating System Standards.  REM/Rate is cited here as an example of an accredited software which has a module that compares the energy characteristics of the energy efficient home to the baseline/reference home and calculates savings.

The system peak electric demand savings will be calculated from the software output with the following savings’ algorithms, which are based on compliance and certification of the energy efficient home to the EPA’s ENERGY STAR for New Homes’ program standard:

Peak demand of the baseline home = (PLb X OFb) / (SEERb X BLEER X 1,000).

Peak demand of the qualifying home = (PLq X OFq) / (EERq X 1,000).

Coincident system peak electric demand savings = (Peak demand of the baseline home – Peak demand of the qualifying home) X CF.

#### Definition of Terms

PLb = Peak load of the baseline home in Btuh.

OFb = The over sizing factor for the HVAC unit in the baseline home.

SEERb = The Seasonal Energy Efficiency Ratio of the baseline unit.

BLEER = Factor to convert baseline SEERb to EERb.

PLq = The actual predicted peak load for the program qualifying home constructed, in Btuh.

OFq = The oversizing factor for the HVAC unit in the program qualifying home.

EERq = The EER associated with the HVAC system in the qualifying home.

CF = The coincidence factor which equates the installed HVAC system’s demand to its demand at time of system peak.

A summary of the input values and their data sources follows:

Table 3: Applicable to Building Completions from April 2003 to Present

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| PLb | Variable |  | 1 |
| OFb | Fixed | 1.6 | 2 |
| SEERb | Fixed | 13 | 3 |
| BLEER | Fixed | 0.92 | 4 |
| PLq | Variable |  | Software Output |
| OFq | Fixed | 1.15 | 5 |
| EERq | Variable |  | AEPS Application; EDC’s Data Gathering |
| CF | Fixed | 0.70 | 6 |

Sources:

- Calculation of peak load of baseline home from the home energy rating tool, based on the reference home energy characteristics.

- PSE&G 1997 Residential New Construction baseline study.

- Federal Register, Vol. 66, No. 14, Monday, January 22, 2001/Rules and Regulations, p. 7170-7200

- Engineering calculation.

- Program guideline for qualifying home.

- Based on an analysis of six different utilities by Proctor Engineering.

### Lighting and Appliances

Quantification of additional saving due to the addition of high-efficiency lighting and clothes washers will be based on the algorithms presented for these appliances in the Energy Star Lighting Algorithms and the Energy Star Appliances Algorithms, respectively.  These algorithms are found in Energy Star Products.

### Ventilation Equipment

Additional energy savings of 175 kWh and peak-demand saving of 60 Watts will be added to the output of the home energy rating software to account for the installation of high-efficiency ventilation equipment.  These values are based on a baseline fan of 80 Watts and an efficient fan of 20 Watts running for eight-hours per day.

The following tables describe the characteristics of the three reference homes.

Table 4: ENERGY STAR Homes

REMRate User Defined Reference Homes -- Applicable to building completions from

pril 2003 to present -- Reflects MEC 95

| Data Point | Single and Multiple Family Except as Noted. |
| --- | --- |
| Active Solar | None |
| Ceiling Insulation | U=0.031 (1) |
| Radiant Barrier | None |
| Rim/Band Joist | U=0.141 Type A-1, U=0.215 Type A-2 (1) |
| Exterior Walls - Wood | U=0.141 Type A-1, U=0.215 Type A-2 (1) |
| Exterior Walls - Steel | U=0.141 Type A-1, U=0.215 Type A-2 (1) |
| Foundation Walls | U=0.99 |
| Doors | U=0.141 Type A-1, U=0.215 Type A-2 (1) |
| Windows | U=0.141 Type A-1, U=0.215 Type A-2 (1), No SHGC req. |
| Glass Doors | U=0.141 Type A-1, U=0.215 Type A-2 (1), No SHGC req. |
| Skylights | U=0.031 (1), No SHGC req. |
| Floor over Garage | U=0.050 (1) |
| Floor over Unheated Basement | U=0.050 (1) |
| Floor over Crawlspace | U=0.050 (1) |
| Floor over Outdoor Air | U=0.031 (1) |
| Unheated Slab on Grade | R-0 edge/R-4.3 under |
| Heated Slab on Grade | R-0 edge/R-6.4 under |
| Air Infiltration Rate | 0.51 ACH winter/0.51 ACH summer |
| Duct Leakage | No Observable Duct Leakage |
| Mechanical Ventilation | None |
| Lights and Appliances | Use Default |
| Setback Thermostat | Yes for heating, no for cooling |
| Heating Efficiency |  |
| Furnace | 80% AFUE (3) |
| Boiler | 80% AFUE |
| Combo Water Heater | 76% AFUE (recovery efficiency) |
| Air Source Heat Pump | 7.7 HSPF |
| Geothermal Heat Pump | Open not modeled, 3.0 COP closed |
| PTAC / PTHP | Not differentiated from air source HP |
| Cooling Efficiency |  |
| Central Air Conditioning | 13.0 SEER |
| Air Source Heat Pump | 13.0 SEER |
| Geothermal Heat Pump | 3.4 COP (11.6 EER) |
| PTAC / PTHP | Not differentiated from central AC |
| Window Air Conditioners | Not differentiated from central AC |
| Domestic WH Efficiency |  |
| Electric | 0.97 EF (4) |
| Natural Gas | 0.67 EF (4) |
| Water Heater Tank Insulation | None |
| Duct Insulation | N/A |
| Notes: |  |

Table 5: ENERGY STAR Homes

REMRate User Defined Reference Homes -- Applicable to building completions from January 2008 to present

| Data Point | Single and Multiple Family Except as Noted. |
| --- | --- |
| Domestic WH Efficiency |  |
| Electric | EF = 0.97 - (0.00132 * gallons) (1) |
| Natural Gas | EF = 0.67 - (0.0019 * gallons) (1) |
| Notes: |  |

ENERGY STAR Products

ENERGY STAR Appliances, ENERGY STAR Lighting, ENERGY STAR Windows, and ENERGY STAR Audit

## ENERGY STAR Appliances

## Algorithms

The general form of the equation for the ENERGY STAR Appliance measure savings’ algorithms is:

Number of Units X Savings per Unit

To determine resource savings, the per unit estimates in the algorithms will be multiplied by the number of appliance units.  The number of units will be determined using market assessments and market tracking.  Some of these market tracking mechanisms are under development.  Per unit savings’ estimates are derived primarily from a 2000 Market Update Report by RLW for National Grid’s appliance program and from previous NEEP screening tool assumptions (clothes washers).

Note that the pre-July 2001 refrigerator measure has been deleted given the timing of program implementation.  As no field results are expected until July 2001, there was no need to quantify savings relative to the pre-July 2001 efficiency standards improvement for refrigerators.

### ENERGY STAR Refrigerators

Electricity Impact (kWh) = ESavREF

Demand Impact (kW) = DSavREF X CFREF

### ENERGY STAR Clothes Washers

Electricity Impact (kWh) = ESavCW

Demand Impact (kW) = DSavCW X CFCW

### ENERGY STAR Dishwashers

Electricity Impact (kWh) = ESavDW

Demand Impact (kW) = DSavREF X CFDW

### ENERGY STAR Dehumidifiers

Electricity Impact (kWh) = ESavDH

Demand Impact (kW) = DSavDH X CFDH

### ENERGY STAR Room Air Conditioners

Electricity Impact (kWh) = ESavRAC

Demand Impact (kW) = DSavRAC X CFRAC

### ENERGY STAR Freezer

Demand Impact (kW) = kWBASE – kWEE

#### Energy Impact (kWh) = (kW X HOURS

#### Definition of Terms

ESavREF = Electricity savings per purchased Energy Star refrigerator.

DSavREF  = Summer demand savings per purchased Energy Star refrigerator.

ESavCW = Electricity savings per purchased Energy Star clothes washer.

DSavCW = Summer demand savings per purchased Energy Star clothes washer.

ESavDW = Electricity savings per purchased Energy Star dishwasher.

DSavDW = Summer demand savings per purchased Energy Star dishwasher.

ESavDH = Electricity savings per purchased ENERGY STAR dehumidifier

DSavDH = Summer demand savings per purchased ENERGY STAR dehumidifier

ESavRAC = Electricity savings per purchased Energy Star room AC.

DSavRAC = Summer demand savings per purchased Energy Star room AC.

CFREF, CFCW, CFDW, CFDH, CFRAC = Summer demand coincidence factor.  The coincidence of average appliance demand to summer system peak equals 1 for demand impacts for all appliances reflecting embedded coincidence in the DSav factor except for room air conditioners where the CF is 58%.

(kW = gross customer connected load kW savings for the measure

kWBASE = Baseline connected kW

kWEE = Energy efficient connected kW

HOURS = average hours of use per year

Table 6: Energy Star Appliances

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| ESavREF | Fixed | see Table _ below | 12 |
| DSavREF | Fixed | 0.0125 kW | 1 |
| REF Time Period Allocation Factors | Fixed | Summer/On-Peak 20.9% Summer/Off-Peak 21.7% Winter/On-Peak 28.0% Winter/Off-Peak 29.4% | 2 |
| ESavCW | Fixed | see Table _ below | 12 |
| DSavCW | Fixed | 0.0147 kW | 3 |
| CW Electricity Time Period Allocation Factors | Fixed | Summer/On-Peak 24.5% Summer/Off-Peak 12.8% Winter/On-Peak 41.7% Winter/Off-Peak 21.0% | 2 |
| ESavDW | Fixed | see Table _ below | 12 |
| DSavDW | Fixed | 0.0225 | 4 |
| DW Electricity Time Period Allocation Factors | Fixed | 19.8%, 21.8%, 27.8%, 30.6% | 2 |
| ESavDH | Fixed | see Table _ below | 12 |
| DSavDH | Fixed | .0098 kW | 10 |
| ESavRAC | Fixed | see Table _ below | 12 |
| DSavRAC | Fixed | 0.1018 kW | 6 |
| CFREF, CFCW, CFDW, CFDH, CFRAC | Fixed | 1.0, 1.0, 1.0, 1.0, 0.58 | 7 |
| RAC Time Period Allocation Factors | Fixed | 65.1%, 34.9%, 0.0%, 0.0% | 2 |
| kWBASE | Fixed | 0.0926 | 11 |
| kWEE | Fixed | 0.0813 | 11 |
| HOURS | Fixed | 5000 | 11 |
| (kW | Fixed | 0.0113 | 11 |

Sources:

- Energy Star Refrigerator Savings Calculator (Calculator updated: 2/15/05; Constants updated 05/07). Demand savings derived using refrigerator load shape.

- Time period allocation factors used in cost-effectiveness analysis.  From residential appliance load shapes.

- Energy and water savings based on Consortium for Energy Efficiency estimates. Assumes 75% of participants have gas water heating and 60% have gas drying (the balance being electric). Demand savings derived using NEEP screening clothes washer load shape.

- Energy and water savings from RLW Market Update.  Assumes 37% electric hot water market share and 63% gas hot water market share.  Demand savings derived using dishwasher load shape.

- Energy and demand savings from engineering estimate based on 600 hours of use.  Based on delta watts for ENERGY STAR and non-ENERGY STAR units in five different size (cooling capacity) categories.  Category weights from LBNL Technical Support Document for ENERGY STAR Conservation Standards for Room Air Conditioners.

- Average demand savings based on engineering estimate.

- Coincidence factors already embedded in summer peak demand reduction estimates with the exception of RAC.  RAC CF is based on data from PEPCO.

- Prorated based on six months in the summer period and six months in the winter period.

- Energy Star Dehumidifier Savings Calculator (Calculator updated: 2/15/05; Constants updated 05/07).   A weighted average based on the distribution of available ENERGY STAR products was used to determine savings.

- Conservatively assumes same kW/kWh ratio as Refrigerators.

- Efficiency Vermont. Technical Reference User Manual: Measure Savings Algorithms and Cost Assumptions (July 2008).

- All values are taken from the Energy Star Savings Calculators at www.energystar.gov.

Table 7: Energy Savings from Energy Star Calculators

| Refrigerator |  |
| --- | --- |
| Manual Defrost | 72 kWh |
| Partial Automatic Defrost | 72 kWh |
| Top mount freezer without door ice | 80 kWh |
| Side mount freezer without door ice | 95 kWh |
| Bottom mount freezer without door ice | 87 kWh |
| Top mount freezer with door ice | 94 kWh |
| Side mount freezer with door ice | 100 kWh |
| Freezers |  |
| Upright with manual defrost | 55 kWh |
| Upright with automatic defrost | 80 kWh |
| Chest Freezer | 52 kWh |
| Compact Upright with manual defrost | 62 kWh |
| Compact Upright with automatic defrost | 83 kWh |
| Compact Chest Freezer | 55 kWh |
| Dehumidifier |  |
| 1-25 pints/day | 54 kWh |
| 25-35 pints/day | 117 kWh |
| 35-45 pints/day | 213 kWh |
| 45-54 pints/day | 297 kWh |
| 54-75 pints/day | 342 kWh |
| 75-185 pints/day | 374 kWh |
| Room Air Conditioner (Load hours in parentheses) |  |
| Allentown | 74 kWh (784 hours) |
| Erie | 46 kWh (482 hours) |
| Harrisburg | 88 kWh (929 hours) |
| Philadelphia | 98 kWh (1032 hours) |
| Pittsburgh | 70 kWh (737 hours) |
| Scranton | 59 kWh (621 hours) |
| Williamsport | 62 kWh (659 hours) |
| Dishwasher |  |
| With Gas Hot Water Heater | 77 kWh |
| With Electric Hot Water Heater | 137 kWh |
| Clothes Washer |  |
| With Gas Hot Water Heater | 26 kWh |
| With Electric Hot Water Heater | 258 kWh |

## Residential ENERGY STAR Lighting

## Algorithms

Savings from installation of screw-in ENERGY STAR CFLs, ENERGY STAR fluorescent torchieres, ENERGY STAR indoor fixtures and ENERGY STAR outdoor fixtures are based on a straightforward algorithm that calculates the difference between existing and new wattage and the average daily hours of usage for the lighting unit being replaced.  An “in-service” rate is used to reflect the fact that not all lighting products purchased are actually installed.

The general form of the equation for the ENERGY STAR or other high-efficiency lighting energy savings algorithm is:

Number of Units X Savings per Unit

Per unit savings estimates are derived primarily from a 2004 Nexus Market Research report evaluating similar retail lighting programs in New England (MA, RI and VT)

### ENERGY STAR CFL Bulbs

Electricity Impact (kWh) = ((CFLwatts X (CFLhours X 365))/1000) X  ISRCFL

Peak Demand Impact (kW) = (CFLwatts) X Light CF

### ENERGY STAR Torchieres

Electricity Impact (kWh) = ((Torchwatts X (Torchhours X 365))/1000) X ISRTorch

Peak Demand Impact (kW) = (Torchwatts) X Light CF

### ENERGY STAR Indoor Fixture

Electricity Impact (kWh) = ((IFwatts X (IFhours X 365))/1000) X ISRIF

Peak Demand Impact (kW) = (IFwatts) X Light CF

### ENERGY STAR Outdoor Fixture

Electricity Impact (kWh) = ((OFwatts X (OFhours X 365))/1000) X ISROF

Peak Demand Impact (kW) = (OFwatts) X Light CF

### Ceiling Fan with ENERGY STAR Light Fixture

Energy Savings (kWh) =180 kWh

Demand Savings (kW) = 0.01968

Definition of Terms

CFLwatts = Average delta watts per purchased Energy Star CFL

CFLhours = Average hours of use per day per CFL

ISRCFL = In-service rate per CFL

Torchwatts = Average delta watts per purchased Energy Star torchiere

Torchhours = Average hours of use per day per torchiere

ISRTorch = In-service rate per Torchier

IFwatts = Average delta watts per purchased Energy Star Indoor Fixture

IFhours = Average hours of use per day per Indoor Fixture

ISRIF = In-service rate per Indoor Fixture

OFwatts = Average delta watts per purchased Energy Star Outdoor Fixture

OFhours = Average hours of use per day per Outdoor Fixture

ISROF = In-service rate per Outdoor Fixture

Light CF = Summer demand coincidence factor.

(kWh	= Gross customer annual kWh savings for the measure

(kW = Gross customer connected load kW savings for the measure

Table 8: ENERGY STAR Lighting

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| CFLwatts | Fixed | Variable | Data Gathering |
| CFLhours | Fixed | 3.0 | 6 |
| ISRCFL | Fixed | 84% | 3 |
| Torchwatts | Fixed | 115.8 | 1 |
| Torchhours | Fixed | 3.0 | 2 |
| ISRTorch | Fixed | 83% | 3 |
| IFwatts | Fixed | 48.7 | 1 |
| IFhours | Fixed | 2.6 | 2 |
| ISRIF | Fixed | 95% | 3 |
| OFwatts | Fixed | 94.7 | 1 |
| OFhours | Fixed | 4.5 | 2 |
| ISROF | Fixed | 87% | 3 |
| Light CF | Fixed | 5% | 4 |
| (kWh | Fixed | 180 kWh | 5 |
| (kW | Fixed | 0.01968 | 5 |

Sources:

- Nexus Market Research, “Impact Evaluation of the Massachusetts, Rhode Island and Vermont 2003 Residential Lighting Programs”, Final Report, October 1, 2004, p. 43 (Table 4-9)

- Ibid., p. 104 (Table 9-7).  This table adjusts for differences between logged sample and the much larger telephone survey sample and should, therefore, have less bias.

- Ibid., p. 42 (Table 4-7).  These values reflect both actual installations and the % of units planned to be installed within a year from the logged sample.   The logged % is used because the adjusted values (i.e to account for differences between logging and telephone survey samples) were not available for both installs and planned installs.  However, this seems appropriate because the  % actual installed in the logged sample from this table is essentially identical to the % after adjusting for differences between the logged group and the telephone sample (p. 100, Table 9-3).

- RLW Analytics, “Development of Common Demand Impacts for Energy Efficiency Measures/Programs for the ISO Forward Capacity Market (FCM)”, prepared for the New England State Program Working Group (SPWG), March 25, 2007, p. IV.

- Efficiency Vermont. Technical Reference User Manual: Measure Savings Algorithms and Cost Assumptions (July 2008).

- US Department of Energy, Energy Star Calculator.  Accessed 3-16-2009.

## ENERGY STAR Windows

## Algorithms

The general form of the equation for the ENERGY STAR or other high-efficiency windows energy savings’ algorithms is:

Square Feet of Window Area X Savings per Square Foot

To determine resource savings, the per square foot estimates in the algorithms will be multiplied by the number of square feet of window area.  The number of square feet of window area will be determined using market assessments and market tracking.  Some of these market tracking mechanisms are under development.  The per unit energy and demand savings estimates are based on prior building simulations of windows.

ENERGY STAR Windows

Savings’ estimates for Energy Star Windows are based on modeling a typical 2,500 square foot home using REM Rate, the home energy rating tool.  Savings are per square foot of qualifying window area.  Savings will vary based on heating and cooling system type and fuel.  These fuel and HVAC system market shares will need to be estimated from prior market research efforts or from future program evaluation results.

#### Heat Pump

Electricity Impact (kWh) = ESavHP

Demand Impact (kW) = DSavHP X CF

#### Electric Heat/CAC

Electricity Impact (kWh) = ESavRES/CAC

Demand Impact (kW)  = DSavCAC X CF

#### Electric Heat/No CAC

Electricity Impact (kWh) = ESavRES/NOCAC

Demand Impact (kW) = DSavNOCAC X CF

#### Definition of Terms

ESavHP = Electricity savings (heating and cooling) with heat pump installed.

ESavRES/CAC = Electricity savings with electric resistance heating and central AC installed.

ESavRES/NOCAC = Electricity savings with electric resistance heating and no central AC installed.

DSavHP = Summer demand savings with heat pump installed.

DSavCAC = Summer demand savings with central AC installed.

DSavNOCAC = Summer demand savings with no central AC installed.

CF = System peak demand coincidence factor.  Coincidence of building cooling demand to summer system peak.

Table 9: Energy Star Windows

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| ESavHP | Fixed | 2.2395 kWh | 1 |
| HP Time Period Allocation Factors | Fixed | Summer/On-Peak 10% Summer/Off-Peak 7% Winter/On-Peak 40% Winter/Off-Peak 44% | 2 |
| ESavRES/CAC | Fixed | 4.0 kWh | 1 |
| Res/CAC Time Period Allocation Factors | Fixed | Summer/On-Peak 10% Summer/Off-Peak 7% Winter/On-Peak 40% Winter/Off-Peak 44% | 2 |
| ESavRES/NOCAC | Fixed | 3.97 kWh | 1 |
| Res/No CAC Time Period Allocation Factors | Fixed | Summer/On-Peak 3% Summer/Off-Peak 3% Winter/On-Peak 45% Winter/Off-Peak 49% | 2 |
| DSavHP | Fixed | 0.000602 kW | 1 |
| DSavCAC | Fixed | 0.000602 kW | 1 |
| DSavNOCAC | Fixed | 0.00 kW | 1 |
| CF | Fixed | 0.75 | 3 |

Sources:

- From REMRATE Modeling of a typical 2,500 sq. ft. NJ home.  Savings expressed on a per square foot of window area basis.  New Brunswick climate data.

- Time period allocation factors used in cost-effectiveness analysis.

- Based on reduction in peak cooling load.

- Prorated based on 12% of the annual degree days falling in the summer period and 88% of the annual degree days falling in the winter period.

## ENERGY STAR Audit

## Algorithms

No algorithm was developed to measure energy savings for this program.  The purpose of the program is to provide information and tools that residential customers can use to make decisions about what actions to take to improve energy efficiency in their homes.  Many measure installations that are likely to produce significant energy savings are covered in other programs.  These savings are captured in the measured savings for those programs.  The savings produced by this program that are not captured in other programs would be difficult to isolate and relatively expensive to measure.

## Refrigerator/Freezer Retirement

## Algorithms

The general form of the equation for the Refrigerator/Freezer Retirement savings algorithm is:

Number of Units X Savings per Unit

To determine resource savings, the per unit estimates in the algorithms will be multiplied by the number of appliance units.

Unit savings are the product of average fridge/freezer consumption (gross annual savings).

Algorithm

Electricity Impact (kWh) = ESavRetFridge

Demand Impact (kW) = DSavRetFridge X CFRetFridge

### Definition of Terms

ESavRetFridge = Gross annual energy savings per unit retired appliance

DSavRetFridge = Summer demand savings per retired refrigerator/freezer

CFRetFridge = Summer demand coincidence factor.

Table 10: Refrigerator/Freezer Recycling

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| ESavRetFridge | Fixed | 1,728 kWh | 1 |
| DSavRetFridge | Fixed | .2376 kW | 2 |
| CFRetFridge | Fixed | 1 | 3 |

Sources:

- The average power consumption of units retired under similar recent programs:

a.	Fort Collins Utilities, February 2005. Refrigerator and Freezer Recycling Program 2004 Evaluation Report.

b.	Midwest Energy Efficiency Alliance, 2005. 2005 Missouri Energy Star Refrigerator Rebate and Recycling Program Final Report

c.	Pacific Gas and Electric, 2007.  PGE ARP 2006-2008 Climate Change Impacts Model (spreadsheet)

d.	Quantec, Aug 2005. Evaluation of the Utah Refrigerator and Freezer Recycling Program (Draft Final Report).

e.	CPUC DEER website, http://eega.cpuc.ca.gov/deer/measure.asp?s=1&c=2&sc=7&m=389059

f.	Snohomish PUD, February 2007. 2006 Refrigerator/Freezer Recycling Program Evaluation.

g.	Ontario Energy Board, 2006.  Total Resource Cost Guide.

- Applied the kW to kWh ratio derived from Refrigerator savings in the ENERGY STAR Appliances Program.

- Coincidence factor already embedded in summer peak demand reduction estimates

# Home Performance with ENERGY STAR

In order to implement Home Performance with Energy Star, there are various standards a program implementer must adhere to in order to deliver the program.  The program implementer must use software that meets a national standard for savings calculations from whole-house approaches such as home performance.  The software  program implementer  must adhere to at least one of the following standards:

- A software tool whose performance has passed testing according to the National Renewable Energy Laboratory’s HERS BESTEST software energy simulation testing protocol.

- Software approved by the US Department of Energy’s Weatherization Assistance Program.

- RESNET approved rating software.

There are numerous software packages that comply with these standards.  Some examples of the software packages are REM/Rate, EnergyGauge, TREAT, and HomeCheck.  The HomeCheck software is described below as an example of a software that can be used to determine if a home qualifies for Home Performance with Energy Star.

## HomeCheck Software Example

Conservation Services Group (CSG) implements Home Performance with Energy Star in several states. CSG has developed proprietary software known as HomeCheck which is designed to enable an energy auditor to collect information about a customer’s site and based on what is found through the energy audit, recommend energy savings measures and demonstrate the costs and savings associated with those recommendations.  The HomeCheck software is also used to estimate the energy savings that are reported for this program.

CSG has provided a description of the methods and inputs utilized in the HomeCheck software to estimate energy savings.  CSG has also provided a copy of an evaluation report prepared by Nexant which assessed the energy savings from participants in the Home Performance with Energy Star Program managed by the New York State Energy Research and Development Authority (NYSERDA).  The report concluded that the savings estimated by HomeCheck and reported to NYSERDA were in general agreement with the savings estimates that resulted from the evaluation.

These algorithms incorporate the HomeCheck software by reference which will be utilized for estimating energy savings for Home Performance with Energy Star.  The following is a summary of the HomeCheck software which was provided by CSG:  CSG’s HomeCheck software was designed to streamline the delivery of energy efficiency programs. The software provides the energy efficiency specialist with an easy-to-use guide for data collection, site and HVAC testing algorithms, eligible efficiency measures, and estimated energy savings. The software is designed to enable an auditor to collect information about customers’ sites and then, based on what he/she finds through the audit, recommend energy-saving measures, demonstrate the costs and savings associated with those recommendations. It also enables an auditor/technician to track the delivery of services and installation of measures at a site.

This software is a part of an end-to-end solution for delivering high-volume retrofit programs, covering administrative functions such as customer relationship management, inspection scheduling, sub-contractor arranging, invoicing and reporting. The range of existing components of the site that can be assessed for potential upgrades is extensive and incorporates potential modifications to almost all energy using aspects of the home. The incorporation of building shell, equipment, distribution systems, lighting, appliances, diagnostic testing and indoor air quality represents a very broad and comprehensive ability to view the needs of a home.

The software is designed to combine two approaches to assessing energy savings opportunities at the site. One is a measure specific energy loss calculation, identifying the change in use of BTU’s achieved by modifying a component of the site. Second, is the correlation between energy savings from various building improvements, and existing energy use patterns at a site. The use of both calculated savings and the analysis of existing energy use patterns, when possible, provides the most accurate prescription of the impact of changes at the site for an existing customer considering improvements on a retrofit basis.

This software is not designed to provide a load calculation for new equipment or a HERS rating to compare a site to a standard reference site. It is designed to guide facilities in planning improvements at the site with the goal of improved economics, comfort and safety. The software calculates various economic evaluations such as first year savings, simple payback, measure life cost-effectiveness, and Savings-to-Investment ratio (SIR).

Site-Level Parameters and Calculations

There are a number of calculations and methodologies that apply across measures and form the basis for calculating savings potentials at a site.

Heating Degree Days and Cooling Degree Hours

Heat transfer calculations depend fundamentally on the temperature difference between inside and outside temperature. This temperature difference is often summarized on a seasonal basis using fixed heating degree-days (HDD) and cooling degree-hours CDH). The standard reference temperature for calculating HDD (the outside temperature at which the heating system is required), for example, has historically been 65°F. Modern houses have larger internal gains and more efficient thermal building envelopes than houses did when the 65°F standard was developed, leading to lower effective reference temperatures. This fact has been recognized in ASHRAE Fundamentals, which provides a variable-based degree-day method for calculating energy usage. CSG’s Building Model calculates both HDD and CDH based on the specific characteristics and location of the site being treated.

Building Loads, Other Parameters, and the Building Model

CSG is of the opinion that, in practice, detailed building load simulation tools are quite limited in their potential to improve upon simpler approaches due to their reliance on many factors that are not measurable or known, as well as limitations to the actual models themselves. Key to these limitations is the Human Factor (e.g., sleeping with the windows open; extensive use of high-volume extractor fans, etc.) that is virtually impossible to model. As such, the basic concept behind the model was to develop a series of location specific lookup tables that would take the place of performing hourly calculations while allowing the model to perform for any location. The data in these tables would then be used along with a minimum set of technical data to calculate heating and cooling building loads.

In summary, the model uses:

- Lookup tables for various parameters that contain the following values for each of the 239 TMY2 weather stations:

  - Various heating and cooling infiltration factors.

  - Heating degree days and heating hours for a temperature range of 40 to 72°F.

  - Cooling degree hours and cooling hours for a temperature range of 68 to 84°F.

  - Heating and cooling season solar gain factors.

- Simple engineering algorithms based on accepted thermodynamic principles, adjusted to reflect known errors, the latest research and measured results

- Heating season iterative calculations to account for the feedback loop between conditioned hours, degree days, average “system on” indoor and outdoor temperatures and the building

- The thermal behavior of homes is complex and commonly accepted algorithms will on occasion predict unreasonably high savings, HomeCheck uses a proprietary methodology to identify and adjust these cases.  This methodology imposes limits on savings projected by industry standard calculations, to account for interactivities and other factors that are difficult to model.  These limits are based on CSG’s measured experience in a wide variety of actual installations.

Usage Analysis

The estimation of robust building loads through the modeling of a building is not always reliable. Thus, in addition to modeling the building, HomeCheck calculates a normalized annual consumption for heating and cooling, calculated from actual fuel consumption and weather data using a Seasonal Swing methodology. This methodology uses historic local weather data and site-specific usage to calculate heating and cooling loads. The methodology uses 30-year weather data to determine spring and fall shoulder periods when no heating or cooling is likely to be in use. The entered billing history is broken out into daily fuel consumption, and these daily consumption data along with the shoulder periods is used to calculate base load usage and summer and winter seasonal swing fuel consumption.

Multiple HVAC Systems

HVAC system and distribution seasonal efficiencies are used in all thermal-shell measure algorithms. HVAC system and distribution seasonal efficiencies and thermostat load reduction adjustments are used when calculating the effect of interactivity between mechanical and architectural measures. If a site has multiple HVAC systems, weighted average seasonal efficiencies and thermostat load reduction adjustments are calculated based on the relative contributions (in terms of percent of total load) of each system.

Multiple Heating Fuels

It is not unusual to find homes with multiple HVAC systems using different fuel types. In these cases, it is necessary to aggregate the NACs for all fuel sources for use in shell savings algorithms. This is achieved by assigning a percentage contribution to total NAC for each system, converting this into BTU’s, and aggregating the result. Estimated first year savings for thermal shell measures are then disaggregated into the component fuel types based on the pre-retrofit relative contributions of fuel types.

Interactivity

To account for interactivity between architectural and mechanical measures, CSG’s HomeCheck employs the following methodology, in order:

- Noninteracted first year savings are calculated for each individual measure.

- Non-interacted SIR (RawSIR) is calculated for each measure.

- Measures are ranked in descending order of RawSIR,

- Starting with the most cost-effective measure (as defined by RawSIR), first year savings are adjusted for each measure as follows:

  - Mechanical measures (such as thermostats, HVAC system upgrades or distribution system upgrades) are adjusted to account for the load reduction from measures with a higher RawSIR.

  - Architectural measures are adjusted to account for overall HVAC system efficiency changes and thermostat load reduction changes. Architectural measures with a higher RawSIR than that of HVAC system measures are calculated using the existing efficiencies. Those with RawSIR’s lower than that of heating equipment use the new heating efficiencies.

- Interacted SIR is then calculated for each measure, along with cumulative SIR for the entire job.

- All measures are then re-ranked in descending order of SIR.

- The process is repeated, replacing RawSIR with SIR until the order of measures does not change.

### Lighting

Quantification of additional saving due to the addition of high efficiency lighting will be based on the algorithms presented for these appliances in the Energy Star Lighting Algorithms found in Energy Star Products.

# Commercial and Industrial Energy Efficient Construction

## C&I Electric

### Baselines and Code Changes

All baselines are designed to reflect current market practices which are generally the higher of code or available equipment, that are updated periodically to reflect upgrades in code or information from evaluation results.

### Lighting Equipment

For new construction and entire facility rehabilitation projects, savings are calculated using market-driven assumptions that presume a decision to upgrade the lighting system from an industry standard system.  For existing commercial lighting, the most efficient T-12 lamp and magnetic ballast fixture serves as the baseline.  For T-5 and T-8 fixtures replacing HID, 250 watt or greater T-12 fluorescentor 250 watt or greater incandescent fixtures savings are calculated referencing pre-existing connected lighting load.

Lighting equipment includes fluorescent fixtures, ballasts, compact fluorescent fixtures, exit signs, LED fixtures and metal halide lamps.  The measurement of energy savings is based on algorithms with measurement of key variables (i.e., Coincidence Factor and Operating Hours) through end-use metering data accumulated from a large sample of participating facilities from 1995 through 1999.

#### Algorithms

Energy Savings (kWh) = (kW X EFLH X (1+IF)

Demand Savings (kW) = (kW X CF X (1+IF)

#### Definition of Variables

(kW = Change in connected load from baseline to efficient lighting level.  The baseline value is expressed in watts/square foot calculated as:  (Watts/Sq.Ft. - Watts/Sq.Ft. (qualified equipment by same area))*Area Sq.Ft./1000 (see table above).

CF = Coincidence Factor – the value represents the percentage of the total lighting connected load which is on during electric system’s Peak Window.  The Peak Window covers the time period from 12 noon to 8 p.m.  These values are based on measured usage in the JCP&L service territory.

IF = Interactive Factor – applies to C&I interior lighting only.  This represents the secondary demand and energy savings in reduced HVAC consumption resulting from decreased indoor lighting wattage.

EFLH = Equivalent Full Load Hours – represents the annual operating hours.

Table 11: Traffic Signals

|  | Wattage | % Burn | Burn Hours | kWhs | Demand Savings | Energy Savings |
| --- | --- | --- | --- | --- | --- | --- |
| Round Traffic Signals |
| Red 8" | 69 | 55% | 4,818 | 332 | - | - |
| Red 8" LED | 7 | 55% | 4,818 | 34 | 0.062 | 299 |
| Yellow 8" | 69 | 2% | 175 | 12 | - | - |
| Yellow 8" LED | 10 | 2% | 175 | 2 | 0.059 | 10 |
| Green 8" | 69 | 43% | 3,767 | 260 | - | - |
| Green 8" LED | 9 | 43% | 3,767 | 34 | 0.060 | 226 |
| Red 12" | 150 | 55% | 4,818 | 723 | - | - |
| Red 12" LED | 6 | 55% | 4,818 | 29 | 0.144 | 694 |
| Yellow 12" | 150 | 2% | 175 | 26 | - | - |
| Yellow 12" LED | 13 | 2% | 175 | 2 | 70.137 | 24 |
| Green 12" | 150 | 43% | 3,767 | 565 | - | - |
| Green 12" LED | 12 | 43% | 3,767 | 45 | 0.138 | 520 |
| Turn Arrows |
| Yellow 8" | 116 | 8% | 701 | 81 | - | - |
| Yellow 8" LED | 7 | 8% | 701 | 5 | 0.109 | 76 |
| Yellow 12" | 116 | 8% | 701 | 81 | - | - |
| Yellow 12" LED | 9 | 8% | 701 | 6 | 0.107 | 75 |
| Green 8" | 116 | 8% | 701 | 81 | - | - |
| Green 8" LED | 7 | 8% | 701 | 5 | 0.109 | 76 |
| Green 12" | 116 | 8% | 701 | 81 | - | - |
| Green 12" LED | 7 | 8% | 3767 | 5 | 0.109 | 76 |
| Pedestrian Signs |
| Hand/Man 12" | 116 | 100% | 8,760 | 1,016 | - | - |
| Hand/Man LED | 8 | 100% | 8,760 | 70 | 0.108 | 946 |
| Note: kWh and Energy Savings are Annual; Demand Savings listed are per lamp. |

Reference specifications for above traffic signal wattages are from the following manufacturers:

8” Incandescent traffic signal bulb:  General Electric Traffic Signal Model 17325-69A21/TS

12” Incandescent traffic signal bulb:  General Electric Signal Model 35327-150PAR46/TS

Incandescent Arrows & Hand/Man Pedestrian Signs:  General Electric Traffic Signal Model 19010-116A21/TS

8” and 12” LED traffic signals:  Leotek Models TSL-ES08 and TSL-ES12

8” LED Yellow Arrow:  General Electric Model DR4-YTA2-01A

8” LED Green Arrow:  General Electric Model DR4-GCA2-01A

12” LED Yellow Arrow:  Dialight Model 431-3334-001X

12: LED Green Arrow:  Dialight Model 432-2324-001X

LED Hand/Man Pedestrian Sign:  dialight 430-6450-001X

Coincidence factor for demand savings = 55% for red, 43% for green and 2% for yellow.

### Prescriptive Lighting

Prescriptive Lighting is a fixture replacement program for existing commercial customers that are targeted at facilities performing efficiency upgrades to their lighting systems.

The baseline is existing T-12 fixtures with energy efficient lamps and magnetic ballast.

The baseline for compact fluorescent is that the fixture replaced was four times the wattage of the replacement compact fluorescent.

#### Algorithms

Energy Savings (kWh) = (kW X EFLH

Demand Savings (kW) = (kW X CF

(kW=Number of fixtures installed X (baseline wattage for fixture type(from above baseline))-number of replaced fixtures X (wattage from table)

Table 12: Prescriptive Lighting Savings Table

The table will be updated periodically to include new fixtures and technologies available after table publication. Baselines will be established based on the guidelines noted above.

| Fixture Type | Type | New Watts (w/fixture) | Baseline (w/fixture) | Savings (w/fixture) |
| --- | --- | --- | --- | --- |
| COMPACT FLUORESCENT (2) 11W CF/HW | CFL2 | 26 | 104 | 78 |
| COMPACT FLUORESCENT (2) 13W CF/HW | CFL2 | 30 | 120 | 90 |
| COMPACT FLUORESCENT (2) 18W CF/HW | CFL2 | 36 | 144 | 108 |
| COMPACT FLUORESCENT (2) 18W QD/ELEC | CFL2 | 38 | 152 | 114 |
| COMPACT FLUORESCENT (3) 18W | CFL2 | 54 | 225 | 171 |
| COMPACT FLUORESCENT (2) 26W CF/HW | CFL2 | 53 | 212 | 159 |
| COMPACT FLUORESCENT (2) 26W QD/ELEC | CFL2 | 54 | 216 | 162 |
| COMPACT FLUORESCENT (2) 5W CF/HW | CFL2 | 14 | 56 | 42 |
| COMPACT FLUORESCENT (2) 7W CF/HW | CFL2 | 18 | 72 | 54 |
| COMPACT FLUORESCENT (2) 9W CF/HW | CFL2 | 22 | 88 | 66 |
| COMPACT FLUORESCENT 11W CF/HW | CFL1 | 13 | 52 | 39 |
| COMPACT FLUORESCENT 13W CF/HW | CFL1 | 15 | 60 | 45 |
| COMPACT FLUORESCENT 18W CF/HW | CFL1 | 19 | 76 | 57 |
| COMPACT FLUORESCENT 18W QD/ELEC | CFL1 | 22 | 88 | 66 |
| COMPACT FLUORESCENT 20W CF/HW | CFL1 | 22 | 88 | 66 |
| COMPACT FLUORESCENT 22W QD/ELEC | CFL1 | 26 | 104 | 78 |
| COMPACT FLUORESCENT 26W CF/HW | CFL1 | 28 | 112 | 84 |
| COMPACT FLUORESCENT 26W QD/ELEC | CFL1 | 27 | 108 | 81 |
| COMPACT FLUORESCENT 28W CF/HW | CFL1 | 30 | 120 | 90 |
| COMPACT FLUORESCENT 32W CF/HW | CFL1 | 34 | 136 | 102 |
| COMPACT FLUORESCENT 36W CF/HW | CFL1 | 41 | 164 | 123 |
| COMPACT FLUORESCENT 40W CF/HW | CFL1 | 45 | 180 | 135 |
| COMPACT FLUORESCENT (2) 40W CF/HW | CFL2 | 71 | 180 | 109 |
| COMPACT FLUORESCENT 5W CF/HW | CFL1 | 7 | 28 | 21 |
| COMPACT FLUORESCENT 7W CF/HW | CFL1 | 10 | 40 | 30 |
| COMPACT FLUORESCENT 9W CF/HW | CFL1 | 11 | 44 | 33 |
| Low Bay T-5 2L FP54/T5/Elec/Ho | LOBA | 117 | 250 | 133 |
| Low Bay T-5 3L FP54/T5/Elec/Ho | LOBA | 179 | 290 | 111 |
| Low Bay T-5 4L FP54/T5/Elec/Ho | LOBA | 234 | 409 | 175 |
| Low Bay T-5 6L FP54/T5/Elec/Ho | LOBA | 351 | 992 | 641 |
| Low Bay T-8 2L4 | LOBA | 55 | 73 | 18 |
| Low Bay T-8 2L8 | LOBA | 118 | 158 | 40 |
| Low Bay T-8 3L4 | LOBA | 79 | 105 | 26 |
| Low Bay T-8 4L4 | LOBA | 110 | 146 | 36 |
| Low Bay T-8 4L8 | LOBA | 233 | 316 | 83 |
| Low Bay T-8 6L4 | LOBA | 224 | 454 | 230 |
| High Bay T-5 3L FP54/T5/Elec/Ho | HIBA | 179 | 290 | 111 |
| High Bay T-5 4L FP54/T5/Elec/Ho | HIBA | 234 | 409 | 175 |
| High Bay T-5 6L FP54/T5/Elec/Ho | HIBA | 351 | 992 | 641 |
| High Bay T-8 8L4 FP54/T5/Elec/Ho | HIBA | 468 | 1080 | 612 |
| High Bay T-8 3L4 | HIBA | 79 | 105 | 26 |
| High Bay T-8 4L4 | HIBA | 110 | 146 | 36 |
| High Bay T-8 4L8 | HIBA | 233 | 316 | 83 |
| High Bay T-8 6L4 | HIBA | 224 | 454 | 230 |
| High Efficiency Fluorescent 1L2 (1) FO17T8/Elec | HEF | 18 | 32 | 14 |
| High Efficiency Fluorescent 1L2 (2) FO17T8/Elec | HEF | 34 | 56 | 22 |
| High Efficiency Fluorescent 1L2 (3) FO17T8/Elec | HEF | 50 | 78 | 28 |
| High Efficiency Fluorescent 1L2 (4) FO17T8/Elec | HEF | 62 | 112 | 50 |
| High Efficiency Fluorescent 1L3 (1) FO25T8/Elec | HEF | 30 | 46 | 16 |
| High Efficiency Fluorescent 1L3 (2) FO25T8/Elec | HEF | 48 | 80 | 32 |
| High Efficiency Fluorescent 1L3 (3) FO25T8/Elec | HEF | 68 | 126 | 58 |
| High Efficiency Fluorescent 1L3 (4) FO25T8/Elec | HEF | 90 | 160 | 70 |
| High Efficiency Fluorescent T-5 3L FP54/T5/Elec/Ho | HEF | 179 | 290 | 111 |
| High Efficiency Fluorescent T-5 4L FP54/T5/Elec/Ho | HEF | 234 | 409 | 175 |
| High Efficiency Fluorescent T-5 6L FP54/T5/Elec/Ho | HEF | 351 | 992 | 641 |
| High Efficiency Fluorescent T-8 1L4 | HEF | 28 | 42 | 14 |
| High Efficiency Fluorescent T-8 1L8 | HEF | 67 | 78 | 11 |
| High Efficiency Fluorescent T-8 2L2 | HEF | 62 | 94 | 32 |
| High Efficiency Fluorescent T-8 2L4 | HEF | 55 | 73 | 18 |
| High Efficiency Fluorescent T-8 2L8 | HEF | 118 | 158 | 40 |
| High Efficiency Fluorescent T-8 3L4 | HEF | 79 | 105 | 26 |
| High Efficiency Fluorescent T-8 4L4 | HEF | 110 | 146 | 36 |
| High Efficiency Fluorescent T-8 4L8 | HEF | 233 | 316 | 83 |
| LED Exit Sign | EXIT | 20 | 18 | 2 |
| PULSE START METAL HALIDE 1000 W | PSMH | 1075 | 1080 | 5 |
| PULSE START METAL HALIDE 150 W | PSMH | 185 | 200 | 15 |
| PULSE START METAL HALIDE 175 W | PSMH | 208 | 285 | 77 |
| PULSE START METAL HALIDE 200 W | PSMH | 235 | 285 | 50 |
| PULSE START METAL HALIDE 250 W | PSMH | 288 | 454 | 166 |
| PULSE START METAL HALIDE 300 W | PSMH | 342 | 454 | 112 |
| PULSE START METAL HALIDE 320 W | PSMH | 368 | 454 | 86 |
| PULSE START METAL HALIDE 350 W | PSMH | 400 | 454 | 54 |
| PULSE START METAL HALIDE 400 W | PSMH | 450 | 454 | 4 |
| PULSE START METAL HALIDE 750 W | PSMH | 815 | 1075 | 260 |
| Low Bay LED 85 W for 250 Metal Halide | LBLD | 85 | 248 | 163 |
| Low Bay LED 85 W for 2LHO T-8 | LBLF | 85 | 118 | 33 |

### Lighting Controls

Lighting controls include occupancy sensors, daylight dimmer systems, occupancy controlled hi-low controls for fluorescent and HID controls.  The measurement of energy savings is based on algorithms with key variables (i.e., coincidence factor, equivalent full load hours) provided through existing end-use metering of a sample of facilities or from other utility programs with experience with these measures (i.e., % of annual lighting energy saved by lighting control).  For lighting controls, the baseline is a manual switch.

#### Algorithms

Energy Savings (kWh) =   kWc X SVG X EFLH X (1+IF)

Demand Savings (kW) = kWc  X  SVG X CF

#### Definition of Variables

SVG	 = % of annual lighting energy saved by lighting control; refer to table by control type.

kWc = kW lighting load connected to control.

IF = Interactive Factor – This applies to C&I interior lighting only.  This represents the secondary demand and energy savings in reduced HVAC consumption resulting from decreased indoor lighting wattage.

CF = Coincidence Factor – the percentage of the total load which is on during electric system’s peak window.

EFLH = Equivalent full load hours.

Table 13: Lighting Controls

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| kWc | Variable | Load connected to control | AEPS Application; EDC Data Gathering |
| SVG | Fixed | Occupancy Sensor, Controlled Hi-Low Fluorescent Control and controlled HID = 30% Daylight Dimmer System=50% | , 2, and 3 |
| CF | Fixed | By building type and size see lighting verification summary table | Assumes same as JCP&L metered data |
| EFLH | Variable | Based on Building Type and Location | AEPS Application; EDC Data Gathering |
| IF | Variable |  | AEPS Application; EDC Data Gathering |
| Time Period Allocation Factors | Fixed | Summer/On-Peak 26% Summer/Off-Peak 16% Winter/On-Peak 36% Winter/Off-Peak 22% |  |

Sources:

- Northeast Utilities, Determination of Energy Savings Document, 1992

- Levine, M., Geller, H., Koomey, J., Nadel S., Price, L., "Electricity Energy Use Efficiency: Experience with Technologies, Markets and Policies”  ACEEE, 1992

- Lighting control savings fractions consistent with current programs offered by National Grid, Northeast Utilities, Long Island Power Authority, NYSERDA, and Energy Efficient Vermont.

### 20% Lighting Power Density (LPD) Reduction

Lighting power density reduction is new construction efficient lighting with a reduced wattage.

Algorithms

Energy Savings (kWh) = kWsave X HOURS X WHFe

Demand Savings (kW) = kWsave X WHFd

kWsave 	= (WSFbase – WSFeffic)/1000

Definition of Variables

kWsave	= lighting connected load kW saved

HOURS = annual lighting hours of use per year

WHFe	= Waste heat factor for energy to account for cooling savings from efficient lighting.

WHFd 	= Waste heat factor for demand to account for cooling savings from efficient lighting.

WSFbase = the baseline lighting watts per square foot or linear foot.

WSFeffic = the actual installed lighting watts per square foot or linear foot.

Table 14: Lighting Power Density

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| kWsave | Variable |  | AEPS Application; EDC Data Gathering |
| WHFe | Fixed | Cooled space = 1.12 Refrigerated space: Freezer spaces = 1.15; Medium-temperature refrigerated spaces = 1.29; High-temperature refrigerated spaces = 1.18 Uncooled space =1 | 1 |
| WHFd | Fixed | Cooled space = 1.34 Refrigerated space: Freezer spaces = 1.5; Medium-temperature refrigerated spaces = 1.29; High-temperature refrigerated spaces = 1.18 Uncooled space = 1 | 1 |
| HOURS | Variable |  | AEPS Application; EDC Data Gathering |
| WSFbase | Variable |  | ASHRAE 90.1-2004 |
| WSFeffic | Variable |  | ASHRAE 90.1-2004 |

Source:

- Efficiency Vermont. Technical Reference User Manual: Measure Savings Algorithms and Cost Assumptions (July 2008).

### Fluorescent Lighting Fixture

A fluorescent lighting fixture is a high performance or ‘super’ T8 lamp ballast system.

Algorithms

Energy Savings (kWh) 	= ((WattsBASE – WattsEE )/1000) X HOURS X WHFe

Demand Savings (kW) = ((WattsBASE – WattsEE)/1000) X WHFd

Definition of Variables

WattsBASE = Baseline connected kW.

WattsEE = Energy efficient connected kW.

WHFd	= Waste heat factor for demand to account for cooling savings from efficient lighting.

HOURS = annual lighting hours of use per year.

WHFe	= Waste heat factor for energy to account for cooling savings from efficient lighting

Table 15: Fluorescent Lighting Fixture

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| WHFe | Fixed | Prescriptive measures, default = 1.17 | 1 |
| WHFd | Fixed | Prescriptive measures, default = 1.06 | 1 |
| HOURS | Variable |  | AEPS Application; EDC Data Gathering |
| WattsEE | Fixed | See WattEE and WattBASE Table (below) | 1 |
| WattsBASE | Fixed | See WattEE and WattBASE Table (below) | 1 |

Source:

- Efficiency Vermont. Technical Reference User Manual: Measure Savings Algorithms and Cost Assumptions (July 2008).

Table 16: WattsEE and WattsBASE

| Equipment Description | WattsEE | WattsBASE |
| --- | --- | --- |
| Relamp/Reballast to Super T8 1 Lamp 2 Lamp 3 Lamp 4 Lamp | 25 49 72 94 | 40 68 110 139 |
| Super T8 Troffer/Wrap; Super T8 Industrial/Strip; Super T8 Indirect 1 Lamp 2 Lamp 3 Lamp 4 Lamp | 25 49 72 94 | 32 59 88 114 |

Motors

#### Algorithms

From AEPS application form or EDC data gathering calculate (kW where:

(kW = 0.746 X [(hpbase X RLFbase)/ηbase – (hpee X RLFee)/ηee]

Energy Savings (kWh) = ((kW) X EFLH

Demand Savings (kW) = ((kW) X CF

#### Definition of Variables

hpbase = Rated horsepower of the baseline motor

hpee = Rate horsepower of the energy-efficient motor

RLFbase = Rated load factor of the baseline motor

RLFee = Rated load factor of the energy-efficient motor

ηbase = Efficiency of the baseline motor

ηee = Efficiency of the energy-efficient motor

Table 17: Motors

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| Motor kW | Variable | Based on horsepower and efficiency | AEPS Application; EDC Data Gathering |
| EFLH | Variable | Based on Building Type and Location | AEPS Application; EDC Data Gathering |
| hpbase | Fixed | Comparable EPACT Motor Table Below | EPACT Directory |
| hpee | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| RLFbase | Fixed | 0.70-0.80 | Industry Data |
| RLFee | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| Efficiency – ηbase | Fixed | Comparable EPACT Motor Table Below | From EPACT directory. |
| Efficiency - ηee | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| CF | Fixed | 35% | JCP&L metered data |
| Time Period Allocation Factors | Fixed | Summer/On-Peak 25% Summer/Off-Peak 16% Winter/On-Peak 36% Winter/Off-Peak 23% |  |

Table 18: Baseline Motor Efficiencies - nbase (EPAct)

|  | Open Drip Proof (ODP) # of Poles | Totally Enclosed Fan-Cooled (TEFC) |
| --- | --- | --- |
|  | 6 | 4 | 2 | 6 | 4 | 2 |
|  | Speed (RPM) | Speed (RPM) |
| Size HP | 1200 | 1800 | 3600 | 1200 | 1800 | 3600 |
| 1 | 80.0% | 82.5% | 75.5% | 80.0% | 82.5% | 75.5% |
| 1.5 | 84.0% | 84.0% | 82.5% | 85.5% | 84.0% | 82.5% |
| 2 | 85.5% | 84.0% | 84.0% | 86.5% | 84.0% | 84.0% |
| 3 | 86.5% | 86.5% | 84.0% | 87.5% | 87.5% | 85.5% |
| 5 | 87.5% | 87.5% | 85.5% | 87.5% | 87.5% | 87.5% |
| 7.5 | 88.5% | 88.5% | 87.5% | 89.5% | 89.5% | 88.5% |
| 10 | 90.2% | 89.5% | 88.5% | 89.5% | 89.5% | 89.5% |
| 15 | 90.2% | 91.0% | 89.5% | 90.2% | 91.0% | 90.2% |
| 20 | 91.0% | 91.0% | 90.2% | 90.2% | 91.0% | 90.2% |
| 25 | 91.7% | 91.7% | 91.0% | 91.7% | 92.4% | 91.0% |
| 30 | 92.4% | 92.4% | 91.0% | 91.7% | 92.4% | 91.0% |
| 40 | 93.0% | 93.0% | 91.7% | 93.0% | 93.0% | 91.7% |
| 50 | 93.0% | 93.0% | 92.4% | 93.0% | 93.0% | 92.4% |
| 60 | 93.6% | 93.6% | 93.0% | 93.6% | 93.6% | 93.0% |
| 75 | 93.6% | 94.1% | 93.0% | 93.6% | 94.1% | 93.0% |
| 100 | 94.1% | 94.1% | 93.0% | 94.1% | 94.5% | 93.6% |
| 125 | 94.1% | 94.5% | 93.6% | 94.1% | 94.5% | 94.5% |
| 150 | 94.5% | 95.0% | 93.6% | 95.0% | 95.0% | 94.5% |
| 200 | 94.5% | 95.0% | 94.5% | 95.0% | 95.0% | 95.0% |

### HVAC Systems

The measurement of energy and demand savings for C/I Efficient HVAC for Room AC, Central AC and air cooled DX is based on algorithms. (Includes split systems, air to air heat pumps, packaged terminal systems, water source heat pumps, ground water or ground source heat pumps)

#### Algorithms

Air Conditioning Algorithms:

Energy Savings (kWh) = (Btu/H1000) X (1/EERb-1/EERq) X EFLH

Demand Savings (kW) = (Btu/H1000) X (1/EERb-1/EERq) X CF

Heat Pump Algorithms

Energy Savings-Cooling (kWh) = (Btu/Hc1000) X (1/EERb-1/EERq) X EFLHc

Energy Savings-Heating (kWh) = Btu/Hh1000 X (1/EERb-1/EERq ) X EFLHh

Where c is for cooling and h is for heating.

#### Definition of Variables

BtuH = Cooling capacity in Btu/Hour.

EERb = Efficiency rating of the baseline unit.  For units < 65,000, SEER and HSPF should be used for cooling and heating savings, respectively.

EERq = Efficiency rating of the High Efficiency unit. For units < 65,000, SEER and HSPF should be used for cooling and heating savings, respectively.

CF = Coincidence Factor – The percentage of the total load which is on during electric system’s Peak Window, based on existing measured usage and determined as the average number of operating hours during the peak window period.

EFLH = Equivalent Full Load Hours – A measure of energy use by season during the on-peak and off peak periods.  Value is determined by existing measured data of kWh during the period divided by kW at design conditions.

Table 19: HVAC and Heat Pumps

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| BtuH | Variable | ARI or AHAM or Manufacturer Data | AEPS Application; EDC’s Data Gathering |
| EERb | Variable | See Table below | AEPS Application; EDC’s Data Gathering |
| EERq | Variable | ARI or AHAM Values | AEPS Application; EDC’s Data Gathering |
| CF | Fixed | 67% | Engineering estimate |
| EFLH | Fixed | Allentown Cooling = 784 Hours Allentown Heating = 2,492 Hours Erie Cooling = 482 Hours Erie Heating = 2,901 Hours Harrisburg Cooling = 929 Hours Harrisburg Heating = 2,371 Hours Philadelphia Cooling = 1,032 Hours Philadelphia Heating = 2,328 Hours Pittsburgh Cooling = 737 Hours Pittsburgh Heating = 2,380 Hours Scranton Cooling = 621 Hours Scranton Heating = 2,532 Hours Williamsport Cooling = 659 Hours Williamsport Heating = 2,502 | 1 |
| Cooling Time Period Allocation Factors | Fixed | Summer/On-Peak 45% Summer/Off-Peak 39% Winter/On-Peak 7% Winter/Off-Peak 9% |  |
| Heating Time Period Allocation Factors | Fixed | Summer/On-Peak 0% Summer/Off-Peak 0% Winter/On-Peak 41% Winter/Off-Peak 58% |  |

Sources:

- US Department of Energy.  Energy Star Calculator

Table 20: HVAC Baseline Table

| Equipment Type | Baseline = ASHRAE Std. 90.1 - 2007 |
| --- | --- |
| Unitary HVAC/Split Systems .<=5.4 tons: · >5.4 to 11.25 tons · >11.25 to 20 tons .> 20 to 63.33 tons .> 63.33 tons | 13 SEER 10.1 EER 9.5 EER 9.3 EER 9 EER |
| Air-Air Heat Pump Systems (cooling) · <=5.4 tons: · >5.4 to 11.25 tons · >11.25 to 20 tons .>= 21 to 30 tons | 13 SEER 9.9 EER 9.1 EER 8.8 EER |
| Water Source Heat Pumps (cooling) < 1.42 tons ≥ 1.42 tons | 11.2 EER 12.0 EER |
| GWSHPs Open and Closed Loop All Capacities | 16.2 EER |
| Package Terminal Systems (Replacements) PTAC (cooling) PTHP (cooling) PTHP (heating) | 10.9 - (0.213 x Cap / 1000) EER 10.8 - (0.213 x Cap / 1000) EER 2.9 - (0.213 x Cap / 1000) EER |

### Electric Chillers

The measurement of energy and demand savings for C/I Chillers is based on algorithms with key variables (i.e., kW/ton, Coincidence Factor, Equivalent Full Load Hours) measured through existing end-use metering of a sample of facilities.

#### Algorithms

Energy Savings (kWh) = Tons X (kW/tonb – kW/tonq) X EFLH

Demand Savings (kW) = Tons X (kW/tonb – kW/tonq) X CF

#### Definition of Variables

Tons = The capacity of the chiller (in tons) at site design conditions accepted by the program.

kW/tonb = Baseline, found in the Chiller verification summary table.

kW/tonq  = This is the manufacturer data and equipment ratings in accordance with ARI Standard 550/590 latest edition.

CF = Coincidence Factor – Represents the percentage of the total load which is on during electric system’s Peak Window derived from JCP&L metered data.

EFLH = Equivalent Full Load Hours – A measure of chiller use by season determined by measured kWh during the period divided by kW at design conditions from JCP&L measurement data.

Table 21: Electric Chillers

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| Tons | Variable | From AEPS Application; EDC Data Gathering |  |
| kW/tonb | Fixed | Water Cooled Chillers (=<150 tons) Baseline:…………… 0.703 kW/Ton Water Cooled Chillers (151 to <300 tons) Baseline:…………… 0.634 kW/Ton Water Cooled Chillers (>301 tons) Baseline:…………… 0.577 kW/Ton Air Cooled Chillers (<150 tons) Baseline:…………… 1.256 kW/Ton | ASHRAE 90.1 2004 |
| kW/tonq | Variable | ARI Standards 550/590-Latest edition | AEPS Application; EDC Data Gathering |
| CF | Fixed | 67% | Engineering estimate |
| EFLH | Fixed | Allentown Cooling = 784 Hours Erie Cooling = 482 Hours Harrisburg Cooling = 929 Hours Philadelphia Cooling = 1,032 Hours Pittsburgh Cooling = 737 Hours Scranton Cooling = 621 Hours Williamsport Cooling = 659 Hours | 1 |
| Time Period Allocation Factors | Fixed | Summer/On-Peak 45% Summer/Off-Peak 39% Winter/On-Peak 7% Winter/Off-Peak 9% |  |

Sources:

- US Department of Energy.  Energy Star Calculator

For certain fixed components, studies and surveys developed based on a review of manufacturer’s data, other utilities, regulatory commissions or consultant’s reports will be used to update the values for future filings.

### Variable Frequency Drives

The measurement of energy and demand savings for C/I Variable Frequency Drive for VFD AEPS applications is for HVAC fans and water pumps only.  VFD AEPS applications for other than this use should follow the custom path.

#### Algorithms

Energy Savings (kWh) = 0.746 X HP X RLF/ηmotor X ESF X FLHbase

Demand Savings (kW) = 0.746 X HP X RLF/ηmotor X DSF

#### Definitions of Variables

HP = nameplate motor horsepower.

RLF = Rated Load Factor.  Ratio of the peak running load to the nameplate rating of the motor.

ηmotor = Motor efficiency at the peak load.  Motor efficiency varies with load.  At low loads of relative to the rated hp (usually below 50%) efficiency often drops dramatically.

ESF = Energy Savings Factor.  The energy savings factor is equal to 1 – FLHasd/FLHbase.  This factor can also be computed according to fan and pump laws assuming an average flow reduction and a cubic relationship between flow rate reduction and power draw savings.

FLHasd = Full Load Hours of the fan/pump with the VSD.

FLHbase = Full Load Hours of the fan/pump with baseline drive.

DSF = Demand Savings Factor, calculated by determining the ratio of the power requirement for baseline and VFD control at peak conditions.

DSF = 1 – (kWasd/kWbase)peak.

kWasd = peak demand of the motor under the variable control conditions.

kWbase = peak demand of the motor under the base operating conditions.

Table 22: Variable Frequency Drives

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| Motor HP | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| kWh/motor HP | Fixed | 1,653 for VAV air handler systems. 1,360 for chilled water pumps. | JCP&L metered data for VFD’s and chillers. |
| RLF | Variable | Dependent on HP and peak running load |  |
| ηmotor | Variable | Nameplate or manufacturer specs | AEPS Application; EDC Data Gathering |
| ESF | Variable | Dependent on full load of base and VFD |  |
| FLHasd | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| FLHbase | Fixed |  | Manufacturer Data |
| DSF | Variable | Dependent on base and variable peak demand |  |
| kWasd | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| kWbase | Fixed |  | Manufacturer Data |
| Time Period Allocation Factors | Fixed | Summer/On-Peak 22% Summer/Off-Peak 10% Winter/On-Peak 47% Winter/Off-Peak 21% |  |

### Air Compressors with Variable Frequency Drives

The measurement of energy and demand savings for variable frequency drive (VFD) air compressors.

#### Algorithms

Energy Savings (kWh) = 774 X HP

Demand Savings (kW) = 0.129 X HP

Coincident Peak Demand Savings (kW) = 0.106 X HP

#### Definitions of Variables

HP = nameplate motor horsepower

Table 23: Air Compressors with VFDs

| Component | Type | Value | Source |
| --- | --- | --- | --- |
| Motor HP | Variable | Nameplate | AEPS Application; EDC Data Gathering |
| kWh/motor HP | Fixed | 774 | 1 |
| kW/motor HP | Fixed | 0.129 | 1 |
| Coincident Peak kW/motor HP | Fixed | 0.106 | 1 |
| Time Period Allocation Factors | Fixed | Summer/On-Peak 28% Summer/Off-Peak 39% Winter/On-Peak 14% Winter/Off-Peak 19% |  |

Sources:

1.  Aspen Systems Corporation, Prescriptive Variable Speed Drive Incentive Development Support for Industrial Air Compressors, Executive Summary, June 20, 2005.

# Demand Response Programs

Commercial and Industrial Application, Residential Applications

## Commercial and Industrial Applications

Each commercial and industrial application will be treated independently as a custom program.   An application must be submitted, containing adequate documentation fully describing the energy efficiency measures installed or proposed and an explanation of how the installed facilities qualify for A E Cs.  Each program application will be required to include:

- Program Name

- Program Utility Company

- Program Location (s)

- Type of facilities in which the measures, systems, processes, or strategies will be implemented

- Customer class and end-use served

- Estimated demand reduction value (kW) per measure including supporting documentation (i.e. engineering estimates or documentation of verified savings from comparable projects)

- Estimated energy reduction value (kWh) throughout the year

- The date by which commercial operation is expected

The required application information is the minimum requirement for submitting a program.  If a submitter relies on PJM protocols for participation in the PJM market, the PJM methodology will be accepted as a reporting method.

## Residential Applications

## Algorithms

The general form of the equation for the residential demand response measure savings algorithms is:

Number of Units X Savings per Unit

To determine resource savings, the per unit estimates in the algorithms will be multiplied by the number of demand response units.  The number of units will be determined by the program.  Per unit savings estimates will be estimated by each specific measure.

### Direct Load Control (Air Conditioning Cycling and Pool Pump Load Control)

Electricity Impact (kWh) = ESav X Units X Hours

Demand Impact (kW) = ESav X Units

Definition of Terms

ESav = Energy Saved in One Hour in kW

Units = Number of Units in the Program

Hours = Number or hours throughout the year the measure operates

| Component | Type | Value | Sources |
| --- | --- | --- | --- |
| ESav | Fixed | Air conditioning Cycling = 0.72 kW Pool Pump Load Control = 0.75 kW | 1 |
| Units | Variable |  | AEPS Application; EDC Data Gathering |
| Hours | Variable |  | AEPS Application; EDC Data Gathering |

Sources:

1.  Public Service Electric and Gas Company.  Petition for Approval of Demand Response Programs.  August 5, 2008.

Appendix A
Measure Lives

Measure Lives Used in Cost-Effectiveness Screening February 2008

| PROGRAM/Measure *For the purpose of calculating the total Resource Cost Test for Act 129, measure cannot claim savings for more than fifteen years. | Measure Life |
| --- | --- |
| Residential Programs |  |
| Energy Star Appliances |  |
| Energy Star Refrigerator post-2001 | 13 |
| Energy Star Refrigerator 2001 | 13 |
| Energy Star Dishwasher | 11 |
| Energy Star Clothes Washer | 11 |
| Energy Star Dehumidifier | 12 |
| Energy Star Room Air Conditioners | 10 |
| Energy Star Lighting |  |
| Compact Fluorescent Light Bulb | 6.4 |
| Recessed Can Fluorescent Fixture | 20* |
| Torchieres (Residential) | 10 |
| Fixtures Other | 20* |
| Energy Star Windows |  |
| WINDOW -heat pump | 20* |
| WINDOW -gas heat with central air conditioning | 20* |
| WIN-oil heat/CAC | 20 |
| WIN-oil No CAC | 20 |
| WINDOW – electric heat without central air conditioning | 20* |
| WINDOW – electric heat with central air conditioning | 20* |
| Refrigerator/Freezer Retirement |  |
| Refrigerator/Freezer retirement | 8 |
| Residential New Construction |  |
| Single Family - gas heat with central air conditioner | 20* |
| Single Family - oil heat with central air conditioner | 20* |
| Single Family - all electric | 20* |
| Multiple Single Family (Townhouse) – gas heat with central air conditioner | 20* |
| Multiple Single Family (Townhouse) – oil heat with central air conditioner | 20* |
| Multiple Single Family (Townhouse) - all electric | 20* |
| Multi-Family – gas heat with central air conditioner | 20* |
| Multi-Family - oil heat with central air conditioner | 20* |
| Multi-Family - all electric | 20* |
| Energy Star Clothes Washer | 11 |
| Recessed Can Fluorescent Fixture | 20* |
| Fixtures Other | 20* |
| Efficient Ventilation Fans with Timer | 10 |
| Residential Electric HVAC |  |
| Central Air Conditioner SEER 13 | 14 |
| Central Air Conditioner SEER 14 | 14 |
| Air Source Heat Pump SEER 13 | 12 |
| Air Source Heat Pump SEER 14 | 12 |
| Central Air Conditioner proper sizing/install | 14 |
| Central Air Conditioner Quality Installation Verification | 14 |
| Central Air Conditioner Maintenance | 7 |
| Central Air Conditioner duct sealing | 14 |
| Air Source Heat Pump proper sizing/install | 12 |
| Energy Star Thermostat (Central Air Conditioner) | 15 |
| Energy Star Thermostat (Heat Pump) | 15 |
| Ground Source Heat Pump | 30* |
| Central Air Conditioner SEER 15 | 14 |
| Air Source Heat Pump SEER 15 | 12 |
| Home Performance with ENERGY STAR |  |
| Blue Line Innovations – PowerCost MonitorTM | 5 |
| Non-Residential Programs |  |
| C&I Construction |  |
| Commercial Lighting — New | 15 |
| Commercial Lighting — Remodel/Replacement | 15 |
| Commercial Custom — New | 18* |
| Commercial Chiller Optimization | 18* |
| Commercial Unitary HVAC — New - Tier 1 | 15 |
| Commercial Unitary HVAC — Replacement - Tier 1 | 15 |
| Commercial Unitary HVAC — New - Tier 2 | 15 |
| Commercial Unitary HVAC — Replacement Tier 2 | 15 |
| Commercial Chillers — New | 20* |
| Commercial Chillers — Replacement | 20* |
| Commercial Small Motors (1-10 horsepower) — New or Replacement | 20* |
| Commercial Medium Motors (11-75 horsepower) — New or Replacement | 20* |
| Commercial Large Motors (76-200 horsepower) — New or Replacement | 20* |
| Commercial Variable Speed Drive — New | 15 |
| Commercial Variable Speed Drive — Retrofit | 15 |
| Commercial Comprehensive New Construction Design | 18* |
| Commercial Custom — Replacement | 18* |
| Industrial Lighting — New | 15 |
| Industrial Lighting — Remodel/Replacement | 15 |
| Industrial Unitary HVAC — New - Tier 1 | 15 |
| Industrial Unitary HVAC — Replacement - Tier 1 | 15 |
| Industrial Unitary HVAC — New - Tier 2 | 15 |
| Industrial Unitary HVAC — Replacement Tier 2 | 15 |
| Industrial Chillers — New | 20* |
| Industrial Chillers — Replacement | 20* |
| Industrial Small Motors (1-10 horsepower) — New or Replacement | 20* |
| Industrial Medium Motors (11-75 horsepower) — New or Replacement | 20* |
| Industrial Large Motors (76-200 horsepower) — New or Replacement | 20* |
| Industrial Variable Speed Drive — New | 15 |
| Industrial Variable Speed Drive — Retrofit | 15 |
| Industrial Custom — Non-Process | 18* |
| Industrial Custom — Process | 10 |
| Building O&M |  |
| O&M savings | 3 |

# Footnotes

Order entered on October 3, 2005, under the above-referenced caption and Docket Number.

Id. at page 13.

Order entered on January 16, 2009, at Docket No. M-2008-2069887, at page 13 (Implementing the energy efficiency and conservation program requirements of Act 129 of 2008, 66 Pa.C.S. §§ 2806.1).

See page 13 of Implementation Order at Docket No. M-2008-2069887, entered January 16, 2009.

Commission staff developed this proposed TRM in consultation with Clean Power Markets, the Commission’s Alternative Energy Program Administrator, and Lawrence Berkeley National Laboratory.

42 U.S.C.S. § 6295

National Action Plan for Energy Efficiency (2008).  Understanding Cost-Effectiveness of Energy Efficiency Programs:  Best Practices, Technical Methods, and Emerging Issues for Policy-Makers.  Energy and Environmental Economics, Inc. and Regulatory Assistance Project.  www.epa.gov/eeactionplan

Note:  Information in the TRM specifically relating to the AEPS Act are shaded in gray.

Values for lighting, air conditioners, chillers and motors are based on measured usage from a large sample of participants from 1995 through 1999. Values for heat pumps reflect metered usage from 1996 through 1998 and variable speed drives reflect metered usage from 1995 through 1998.

Note:  Programs where measures are replaced before the end of their useful life are considered Custom Measures.  In these programs, savings are measured from the efficient unit versus the replaced unit for the existing life of the unit, then from the efficiency unit versus a new standard unit for the remaining life of the efficient measure.

Desuperheaters are generally utilized to reduce the temperature of superheated steam to a desired set point for the protection of downstream piping and equipment or for the supply of saturated steam for heat transfer purposes.

Energy Information Administration.  Residential Energy Consumption Survey.  2005.  http://www.eia.doe.gov/emeu/recs/recs2005/hc2005_tables/detailed_tables2005.html

A new standard for BESTEST is currently being developed.  The existing 1995 standard can be found at http://www.nrel.gov/docs/legosti/fy96/7332a.pdf .

A listing of the approved software available at http://www.waptac.org/si.asp?id=736 .

A listing of the approved software available at http://resnet.us .

M&V Evaluation, Home Performance with Energy Star Program, Final Report, Prepared for the New York State Energy Research and Development Authority, Nexant, June 2005.

Source:  PECO Comments on the PA TRM, received March30, 2009.

Results reflect metered use from 1995 – 1998.

Results reflect metered use from 1995 – 1999.

Application criteria for submittals is taken from ISO New England’s Measurement and Verification of Demand Reduction Value from Demand Resources.  October 1, 2007.

Energy Star Appliances, Energy Star Lighting, and several Residential Electric HVAC measures lives updated February 2008. U.S. Environmental Protection Agency and U.S. Department of Energy, Energy Star. <http://www.energystar.gov/>.