ANNUAL REPORT

ADVANCED METERING ACTIVITIES

OCTOBER 1, 1998-OCTOBER 1, 1999

SUBMITTED TO

THE PENNSYLVANIA PUBLIC UTILITY COMMISSION

PURSUANT TO 52 PA CODE (57.253(a)(3)

METERING COMMITTEE

OCTOBER 1, 1999

TABLE OF CONTENTS

EXECUTIVE SUMMARY.......................................................................................3

CHRONOLOGY & SUMMARY OF ACTIVITIES................................................4

OVERVIEW & CONCLUSIONS............................................................................7

METERING WORKING GROUP & METERING COMMITTEE.......................8

ADVANCED METER CATALOG-“GRANDFATHERED”...............................19

EXECUTIVE SUMMARY

This Advanced Metering Activities Annual Report (Annual Report) is submitted to the Pennsylvania Public Utility Commission (Commission) pursuant to 52 Pa Code (57.253(a)(3) and provides a summary of activities related to advanced metering which occurred during the period October 1, 1998 to October 1, 1999.  The Annual Report was distributed via e-mail to the Metering Working Group for comment.  The comments received were addressed and the document was subsequently finalized as provided herein.

The activities during the October 1, 1998 to October 1, 1999 time period established the foundation for future advanced metering activities in the Commonwealth of Pennsylvania under the “Electricity Generation Customer Choice and Competition Act”(Act).  During this period, the structure, processes,  procedures and standards were developed to: (1) facilitate customer selection and deployment of a qualified advanced meter; and (2) facilitate advanced meter services provider certification in Electric Distribution Company (EDC) Service Territories using a competitive advanced metering market.

Significant events which occurred during the year include Commission  approval of: (1) a revised final rulemaking on advanced meter deployment;

(2) Advanced Meter Standards Report; (3) Reference Manual on Advanced Meter Qualification and Review; Competitive Metering Specifications/Advanced Meter Services Provider Certification (Reference Manual); (4) Listing of “Grandfathered” advanced meters, meter-related devices and/or networks submitted by jurisdictional EDCs; and (5) EDC “Grandfathered” Advanced Meter Tariff Supplement Filings and Advanced Meter Catalog (Catalog)-“Grandfathered” devices.

The Advanced Meter Deployment for Electricity Providers Regulations at 52 Pa Code ((57.251 to 57.259, Advanced Meter Standards Report and Reference Manual documents establish the structure, processes, procedures and standards which govern advanced metering activities.  The Catalog lists the “grandfathered” devices eligible for deployment in the respective EDC Service Territories.  As of the date of this Annual Report, there have been no applications for inclusion of additional advanced meters, meter-related devices and/or networks into the Catalog or for advanced meter services provider certification.  The year has been primarily a developmental and transitional period.

Chronology and Summary of Activities:  October 1, 1998-October 1, 1999

(  Advanced Meter Deployment for Electricity Providers Regulations

On October 16, 1998 the Commission approved a revised final rulemaking order on Advanced Meter Deployment for Electricity Providers at Docket No. L-00970128 52 Pa Code ((57.251-57.259.  The final regulations were published in the Pennsylvania Bulletin and became effective on December 26, 1998 at 28 Pa.B. 6302.  The final regulations establish the structure, processes, procedures and standards to facilitate customer selection and deployment of a qualified advanced meter.

These regulations retain advanced metering as a regulated function of the EDC unless the Commission approves a Restructuring Settlement Agreement incorporating provisions to the contrary.  The following EDC Service Territories are using a non-competitive advanced metering market: (1) Citizen’s Electric Company; (2) Duquesne Light Company; (3) Pike County Light and Power;

(4) Pennsylvania Power Company (PennPower); (5) UGI Utilities (UGI); and

(6) Wellsboro Electric Company.  The following EDC Service Territories are using a competitive advanced metering market as a result of a Restructuring Settlement Agreement with the Commission: (1) Allegheny Power System;

(2) GPU; (3) PECO Energy Company (PECO); and (4) PP&L.

(  Advanced Meter Standards Report

On March 31, 1999 the Commission adopted a Final Order at

Docket No. M-00991219 which approved the Metering Committee Advanced Meter Standards Report required pursuant to 52 Pa Code (57.254 (b).  This Final Order was published in the Pennsylvania Bulletin and became effective on April 17, 1999 at 29 Pa.B. 2112.  The standards supplement the Advanced Meter Deployment for Electricity Providers regulations and seek to maintain accuracy, performance and safety of advanced meter services while simultaneously facilitating technical innovation.

This report is divided into five sections: I. Summary of Advanced Meter Standards; II. Table of Tests in ANSI C12.1 and C12.20; III. Certification Testing Requirements; IV. Registration and Centralized Database for Compliant Meter Type; and V. List of Metering Working Group and Metering Committee members.

Section I summarizes the various American National Standards Institute (ANSI) Standards, Edison Electric Institute (EEI) Metering Handbook, National Electric Code (NEC)/Local Requirements, and applicable Federal Communications (FCC) Regulations that meters must comply with to be considered for approval as advanced meters in the Commonwealth of Pennsylvania.  The section also stresses that products and systems deemed used and useful by the State’s utilities today should be “grandfathered” for use going forward in order to avoid the prospect of premature removal of a product from service. Section II provides a checklist for various tests associated with ANSI C12 compliance.  Section III describes the certification testing requirements that advanced meter products used in Pennsylvania must comply with.  Section IV requires manufacturers to file with the Commission their meter type self-certification document to state compliance with applicable testing requirements.  Section V lists the Metering Working Group and Metering Committee membership.  (See page 8 for updated membership listing)

(  Reference Manual

On April 1, 1999 the Commission issued a Secretarial Letter approving the Metering Committee Reference Manual at Docket No. M-00991233.  This document summarizes the procedures and requirements related to: 1. Advanced Meter Qualification; and 2. Competitive Metering Specifications and Advanced Meter Services Provider Certification for licensed Electric Generation Suppliers (EGSs) in PECO, GPU, PP&L and Allegheny Power Service Territories.

The Advanced Meter Qualification materials summarize the process established in the Advanced Meter Regulations 52 Pa Code ((57.251-57.259 for advanced meter, meter-related device or network inclusion in the Commission’s  Catalog.  The Competitive Metering Specifications and Advanced Meter Services Provider Certification materials present the competitive metering specifications and advanced meter services provider certification application approved by the Commission in PECO, GPU, PP&L and Allegheny Power Service Territories.

The Commission Docket Numbers, Entered Dates and Effective Dates for competitive advanced metering services pursuant to the various Restructuring Settlement Agreements and Competitive Metering Specifications are as follows:

(1) PECO-  Docket No. R-00973953 & P-00971265 Entered July 1, 1998;

Effective January 1, 1999 for all customer classes with no conditions.

(2) GPU- Docket No. R-00974008 & R-00974009 Entered

November 5, 1998;

Effective January 1, 1999 a licensed EGS may provide, finance, own, calibrate and remotely read advanced meters for service to residential customers; An EGS may not install, initially test or maintain advanced meters for residential customers prior to January 1, 2004.  Prior to January 1, 2004 all advanced meters for residential customers must be installed, initially tested and maintained by GPU employees.  The January 1, 2004 requirements do not apply to C&I customers.

(3) PP&L-  Docket No. R-00973954 Entered August 28, 1998;

Effective January 1, 1999 a licensed EGS may provide, finance, own, calibrate and remotely read advanced meters for service to residential customers; An EGS may not install, initially test or maintain advanced meters for residential customers prior to January 1, 2003.  Prior to January 1, 2003 all advanced meters for residential customers must be installed, initially tested and maintained by PP&L employees.  The January 1, 2003 requirements do not apply to C&I customers.

(4) Allegheny Power-  Currently working on Competitive Metering Specs.

(  “Grandfathered” Advanced Meters, Meter-Related Devices & 		      Networks

On May 13, 1999, the Commission issued a Secretarial Letter at

Docket No. M-00991233 which approved the listing of “grandfathered” advanced meters, meter-related devices and/or networks submitted by the jurisdictional EDCs.  In compliance with applicable Reference Manual provisions, the Secretarial Letter also directed the EDCs to prepare and submit to the Commission a Tariff Filing regarding these “grandfathered” devices.

(  “Grandfathered Advanced Meter Tariff Supplement Filings & Advanced Meter Catalog

On July 16, 1999 the Commission issued a Secretarial Letter at

Docket No. M-00991233 which approved the EDC “Grandfathered” Advanced Meter Tariff Supplement Filings and Catalog.  These Tariff Supplement Filings:

(1) add certain clarifying language to existing EDC Electric Service Tariffs and/or Supplier Tariffs addressing “grandfathered” devices and other related areas as deemed necessary by the respective EDCs; and (2) list or reference the “grandfathered” devices contained in Attachment 1 thereto as eligible for deployment in the respective EDC Service Territories upon Commission approval and inclusion in the Catalog.

OVERVIEW & CONCLUSIONS

In retrospect the year October 1, 1998 to October 1, 1999 was a crucial period wherein the fundamental structure, processes, procedures and standards were developed to govern advanced metering in the Commonwealth of Pennsylvania under the Act.  The intent of the advanced metering activities was to develop a framework which facilitates customer selection and deployment of a qualified advanced meter as well as certification of licensed EGSs as advanced meter services providers.

To this end, the Commission approved several Orders and/or Secretarial Letters between October 1998 and July 1999 dealing with regulations, standards, procedures, “Grandfathered” devices, EDC Tariff Supplement Filings and the initial Catalog.  The period began with approval of regulations and ended with approval of the EDC Tariff Supplement Filings and Catalog for “Grandfathered” devices.  The underlying structure was therefore not finalized until July 1999.

With this foundation in place, the Commonwealth is prepared to move from a transitional and developmental year to the actual implementation period wherein interested parties will be able to: (1) select a qualified advanced meter from the Catalog for deployment; (2) submit an application for inclusion of a qualified advanced meter, meter-related device and/or network in the Catalog; and

(3) submit an application as a licensed EGS for certification to perform advanced meter services as defined in applicable EDC Service Territories.  Commission staff included  in the Metering Working Group Membership List will provide ongoing administration and coordination of the various processes and procedures required pursuant to the Advanced Meter Deployment for Electricity Providers Regulations, Advanced Meter Standards Report and Reference Manual.

METERING WORKING GROUP & *METERING COMMITTEE

ELECTRIC DISTRIBUTION COMPANIES

ALLEGHENY POWER

* Thomas L. Dugan

Allegheny Power                               Phone: (724) 626-5250

South Seventh Street                         Fax:     (724) 626-5290

Connellsville, PA  15425                  E-Mail:tdugan1@alleghenypower.com

** Damian S. Wess

Allegheny Power                               Phone: (724) 626-5220

S. Seventh Street                               Fax:    (724) 626-5290

Connellsville, Pa. 15425                   E-Mail: dwess@alleghenypower.com

CITIZEN’S ELECTRIC COMPANY

Eric Winslowe

1775 Indusrtial Blvd                          Phone: (570) 524-2231

PO Box 551                                        Fax:     (570) 524-5887

Lewisburg, PA 17837-0551               E-Mail: winslowe@citizenselectric.com

DUQUESNE LIGHT

* David P. Barger

Duquesne Light Company                  Phone: (412) 393-8705

2101 Beaver Avenue M-MT               Fax:     (412) 393-8737

Pittsburgh, PA  15233                         E-Mail: david_p_barger@dlc.dqe.com

** Arlin Rummel

Duquesne Light Company

2102 Beaver Avenue                         Phone: (412) 393-8779

M-MT                                                Fax:     (412) 393-8737

Pittsburgh, PA 15233                         E-Mail: arlin_a_rummel@dlc.dqe.com

GPU

* Earl E. Frantz

GPU Energy                                      Phone: (610) (610)-375-5731

P.O. Box 15152                                 Fax: (610)-396-8546

Reading, PA  19612-5152	 E-Mail: efrantz@gpu.com

** James Catanach

GPU Energy                                       Phone: (610) 375-5481

PO. Box 15152                                   Fax:     (610) 396-8534

Reading, PA 19612-5152                   E-Mail:jcatanach@GPU.com

PECO ENERGY COMPANY

** Peter W. Linn

PECO Energy Company

Corporate Strategy                               Phone:  (215) 841-6147

2301 Market Street, S4-4                     Fax:      (215)  841-4728

Philadelphia, PA  19101                       E-Mail: plinn@peco-energy.com

*Gustavo Paz

PECO Energy                                    Phone:  (610) 648-7860

1060 West Swedesford Road             Fax:      (610) 648-7965

Berwyn, PA  19312                           E-Mail: gpaz@peco-energy.com

PP&L

*Anthony Osmanski

Pennsylvania Power & Light Co.

Humboldt Industrial Park                  Phone:  (570) 384-5202

One Scotch Pine Drive                      Fax:       (570) 384-5311

Hazleton, PA  18201                         E-Mail: amosmanski@papl.com

** Wayne R. Fairchild

PP&L Inc

System Facilities Center                    Phone: (570) 384-5303

One Scotch Pine Drive                      Fax:     (570) 384-5311

Hazelton, PA 18201                          E-Mail: wrfairchild@papl.com

PENN POWER

* Scott R. Wyman

Pennsylvania Power Company

P.O. Box 891                                     Phone: (724) 656-5310

1 East Washington Street                  Fax:     (724) 656-4363

New Castle, PA 16103-0891            E-Mail: wymans@firstenergycorp.com

** Gregory F. Hussing

First Energy Corp                             Phone: (330) 384-5144

76 South Main Street                        Fax:     (330) 384-3869

Akron, OH 44208                             E-Mail:hussingg@firstenergycorp.com

PIKE COUNTY LIGHT & POWER COMPANY

Michael Pagliocca, Jr.

Orange & Rockland                              Phone: (914) 577-3145

390 West Route 59                               Fax:

Spring Valley, New York 10977-5300 E-Mail: mpagliocca@oru.com

UGI

** Vincent DeGiusto, Sr.

UGI Utilities, Inc.

400 Stewart Rd.                                  Phone: (570) 830-1290

P.O. Box 3200                                    Fax:     (570) 830-1190

Wilkes-Barre, PA  18773-3200          E-Mail: vdegiustosr@ugi.com

Rich Gill

UGI Utilities, Inc.

400 Stewart Rd.                                  Phone: (570) 830-1233

P.O.Box 3200                                     Fax:     (570) 830-1190

Wilkes-Barre, PA  18773-3200          E-Mail: rgill@ugi.com

* Robert F. Pavolonis

UGI Utilities Inc                                 Phone: (570) 830-1288

400 Stewart Road P.O. Box 3200       Fax:     (570) 830-1190

Wilkes Barre, PA 18773-3200            E-Mail: rpavolonis@ugi.com

WELLSBORO ELECTRIC COMPANY

Robert S. McCarthy

Wellsboro Electric Company

PO Box 138                                        Phone: (717) 724-3516

33 Austin Street                                  Fax: (717)724-1798

Wellsboro, PA 16901                         E-Mail: rmcCarthy@wellsboroelectric.com

RUMSEY ELECTRIC COMPANY

Russell Hamilton

Rumsey Electric Co                            Phone: (724) 539-1266

2223 Dailey Avenue                           Fax:     (724) 539-1336

Latrobe, PA 15650                              E-Mail: rwhrumsey@aol.com

PENNSYLVANIA ELECTRIC ASSOCIATION

Jim Cunningham

Pennsylvania Electric Assoc               Phone: (717) 901-0603

800 North Third Street                        Fax:     (717) 257-5858

Harrisburg, PA 17102                         E-mail: jcunningham@paea.org

David O. Epple

Pennsylvania Electric Association      Phone: (717) 901-0605

800 North Third Street                        Fax:     (717) 257-5858

Harrisburg, PA  17102                        E-Mail: depple@paea.org

ELECTRIC GENERATION SUPPLIERS

STRATEGIC ENERGY LIMITED

*Alexander Galatic

Senior Energy Consultant

SEL                                                     Phone:   (412) 394-5629

Two Gateway Center                           Fax:      (412) 394-6576

Pittsburgh, PA  15222                         E-Mail: agalatic@sel.com

** Michael Cammerata

Strategic Energy Limited                    Phone:  (412) 394-5622

Two Gateway Center                           Fax:     (412) 394-6576

Pittsburgh, PA 15222                          E-Mail: mcammera@sel.com

ALLEGHENY ELECTRIC  COOPERATIVE

* John Dalton

PA Rural Electric Association

212 Locust Street                                 Phone:  (717) 901-4507

P.O. Box 1266                                     Fax:       (717) 234-3908

Harrisburg, PA  17108-1266               E-Mail: jdalton@prea.com

AMERICAN ENERGY SOLUTIONS

David Butsack

American Energy                                Phone:  (610) 372-8500

516 Kenhorst Bivd                              Fax:      (610) 777-3770

Reading PA 19611                              E-Mail: david..b@prodigy.net

GPU ADVANCED RESOURCES

* Stephen Russial

GPU Advanced Resources

2675 Morgantown Road                     Phone: (888) 850-6150 ext 5806

Suite GH-2-3300                                Fax:      (610) 856-5849

Reading, PA 19607                            E-Mail: srussial@gpu.com

CONECTIV POWER DELIVERY

David R. Elzey

Conectiv Power Delivery                  Phone: (302) 454-4184

PO Box 9239                                      Fax:     (302) 454-4167

Newark, DE 19714                             E-Mail: david.elzey@conectiv.com

Maury Ward

Conectiv Power Delivery                  Phone: (609) 965-3940

PO Box 1264                                      Fax:     (609) 965-3939

Pleasantville, NJ 08232                      E-Mail: maurice.ward@conectiv.com

ENRON

* Clifford Pelchat

ENRON                                              Phone:  (713) 853-0490

1400 Smith Street                               Fax:      (713) 646-5926

Houston, Texas 77002                        E-Mail: cpelchat@ees.enron.com

** Brian Musthaler

ENRON                                              Phone: (713) 853-9323

1400 Smith Street                               Fax:

Houston Texas 77002                         E-Mail: brian.musthaler@ees.enron.com

Jeff Brown

Director, Government Affairs

ENRON Corp.                                    Phone:  (615) 851-5499

400 Professional Park Drive               Fax:      (615) 851-5497

Goodlettsville, TN 37072                   E-Mail: jeff_brown@ees.enron.com

DUKE SOLUTIONS

* James Mayhew

Director

Duke Solutions                                    Phone: (704) 373-6884 or 6885

128 South Tyron Street FC05A           Fax:    (704) 382-1255

Charlotte, NC 28202                           E-Mail: jamayhew@duke-energy.com

Sabrina Austin

Duke Solutions                                    Phone (704) 373-6885

128 South Tyron Street FC05A          Fax:    (704) 373-6392

Charlotte, NC 28202                           E-Mail: skaustin@duke-energy.com

LG&E RETAIL ACCESS SERVICES

Diane Rihn

LG&E Retail Access Services             Phone: (502) 627-3919

220 West Main Street                          Fax:     (502) 627-2985

Louisville, KY 40202                          E-Mail: diane.rihn@lgeenergy.com

NEW ENERGY VENTURES

* Jeff Bladen

New Energy Ventures                         Phone: (215) 563-9290

1845 Walnut Street Suite 2525            Fax:      (215) 563-9292

Philadelphia, PA 19103                       E-Mail: jbladen@newenergy.com

METER COMPANIES

ABB POWER T&D CO., INC.

Jyoti Lynch

ABB Power T&D Co., Inc.                 Phone:  (919) 212-4835

208 South Rogers Lane                       Fax:      (919) 250-5489

Raleigh, NC 27610                             E-Mail: jyoti.a.lynch@us.abb.com

Pat Corrigan

ABB Power T&D Co., Inc.                 Phone:  (919) 212-5071

208 South Rogers Lane                       Fax:      (919) 212-4717

Raleigh, NC 27610                             E-Mail: pat.m.corrigan@ustra.mail.abb.com

Ted McClelland

ABB Power T&D Co., Inc                  Phone:  (919) 212-4827

208 South Rogers Lane                       Fax:      (919-250-5489

Raleigh, NC 27610-2107                    E-Mail: ted.mcclelland@ustra.mail.abb.com

Kathy Smith

ABB Power T&D Co., Inc.                 Phone: (919) 212-5429

208 South Rogers Lane                       Fax:     (919) 212-4717

Raleigh, NC 27610                             E-mail: kathy.smith@ustra.mail.abb.com

AES CORPORATION

Gerald Mimno

AES Corporation                                 Phone:  (978) 535-7310 Ext. 125

285 Newbury Street                             Fax:      (979) 535-7313

Peabody, MA 01960                            E-Mail mimno@tiac.net

AMERICAN INNOVATIONS, LTD.

Brooks Walsh

American Innovations Ltd.                  Phone: (508) 760-6967

3 Pinefield Lane                                   Fax:     (508) 760-5416

South Dennis, MA 02660                    E-Mail: brooks@aimetering.com

CB ASSOCIATES

Ralph Amato

CB Associates                                     Phone:   (973) 948-5100

P.O. Box 890                                      Fax:       (973) 948-5150

Branchville, NJ 07826                        E-Mail: ralphamato@cb-associates.com

CELLNET DATA SYSTEMS

Jim Peters

CellNet Data Systems

3 Agronomy Road                               Phone: (860) 429-4502

P.O. Box 789                                       Fax:     (860) 429-5288

Storrs, CT 06268                                 E-Mail: jsp3@neca.com

Chris King

CellNet Data Systems                         Phone: (925) 543-1017

12667 Alcosta Boulevard                   Fax:     (925) 543-1060

San Ramon, CA 94583                       E-Mail: chrisk@CellNet.com

Mark W. Schaefer

CellNet Data Systems                         Phone: (412) 635-2396

731 Venango Avenue                         Fax:    (412) 635-2397

Pittsburgh, PA 15209                         E-Mail: schaefer@cellnet.com

COMVERGE TECHNOLOGIES

Richard A. Michelfelder, Ph.D.          Phone: (973) 560-4800

80 S. Jefferson Road                           Fax:     (973) 560-4806

Whippany, NJ 07981                          E-Mail: ram@comverge-tech.com

John F. Rossi

Comverge Technologies                     Phone: (973) 560-4800

80 S. Jefferson Street                          Fax:    (973) 560-4806

Whippany, NJ 07981                          E-Mail: rossi@comverge-tech.com

C3 COMMUNICATIONS, INC

Stephen T. Bell

C3 Communications, Inc                    Phone: (512) 306-5843

2600 Via Fortuna, Suite 500               Fax:     (512) 306-5881

Austin, Texas 78746                           E-Mail: sbell@c3com.com

Eric Landis

C3 Communications

2600 Via Fortuna                                Phone: (512) 306-5870

Suite 500                                             Fax:     (512) 306-5889

Austin, Texas 78746                           E-Mail: elandis@C3com.com

E-MON CORP

Donald Millstein

E-MON Corp

One Oxford Valley Road                    Phone:  (800) 334-3666

Suite 418                                             Fax:      (215) 752-3094

Langhorne, PA 19047                         E-Mail:dmillstn@emon.com

Dave Bovankovich

E-Mon Corp.

One Oxford Valley Road                    Phone:  (800) 334-3666

Suite 418                                             Fax:      (215) 752-3094

Langhorne, PA 19047                         E-Mail:dbovank@emon.com

GENERAL ELECTRIC

David Ellis

General Electric                                  Phone:  (610) 954-9860

3740 Sydna Street                               Fax:      (610) 954-9865

Bethlehem, PA 18017                         E-Mail: david.ellis@indsys.ge.com

ITRON

Barry Goodstadt, Ph.D.

Vice President

Itron, Inc.                                            Phone: (410) 884-9365

P.O. Box 1160                                    Fax:     (410) 884-9367

Columbia, MD  21044                        E-Mail: barry.goodstadt@itron.com

MEASURING & MONITORING SERVICES INC.

Joseph Polaski

Measuring & Monitoring Services     Phone: (800) 942-2703 or (732)-530-3280

620 Shrewsbury Avenue                    Fax:    (732) 576-8067

Tinton Falls, NJ 07701                      E-Mail: jpolaski@mmsinc.com

OLAMETER INC.

John F. Payes

2000 McGill College, Suite 500        Phone: 514-982-6664

Montreal, Quebec, Canada                Fax:     514-982-6648

H3A 3H3                                           E-Mail: jpayes@olameter.com

PHASER ADVANCED METERING SERVICES

Tara Sachs

Phaser Advanced Metering Services  Phone: (505) 241-2646

400 Gold, SW, Suite 1200                  Fax:    (505) 241-4310

Albuquerque, NM 87102                    E-Mail: tara.sachs@phaser.com

POWER MEASUREMENT LTD.

Richard W. Stetler

Power Measurement, Ltd                    Phone: (250) 652-7149

2195 Keating Cross Road                   Fax:     (250) 652-0411

Saanichton, BC V8M2A5                   E-Mail: rick_stetler@pml.com

SARGENT ELECTRIC COMPANY

Richard A. Schwarz

Sargent Electric Company

c/o Virginia Power                              Phone: (804) 236-4799

2901 Charles City Road                      Fax:     (804) 236-4795

Richmond, VA 23231                         E-Mail: rschwarz@epix.net

SIEMENS POWER TRANSMISSION AND DISTRIBUTION, LLC.

Michael K Anderson

Siemens Power T & D

Metering Division                              Phone: (765) 429-1216

3601 Sagamore Parkway North         Fax:     (765) 742-0936

Lafayette, IN 47904                           E-Mail: michael.anderson@ptd.siemens.com

George D. Kostell

Siemens Power T & D

Meter Division                                 Phone:  (704)588-4660

P.O. Box 240451                              Fax:     (704) 588-4660

Charlotte, NC 28224-0451               E-Mail: george.kostell@ptd.siemens.com

SCHLUMBERGER

George C. Roberts

Schlumberger                                   Phone:  (770) 368-3461

5430 Metric Place                            Fax:      (770) 368-3425

Norcross, GA 30092                        E-Mail: groberts@norcross.rms.slb.com

Matt Swartz

Schlumberger                                      Phone:   (770) 368-3447

5430 Metric Place                               Fax:

Norcross, GA 30092-2550                 E-Mail: mswartz@newjughead.norcross.rms.slb.com

VOLUNTEER ENERGY CORPORATION

James Ryan

Volunteer Energy Corporation           Phone: (614) 882-2100

2602 Oakstone Drive                          Fax:     (614) 882-8154

Columbus, Ohio 43231                      E-Mail: jryan@volunteer-nrg.com

ELECTRICAL WORKER UNIONS

AFL-CIO/IBEW

**Mike Welsh, Secretary/Treasurer

Utility Workers/Pennsylvania

Utility Caucus                                     Phone:  (814) 535-7655

408-412 Broad Street                          Fax:      (814) 535-7657

Johnstown, PA  15906                        E-Mail: mikeibew@twd.net

*John Fitzkee

IBEW Local 1600

540 Grange Road                              Phone: (610) 395-8167

P.O. Box 470                                     Fax:     (610) 395-6158

Trexlertown, PA 18087                     E-Mail: ibewjohn@aol.com

UTILITY WORKERS UNION OF AMERICA LOCAL 102

Dale Dix                                            Phone: (724) 838-8883

1010 Hillcrest Drive                          Fax:     (724)-836-1288

Greensburg, PA   15601                    E-mail: daledix@westol.com

ENVIRONMENTAL

CLEAN AIR COUNCIL

* Michael Fiorentino, Esq.

Clean Air Council                             Phone:  (717) 541-1955

3700 Vartan Way                              Fax:      (717) 541-1970

Harrisburg, PA 17110                       E-Mail: mfioren@ paonline.com

** Brooks Mountcastle

Clean Air Council                             Phone:  (717) 541-1945

3700 Vartan Way                              Fax:      (717) 541-1970

Harrisburg, PA 17110                       E-Mail: bmount@paonline.com

CONSUMER

OFFICE OF CONSUMER ADVOCATE

* Tanya McCloskey

Office of Consumer Advocate           Phone: (717) 783-5048

14th Floor, Strawberry Square          Fax:     (717) 783-7152

Harrisburg, PA  17120                      E-Mail: paoca@ptd.net

AMERICAN ASSOCIATION OF RETIRED PERSONS (AARP)

Edward A. Essl

AARP

225 Market Street                              Phone: (717) 238-2277

Suite 502                                            Fax:     (717) 236-4078

Harrisburg, PA  17101                       E-Mail: Not Available

PENNSYLVANIA UTILITY LAW PROJECT

Harry Geller

Pa. Utility Law Project Director        Phone:  (717) 232-2719

118 Locust Street		                Fax:      (717) 233-4088

Harrisburg, PA  17101 	                E-Mail: HN0708@handsnet.org

MISCELLANEOUS

INDUSTRIAL ENERGY CONSUMERS OF PA (IECPA)

David Kleppinger, Esquire

McNees, Wallace & Nurick                 Phone:  (717) 237-5214

P. O. Box 1166                                     Fax:      (717) 237-5300

Harrisburg, PA  17108-1166               E-Mail: dkleppin@mwn.com

BOROUGH OF CHAMBERSBURG

Anthony C. Adonizio                         Phone: (717) 730-2052

250 North 24th Street                         Fax:     (717) 730-0719

Camp Hill, PA  17011                        E-Mail: acadon@ezonline.com

PEOPLES GAS

Philip Cancilla

Peoples Gas Company                        Phone:  (412) 244-2551

1201 Pitt Street                                   Fax:      (412) 244-2611

Pittsburgh, PA 15221                         E-Mail: Philip_J_Cancilla@corp.cng.com

PSE&G

Bill Nash

PSE&G                                              Phone: (973) 430-7970

80 Park Plaza, T25                             Fax:     (973) 824-0167

Newark, NJ 07102                             E-Mail: wnash@pseg.com

Jack Greenfeder

PSE&G                                               Phone: (973) 430-8691

80 Park Plaza                                      Fax:     (973) 824-0167

Newark, NJ 07101                             E-Mail: jgreenfe&pseg.com

Terence Moran

PSE&G                                               Phone:  (973) 430-7105

80 Park Plaza T25                              Fax:      (973) 824-0167

Newark, NJ 07102                             E-Mail: tmoran1@pseg.com

Glenn Powers

PSE&G                                              Phone:  (973) 912-3262

24 Brown Avenue                              Fax:      (973) 912-3226

Springfield, NJ 07081                        E-Mail: gpowers@pseg.com

X-ENERGY

Tom Michelman

X-Energy                                            Phone: (781) 273-5700 ext 363

3 Burlington Woods                           Fax:     (781) 273-9368

Burlington, MA 01803                       E-Mail: tmichelman@xenergy.com

PUBLIC UTILITY COMMISSION STAFF

Charles F. Covage

Bureau of CEEP

PA Public Utility Commission           Phone: (717) 783-3835

P.O. Box 3265                                    Fax:    (717) 787-2545

Harrisburg, PA 17105-3265               E-Mail: covage@puc.state.pa.us

Stephen Gorka

Law Bureau

PA Public Utility Commission           Phone: (717) 772-8840

P.O. Box 3265                                    Fax:    (717) 783-3458

Harrisburg, PA 17105-3265               E-Mail: gorka@puc.state.pa.us

COUNT: 81  MEMBERS

*   Metering Committee Member

** Metering Committee Alternate Member

ATTACHMENT 1

PENNSYLVANIA PUBLIC UTILITY COMMISSION

ADVANCED METER CATALOG

“GRANDFATHERED” ADVANCED METERS, METER-RELATED DEVICES AND/OR NETWORKS

APPROVED

MAY 13, 1999

TARIFF SUPPLEMENTS

APPROVED

JULY 15, 1999

ELIGIBLE FOR DEPLOYMENT

JULY 15, 1999

IN

THE FOLLOWING

JURISDICTIONAL ELECTRIC DISTRIBUTION COMPANIES (EDCs):

(A) EDCs Using a Competitive Advanced Metering Market-

(1) Allegheny Power System (APS);

(2) GPU Energy (GPU);

(3) PECO Energy Company (PECO); and

(4) Pennsylvania Power and Light Company (PP&L)

(B) EDCs Using a Non-Competitive Advanced Metering Market-

(1) Citizen’s Electric Company (Citizen’s);

(2) Duquesne Light Company (Duquesne);

(3) Pennsylvania Power Company (PennPower);

(4) UGI Utilities (UGI); and

(5) Wellsboro Electric Company.

# Footnotes

The full text of these documents is included on the Commission’s Website at puc.paonline.com.  Click on Electric Competition, Click on Advanced Metering.

Note: Entities that are not licensed EGSs that wish to provide services under the definition of advanced meter services provider may do so only as a subcontractor with the licensed EGS.  In that case the licensed EGS must submit the application for certification.

Note: The PECO Restructuring Settlement Agreement with the Commission established precedent material for the other settlements.

The above-referenced Commission staff will also monitor activities of the Electronic Data Interchange (EDI) Business Practices Working Group on Competitive Advanced Metering Issues which was established by the Commission in August 1999.