PENNSYLVANIA

PUBLIC UTILITY COMMISSION

Harrisburg, PA 17105-3265

Public Meeting held February 26, 2009

Commissioners Present:

James H. Cawley, Chairman

Tyrone J. Christy, Vice Chairman

Robert F. Powelson

Kim Pizzingrilli

Wayne E. Gardner

Implementation of the Alternative Energy

Portfolio Standards Act of 2004: Standard			M-00051865

Interconnection Application Forms

OPINION AND ORDER

BY THE COMMISSION:

On June 25, 2008, this Commission issued a Tentative Order at this docket proposing to establish standardized interconnection application and agreement forms in accordance with the Alternative Energy Portfolio Standards Act of 2004 (AEPS Act), 73 P.S. §§ 1648.1-1648.8, and our Regulations at 52 Pa. Code §§ 75.1 – 75.51.  The proposed standard application and agreement forms are intended to be used for all levels of review for proposed interconnection projects.  Different levels of review are required depending on the nameplate capacity of the generation equipment to be installed and the complexity of the project.  See 52 Pa. Code § 75.34.

The task of developing standard application forms and interconnection agreements for each level of interconnection request was assigned to the Interconnection Standards Working Group.  On November 17, 2006, a sub-group was formed to concentrate on development of the interconnection application and agreement forms.  The sub-group consisted of representatives from consumer interests, alternative energy system vendors, EDCs and the Energy Association of Pennsylvania.

In December of 2007, the Interconnection Standards sub-group finished its work on the proposed forms.  On December 19, 2007, Commission Staff forwarded the draft standard application and agreement forms to the full Interconnection Standards Working Group for comment.  Very few comments were received.  The Interconnection Standards sub-group reviewed and incorporated those comments into a draft of the standard application forms.  On February 13, 2008, Commission Staff forwarded the draft of the standard application and agreement forms to the full Interconnection Standards Working Group for comment.  Only one comment was received which recommended increasing certain nameplate capacity limits to be consistent with amendments to the AEPS Act.  The sub-group revised the draft standard application and agreement forms to address that single comment.

The work product of the sub-group was adopted and issued in the form of a Tentative Order entered June 25, 2008.  The proposed forms were also posted to the Commission’s website.  Very few comments were received.  However, the Department of Environmental Protection (DEP) advised that the forms posted on the Commission’s website contained several drop down menu boxes that failed to operate properly.  The forms were corrected and reposted to the Commission’s website.  On October 21, 2008, Commission staff advised the full Interconnection Standards Working Group of the corrected forms and extended the comment period to November 5, 2008.  Only two comments were filed in response to the corrected forms.

The comments received do not seek to alter the basic structure of the application forms and interconnection agreements.  The applications and interconnection agreements are split into two discrete formats.  First, Level 1 inverter-based systems with nameplate capacities of 10 kW or less, which have been certified per the Commission’s Regulations at 52 Pa. Code § 75.34(1)(ii), will be processed with a basic application form and agreement.  The application form is designed to provide the EDC with sufficient information at the beginning of the process to permit prompt action on the request and reduce the amount of time the EDC will need to evaluate and approve the interconnection.

The Interconnection Agreements for Levels 1 and 2-4 contain specific limitations on liability and indemnification provisions.  These provisions are consistent with the MADRI forms.  It should be noted that there is no requirement for insurance.  Final Rulemaking Re Interconnection Standards for Customer-generators pursuant to Section 5 of the Alternative Energy Portfolio Standards Act, 73 P.S. § 1648.5,

L-00050175 (Order entered August 22, 2006) at 19.

By their nature, Levels 2 through 4 interconnection requests are more complicated endeavors and cover a far broader range of equipment installations than a Level 1 interconnection request.  For that reason, the Level 2 through 4 standard forms advise prospective interconnection customers of the types of information that may be required by an EDC, but direct the customer to work directly with the EDC to determine the kinds of information needed to process the application.  As noted in the standard form, a Level 2, 3 or 4 interconnection may require several meetings with EDC personnel as well as engineering studies as required by the Commission’s Regulations.

The DEP filed comments to the forms proposed in our Tentative Order.  The DEP’s first comment involves the Interconnection Agreement form for Level 1 systems.  At page L-5 of the Application/Agreement, Terms and Conditions for Level 1 systems, there is a requirement for periodic testing of equipment.  The specific provision provides:

3.  Periodic Testing.  All interconnection-related protective functions and associated batteries shall be periodically tested at intervals specified by the manufacturer, system integrator, or authority that has jurisdiction over the Customer-Generator Facility interconnection.  Periodic test reports or a log for inspection shall be maintained.

The DEP expressed concern with the testing requirement as proposed.  The DEP states: “We recognize that this language was adopted from the MADRI forms and that its origin is the IEEE 1547 Standard however, we are concerned that testing may not be practicable for all systems and believe the wording is ambiguous.”  DEP Comments at 1.  The DEP suggests that this Commission should be the entity that sets the appropriate testing intervals and the manner of such testing.  Id. at 2.

We will not adopt the DEP’s suggestion on this issue.  As the DEP notes, this specific testing provision was adopted from the MADRI  process and also finds support in the applicable IEEE 1547 Standards.  We do not find that the proposed language is as ambiguous as the DEP suggests.  It is fairly straightforward.  In those instances where testing intervals and methods are not specified by the manufacturer or other independent body, those details can be agreed upon by the EDC and the Customer-Generator.  In the event that a Customer-Generator believes the EDC is unreasonable as to the testing method and appropriate intervals, the Customer-Generator can avail itself of the Commission’s arbitration process set forth in our Regulations at 52 Pa. Code § 75.51.

The next issue raised by the DEP is the concern that there is a standard form of Agreement Terms and Conditions for certified inverter-based Level 1 facilities, but no standard terms and conditions for Level 2 through 4 facilities.  The Department recommends that standard Agreement Terms and Conditions should attach to other facilities as well.  DEP Comments at 2.

Initially, we note that there is an Application Form which applies to Level 2 through 4 requests.  However, we agree with the DEP that a form Agreement should also attach to Levels 2 through 4.  Accordingly, we have used the existing Level 1 Agreement form and adapted it for use in Levels 2 through 4.  The form Agreement closely tracks the Commission’s Regulations at 52 Pa. Code §§ 75.21 through 75.51 by providing the various steps the parties will move through before a Customer-Generator’s generating facility may become fully operational on an interconnected basis.  We note that the same periodic testing provision is contained in the Level 2 through 4 Agreement that the DEP commented on in the Level 1 Agreement.  Our determination that the testing provision should remain as stated also applies here.

The DEP also commented that, in the Level 2-4 Interconnection Application Form at Page L2-1, there is an inquiry as to whether the Customer-Generator intends to export power.  The DEP expresses the concern that the final choice listed in the drop down menu box may not be appropriate due to recent changes in the net metering rules.  DEP Comments at 4.  The final choice provides for the possibility that the interconnection request contemplates “[s]ignificant annual export/No net-metering/IPP.”  This choice is to provide information to the EDC that the applicant intends to operate as an independent power producer without any net metering involved.

The DEP expresses its concern that this choice may be confusing to some applicants because certain changes to the net metering rules eliminated the requirement that net metering customers use their generating facilities to primarily offset some, or all, of their generating needs.  But it should be noted that this application applies to Levels 2 through 4 installations.  These review levels generally apply to more complex systems.  Accordingly, there will be greater interaction between EDCs and these applicants than a Level 1 installation.  In addition, it can be expected that Level 2 through 4 applicants, or their vendors, will be more knowledgeable about the process.  On that basis, we do not find that the choice presents as much possibility for confusion as suggested by the DEP.  If, over the course of time, we find this issue is a problem, we can readily address it by amending the Application form.

The sub-group has brought a concern to our attention regarding language in the heading of the Level 2 through 4 Application.  Currently, that heading provides that it is applicable to Applications involving “Generation up to 5,000 kW.”  The Sub-group advises that while the Act provides that interconnection may be requested up to 5,000 kW (5 MW), several issues arise as nameplate capacity of generation facilities reach 2,000 kW and above.  In many instances, generation facilities with nameplate capacities in excess of 2,000 kW would require interconnection at the transmission level.  Accordingly, it has been suggested that the heading be modified to read: “Applicants proposing to install generation approaching 2,000 kW or larger should contact the EDC for guidance in determining the appropriate application process.”

We agree with this suggestion and will modify the heading for the Level 2 through 4 Application form.  Preliminary discussions between EDCs and Customer-Generators who propose larger capacity installations will save time and expense over the course of the review process.  As always, in the event that a Customer-Generator believes that an EDC is requiring an inappropriate level of review, or requires interconnection at an inappropriate voltage level, recourse may be had through the mediation provisions at 52 Pa. Code § 75.51.  In our view, the capacity levels at issue here will involve parties with substantial technical and operational expertise.  It is unlikely that installations of this nature will require substantial Commission involvement.

CONCLUSION

Pursuant to Section 1648.5 of the AEPS Act, 73 P.S. § 1648.5, and Section 75.33 of the Commission’s Regulations, 52 Pa. Code § 75.33, we will adopt the standard Interconnection Application and Agreement Forms attached to this Opinion and Order as Appendix A; THEREFORE,

IT IS ORDERED:

1.  	That the standard Interconnection Application and Agreement Forms attached hereto as Appendix A are adopted for use by jurisdictional electric distribution companies for processing interconnection requests brought under the Commission’s Regulations at 52 Pa. Code §§ 75.1 through 75.51.

2.	That a copy of this Opinion and Order and Annex A be served upon the Commission’s Office of Trial Staff, the Office of Consumer Advocate, the Office of Small Business Advocate, all jurisdictional electric utility companies, licensed electric generation suppliers, the Pennsylvania Department of Environmental Protection and the Interconnection Standards Working Group.

3.	That the Secretary shall cause a copy of this Opinion and Order to be published in the Pennsylvania Bulletin.

- That copies of the Application and Agreement Forms attached as Appendix A shall be published on this Commission’s internet website.

5.	That jurisdictional electric distribution companies shall use the Application and Agreement Forms contained in Appendix A for interconnection requests processed under this Commission’s rules and Regulations.  Each jurisdictional electric distribution company shall have copies of the Application and Agreement Forms readily available and shall post copies of the Application and Agreement Forms on their respective internet websites.

BY THE COMMISSION

James J. McNulty,

Secretary

(SEAL)

ORDER ADOPTED:  February 26, 2009

ORDER ENTERED:  February 27, 2009

Appendix A

INTERCONNECTION APPLICATION/AGREEMENT - PART 1

With Terms and Conditions for Interconnection

For a Level 1 Review (Certified Inverter-based Units of 10kW and under)

(Application & Conditional Agreement – to be filled out prior to installation)

CUSTOMER GENERATOR CONTACT INFORMATION

Legal Name and Mailing Address of Customer-Generator: (if an Individual, Individual’s Name)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Contact Person (If other than Above):

Mailing Address (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Alternative Contact Information: (if different from Customer-Generator above)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The Customer-Generator Facility’s Information:

Facility Address:

City:      		State: PA	Zip Code:

Nearest Crossing Street:

Electric Distribution Company (“EDC”):

Account #:      		Meter #:

Current Annual Energy Consumption: 	      kWh 		Estimated In-service Date:

Application Fee Enclosed: 		Inverter Type;

Energy Source:  		Manufacturer:

Number of Units:      		Model Number of Inverter:

Inverter Rating:        kWAC 	Ampere Rating:       AmpsAC 	Number of Phases:

Voltage Rating:        VAC,	 DC Source Rating:        kWDC	Nominal DC Voltage:        VDC

Power Factor:        %, 	Frequency:       Hz,	IEEE1547/UL1741 Certification:

Utility Accessible Disconnect or Lock Box:

One-line Diagram Attached (Required): 	Site Plan Attached (Required):

Do you plan to export power?

If Yes, Estimated Maximum:       kWAC,	Estimated Gross Annual Energy Production:       kWh

Equipment Installation Contractor: (Indicate by owner if applicable)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Electrical Contractor:  (If applicable)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Customer-Generator Insurance Disclosure:

The attached Terms and Conditions contain provisions related to liability, and indemnification and should be carefully considered by the Customer-Generator. The Customer-Generator is not required to obtain liability insurance coverage as part of this Application/Agreement; however, the Customer-Generator is advised to consider obtaining appropriate coverage.

Customer-Generator Signature:

I hereby certify that: 1) I have read and understand the Terms and Conditions which are attached hereto by reference and are made a part of this Application/Agreement; and 2) to the best of my knowledge, all of the information provided in this Application/Agreement is true and I agree to abide by the attached Terms and Conditions, including the application process set forth therein.

Customer-Generator Signature: 	 	Date:

Printed Name: 	 	Title:

Conditional Approval to Interconnect Customer-Generator Facility: (for Use by EDC Only)

The requested information is complete and interconnection of the Customer-Generator Facility is approved contingent upon the Terms and Conditions of this Agreement, the return of a duly executed Certificate of Completion, verification of electrical inspection and successful witness test or EDC waiver thereof.

EDC Signature: 		Date:

Printed Name:      		Title:

Interconnection Application/Agreement

Terms and Conditions for Interconnection

For a Level 1 Review (Certified Inverter-based Units of 10kW and under)

- Construction of the Customer-Generator Facility. The Customer-Generator may proceed to construct (including operational testing not to exceed 2 hours) the Customer-Generator Facility once the approval to install the Customer-Generator Facility has been received from the Electric Distribution Company (EDC).

The Customer-Generator Facility shall be constructed in accordance with information provided in Part 1 of the Interconnection Application/Agreement, IEEE 1547 and the Commission’s regulations.

Once an Interconnection Request is deemed complete, any modification to the proposed Customer-Generator Facility that would affect the application review criteria for a Level 1 review that is not agreed to in writing by the EDC, shall require submission of a new Interconnection Request.

- Interconnection and Operation. The Customer-Generator may interconnect and operate the Customer-Generator Facility with the EDC’s system once all of the following have occurred:

  - Electrical Inspection:  Upon completing construction, the Customer-Generator will have the Customer-Generator Facility inspected or otherwise certified by the local electrical wiring inspection authority having jurisdiction over the Customer-Generator Facility.

  - Certificate of Completion: The Applicant shall provide the EDC with a completed copy of the Certificate of Completion, including evidence of the electrical inspection by the local authority having jurisdiction.  The evidence of completion of the electrical inspection may be provided on inspection forms used by local inspecting authorities.

  - Inspection:  The EDC has either completed its inspection or waived the right to inspection in the Application/Agreement as follows:

    - EDC Right of Inspection.  After receipt of the Certificate of Completion, the EDC will, upon reasonable notice (minimum of 10-days notice as noted in 2.3.2 below) and at a mutually convenient time, conduct an inspection of the Customer-Generator Facility and perform a Witness Test to ensure that all equipment has been appropriately installed and that all electrical connections have been made as required.

    - Witness Test. For Level 1 review projects only, if the EDC does not inspect the installation within the minimum notice period of 10 business days, or by mutual agreement of the Parties, the Witness Test is deemed waived.

  - Metering: Revenue quality metering equipment shall be installed and tested by the EDC.  (Note: The EDC may allow interconnected operations prior to the meter installation.)

  - Acceptance:  The EDC’s representative has signed Part 2, the Certificate of Completion, approving the facility for energization.

- Periodic Testing. All interconnection-related protective functions and associated batteries shall be periodically tested at intervals specified by the manufacturer, system integrator, or authority that has jurisdiction over the Customer-Generator Facility interconnection. Periodic test reports or a log for inspection shall be maintained.

- Safe Operations and Maintenance.  The Customer-Generator shall be fully responsible for the operation, maintenance and repair of the Customer-Generator Facility as required to ensure that the Customer-Generator Facility complies at all times with the interconnection standards it has been certified to meet.

- Access.  The EDC shall have access to the metering equipment and the disconnect/isolation device of the Customer-Generator Facility at all times.  The EDC shall provide reasonable notice to the Customer-Generator, when possible, prior to using its right of access.  In an emergency or outage situation, where there is no access to an AC disconnect/isolation device such as a switch or breaker, the EDC may disconnect the electrical service to the premises.

- Exterior AC Disconnect Switch / Isolation Device. Small generator facilities shall be capable of being isolated from the EDC by means of a lockable, visible-break isolation device accessible by the EDC. The isolation device shall be installed, owned and maintained by the owner of the small generation facility and located between the small generation facility and the point of interconnection. A draw-out type circuit breaker with a provision for padlocking at the draw-out position can be considered an isolation device for purposes of this requirement.

An interconnection customer may elect to provide the EDC access to an isolation device that is contained in a building or area that may be unoccupied and locked or not otherwise readily accessible to the EDC, by installing a lockbox provided by the EDC that shall provide ready access to the isolation device. The interconnection customer shall install the lockbox in a location that is readily accessible by the EDC and the interconnection customer shall permit the EDC to affix a placard in a location of its choosing that provides clear instructions to EDC operating personnel on access to the isolation device.  The interconnection customer, at its option, may provide and install both the lockbox & placard.

- Operations / Disconnection.  The EDC may temporarily disconnect the Customer-Generator Facility upon occurrence of the following conditions:

  - For scheduled outages upon reasonable notice,

  - For unscheduled outages or emergency conditions,

  - If the EDC determines that the Customer-Generator Facility does not operate in a manner consistent with this Application/Agreement.

  - If the EDC determines that continued operation of the Customer-Generator Facility is a safety hazard to the EDC’s personnel or to the general public.

  - In the event the interconnection equipment used by the Customer-Generator Facility is de-listed by the Nationally Recognized Testing Laboratory that provided the listing at the time the interconnection was approved and the EDC ascertains that continued operation has the potential to cause a safety, reliability or a power quality problem.

- Indemnification.  The Parties shall at all times indemnify, defend, and save the other Party harmless from, any and all damages, losses, claims, including claims and actions relating to injury to or death of any person or damage to property, demand, suits, recoveries, costs and expenses, court costs, attorney fees, and all other obligations by or to third parties, arising out of or resulting from the other Party's action or inactions of its obligations under these terms and conditions on behalf of the indemnifying Party, except in cases of gross negligence or intentional wrongdoing by the indemnified Party.

- Limitation of Liability.  Each party’s liability to the other party for any loss, cost, claim, injury, liability, or expense, including reasonable attorney’s fees, relating to or arising from any act or omission in its performance of these terms and conditions, shall be limited to the amount of direct damage actually incurred.  In no event shall either party be liable to the other party for any indirect, incidental, special, consequential, or punitive damages of any kind whatsoever.

- Termination.  This Application/Agreement may be terminated under the following conditions:

  - By Customer-Generator.  The Customer-Generator may terminate this Application/Agreement by providing written notice to the EDC.

  - By the EDC. The EDC may terminate this Application/Agreement if the Customer-Generator fails to remedy a violation of terms of this Application/Agreement upon written notice and a reasonable opportunity to cure.

- Permanent Disconnection.  In the event the Application/Agreement is terminated, the EDC shall have the right to disconnect its facilities or direct the Customer-Generator to disconnect its Customer-Generator Facility.

- Survival Rights.  This Application/Agreement shall continue in effect after termination to the extent necessary to allow or require either Party to fulfill its rights or obligations that arose under the Application/Agreement.

- Assignment/Transfer of Ownership of the Customer-Generator Facility: This Application/Agreement shall survive the transfer of ownership of the Customer-Generator Facility to a new owner unless the new owner terminates this Application/Agreement and so notifies the EDC in writing.  The EDC will be responsible for contacting the new customer to execute a new Application/Agreement or assignation agreement, in order for the new owner to be treated as a Net Metering customer.

- Definitions. The capitalized terms used herein, and the definitions of such terms, are as those used in regulations adopted by the Pennsylvania Public Utility Commission at 52 Pa. Code § 75.22, relating to Interconnection Standards and Definitions.

- Notice. Unless otherwise provided in this Application/Agreement, any written notice, demand, or request required or authorized in connection with this Application/Agreement (“Notice”) shall be deemed properly given if delivered in person, delivered by Electronic Mail (E-mail) delivered by recognized national courier service, or sent by first class mail, postage prepaid, to the person specified below:

If to EDC:

The contact listed on the EDC website as the primary contact for the EDC listed in the Customer-Generator’s Facility Information section on Page 1 of the Interconnection Application/Agreement.

If to Customer-Generator:

The contact listed in the Legal Name and Mailing Address of Customer-Generator section on Page 1 of the Interconnection Application/Agreement.  The Customer-Generator is responsible for notifying the EDC of any change in the contact party information.

In the event the original applicant sells or otherwise transfers ownership of the property listed in the Customer-Generator Facility’s Information section listed on Page 1 of the Interconnection Application/Agreement, the original applicant shall provide the EDC with the appropriate contact information for the new owner of the property.  Upon any subsequent transfer of ownership, the then current owner shall provide the EDC with the new owner’s information.

INTERCONNECTION APPLICATION/AGREEMENT - PART 2

With Terms and Conditions for Interconnection

For a Level 1 Review (Certified Inverter-based Units of 10kW and under)

(Final Agreement – to be filled out after installation)

Certificate of Completion

Customer Generator Information

Legal Name and Mailing Address of Customer-Generator (if an Individual, Individual’s Name)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Mailing Address (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The Customer-Generator Facility’s Information:

Facility Address:

City:      		State: PA  Zip Code:

Nearest Crossing Street:

Electric Distribution Company (“EDC”):

Account #:      		Meter #:

Inverter Type;     Energy Source:

Number of Units:       	   Manufacturer:

Model Number of Inverter:       		Inverter Rating:        kWAC

(Attach additional sheets as necessary in the event of multiple units of various types/sizes)

Equipment Installation Contractor:			Check if owner-installed:  ()

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The undersigned asserts that the Equipment has been installed in accordance with Part 1 of the Interconnection Application/Agreement as well as all applicable codes and regulations.

Signed: 	  Date:

Printed Name:      		Title:

Electrical Contractor: (if Different from Equipment Installation Contractor)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The undersigned asserts that the Equipment has been installed in accordance with Part 1 of the Interconnection Application/Agreement as well as all applicable codes and regulations.

Signed: 	  Date:

Printed Name:      		Title:

Electrical Inspection:

The system has been installed and inspected in compliance with the provisions of the National Electrical Code and other applicable codes and standards as well as the local Building/Electrical Code of:

(Appropriate Governmental Authority)

By:  	  	Date:

Customer-Generator Signature:

The Customer-Generator Facility is complete and ready for interconnected operation in accordance with all of the provisions of the Interconnection Application/Agreement.  The Customer-Generator acknowledges that it shall not operate the Facility until receipt of Final Acceptance (below), or as otherwise provided for by regulation.

Signed: 	  Date:

Printed Name:      		Title:

Final Acceptance to Interconnect Small Generator Facility (for Use by EDC Only)

The requirements for interconnection are complete and interconnection of the Customer-Generator Facility is accepted upon signature and return of this Certificate of Completion by the EDC, below:

Electric Distribution Company waives Witness Test?    (Initial)	Yes	(          )	No	(          )

If no, Successful Witness Test Date:       		Passed: (Initial)   (           )

EDC Signature: 		Date:

Printed Name:      		Title:

INTERCONNECTION APPLICATION

For a Level 2, 3 or 4 Review – Applicants proposing to install generation approaching 2,000 kW or larger should contact the EDC for guidance in determining the appropriate application process.

(To be filled out and submitted prior to installation)

CUSTOMER GENERATOR CONTACT INFORMATION

Legal Name and Mailing Address of Customer-Generator: (if an Individual, Individual’s Name)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Contact Person (If other than Above):

Mailing Address (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Alternative Contact Information: (if different from Customer-Generator above)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The Customer-Generator Facility’s Information:

Facility Address:

City:      		State: PA	Zip Code:

Nearest Crossing Street:

Electric Distribution Company (“EDC”):

Account #:      		Meter #:

Existing Service Voltage:	      VAC	Existing Service Capacity:        Amps	 Phase

Current Annual Energy Consumption: 	      kWh 		Estimated In-service Date:

Do you plan to export power?

If Yes, Estimated Maximum:       kWAC,	Estimated Gross Annual Energy Production:       kWh

One-line Diagram Attached (Required): 	Site Plan Attached (Required):

Energy Source:  		Gross Generator Rating:       kWAC

Utility Accessible Disconnect or Lock Box:

Requested Level of Review: 			Type of Generation Equipment:

Equipment Installation Contractor:       Indicate by owner if applicable

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Electrical Contractor: (If Applicable) 	   Indicate if not applicable

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Consulting Engineer: (If Applicable)        Indicate if not applicable

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Application Fee:

The Applicant shall deposit a not refundable application fee which is approved by the Pennsylvania Public Utility Commission and is listed on the EDC’s Website. Depending on the level of review and nature of the energy generating equipment, additional study and review fees, as permitted by Pennsylvania Public Utility Commission Regulations may be required and are not a part of the aforementioned application fee.

Application Fee Enclosed: 	Amount:

Customer-Generator Insurance Disclosure:

General Liability Insurance coverage is not required under the Pennsylvania Public Utility Commission’s Regulations. However, the Customer still has responsibility and/or liability for any damage(s) or injury(ies) caused by the Customer-Generator Facility and/or the Customer’s Interconnection Facilities.  The Customer-Generator is advised to consider obtaining appropriate coverage.

Customer-Generator Signature:

I hereby certify that to the best of my knowledge, all of the information provided in this Application is accurate.

Legal Name of Customer-Generator:

Customer-Generator Signature: 	 	Date:

Printed Name: 	 	Title:

Customer-Generator Equipment Information for Inverter Based Systems

(May be applicable to a Level 2, 3 or 4 Review)

DC Source information;

Energy Source:

DC Source Rating:        kWDC

Nominal DC Voltage:        VDC

Ampere Rating:       Amps DC

Inverter Information:

Inverter Manufacturer:

Inverter Type;

Model Number of Inverter:

Number of Units:

Inverter Rating:        kWAC

Voltage Rating:       VoltsAC

Ampere Rating:       AmpsAC

Power Factor:        %,

Number of Phases:

Frequency:       Hz,

IEEE1547/UL1741 Certification:

Evidence of Certification attached:

Customer-Generator Equipment Information for Parallel Rotating Equipment Based Systems

(May be applicable to a Level 3 or 4 Review)

It is anticipated that many projects proposing to utilize directly coupled rotating generation may not have the specific information necessary for the EDC to adequately evaluate the impact of the proposed facility on the EDC’s electrical distribution system at the time of the initial application.  Often times the equipment for which this information is needed hasn’t been specified.  The type information necessary may be conveyed during a scoping meeting or other correspondence early on during the project development.  Depending on the nature of the project, this is often an iterative process.  Different EDC’s analytical systems may require that data be provided conforming to specific standard formats which will be conveyed by the EDC.  While not all inclusive, examples of the information commonly required are as follows:

For Synchronous Machines:  Copies of the Saturation Curve and the Vee Curve - Salient vs. Non-Salient - Torque: (lb-ft) - Rated RPM - Field Amperes at rated generator voltage and current and % PF over-excited - Maximum Leading and Lagging Reactive Output Power - Type of Exciter - Output Power of Exciter - Type of Voltage Regulator - Direct-axis Synchronous Reactance (Xd) ohms  - Direct-axis Transient Reactance (X'd) ohms  - Direct-axis Sub-transient Reactance (X"d) ohms - Rated Nominal Frequency

For Induction Machines: Rotor Resistance (Rr) ohms - Exciting Current (Amps) - Rotor Reactance (Xr) (ohms) - VARs (No Load) - Magnetizing Reactance (Xm) - Stator Resistance (Rs) - VARs (Full Load) - Stator Reactance (Xs) – Short Circuit Reactance (X"d) - Number of Phases - Frame Size - Design Letter - Temp. Rise oC

Protective Equipment:  The Customer-Generator shall design a protective scheme that will provide the protective functions specified in IEEE 1547 and submit it to the EDC for review & acceptance.  The submittal shall include a single line drawing showing the location of instrument transformers (current and voltage) and the location of the relays, breakers and fuses. Indicate the manufacturer and model number of each type of device.  Breaker data shall include continuous and interrupting ampere ratings.  If relays are used, indicate function, the tripping source and its voltage.

Isolation Transformer:  Manufacturer - Manufacturer reference number - Nominal Voltage Ratio – High / Low Voltage Taps - Number of Units - Rated kVA – Percentage Impedance @ kVA base – High / Low Voltage Winding Configuration

Level 2, 3 or 4 Interconnection Agreement

This Interconnection Agreement ("Agreement") is made and entered into this       day of , , by The , ("Electric Distribution Company” or “EDC"), and       ("Customer-Generator"), each hereinafter sometimes referred to individually as "Party" or both referred to collectively as the "Parties".  In consideration of the mutual covenants set forth herein, the Parties agree as follows:

- Scope of Agreement -- This Agreement sets forth the conditions under which the EDC and the Customer-Generator agree that one or more generating facilities as further described in Attachment A, with an installed nameplate gross capacity of       kW ("Facility” or “Facilities”) may be interconnected to the EDC's distribution system.  This Agreement is applicable to interconnection requests governed by the rules and Regulations of the Pennsylvania Public Utility Commission.

- Construction of the Customer-Generator Facility. The Customer-Generator may proceed to construct (including operational testing not to exceed 2 hours) the Customer-Generator Facility once the approval to install the Customer-Generator Facility has been received from the EDC.  The Customer-Generator Facility shall be constructed in accordance with information provided in the Interconnection Application, IEEE 1547 and the Pennsylvania Public Utility Commission’s Regulations.

The Applicant shall notify the EDC of any changes to the proposed Customer-Generator Facility that would be subject to the criteria for a Level 2, 3 or 4 review (E.G., Inverter Manufacturer/Model Number, Size, etc.).

Once an Interconnection Request is deemed complete, any modification to the proposed Customer-Generator Facility that would affect the application review criteria for a Level 2, 3 or 4 review that is not agreed to in writing by the EDC, shall require submission of a new Interconnection Application, subject to the provisions of the Pennsylvania Public Utility Commission’s rules and Regulations.

- Interconnection and Operation. The Customer-Generator may interconnect and operate the Customer-Generator Facility with the EDC’s system once all of the following have occurred:

  - Electrical Inspection:  Upon completing construction, the Customer-Generator shall have the Customer-Generator Facility inspected or otherwise certified by the local electrical wiring inspection authority having jurisdiction, that the facility meets the requirements of the National Electric Code.

  - Certificate of Completion: The Applicant shall provide the EDC with a completed copy of the Certificate of Completion, including evidence of the electrical inspection by the local authority having jurisdiction.  The evidence of completion of the electrical inspection may be provided on inspection forms used by local inspecting authorities.

  - Inspection:  The EDC has either completed its inspection or waived the right to inspection in this Agreement.  After receipt of the Certificate of Completion, the EDC may, upon reasonable notice and at a mutually convenient time, conduct an inspection of the Customer-Generator Facility and observe a Witness Test to ensure that all equipment has been appropriately installed and that all electrical connections have been made in accordance with its requirements.

  - Metering: Revenue quality metering equipment shall be installed and tested by the EDC.  (Note: The EDC may allow interconnected operations prior to the meter installation.)

  - Acceptance:  The EDC’s representative has signed and returned the Certificate of Completion or provided notification by electronic mail or other acceptable means that the requirements for interconnection are complete and interconnection of the Customer-Generator Facility is accepted for parallel operation.

- Periodic Testing. All interconnection-related protective functions and associated batteries shall be periodically tested at intervals specified by the manufacturer, system integrator, or authority that has jurisdiction over the Customer-Generator Facility interconnection. Periodic test reports or a log for inspection shall be maintained.

- Safe Operations and Maintenance.  The Customer-Generator shall be fully responsible to operate, maintain, and repair the Customer-Generator Facility as required to ensure that the Customer-Generator Facility complies at all times with the interconnection standards it has been certified to meet.

- Access.  The EDC shall have access to the metering equipment and the disconnecting means of the Customer-Generator Facility at all times.  The EDC shall provide reasonable notice to the Customer-Generator, when possible, prior to using its right of access.  In an emergency or outage situation, where there is no access to an AC disconnecting means such as a switch or breaker, the EDC may disconnect the service to the premises.

- Exterior AC Disconnect Switch / Isolation Device. Small generator facilities shall be capable of being isolated from the EDC by means of a lockable, visible-break isolation device accessible by the EDC. The isolation device shall be installed, owned and maintained by the Customer-Generator and located between the small generation facility and the point of interconnection. A draw-out type circuit breaker with a provision for padlocking at the draw-out position can be considered an isolation device for purposes of this requirement.

A Customer-Generator may elect to provide the EDC access to an isolation device that is contained in a building or area that may be unoccupied and locked or not otherwise readily accessible to the EDC, by installing a lockbox provided by the EDC that shall provide ready access to the isolation device. The Customer-Generator shall install the lockbox in a location that is readily accessible by the EDC and the Customer-Generator shall permit the EDC to affix a placard in a location of its choosing that provides clear instructions to EDC operating personnel on access to the isolation device.  The Customer-Generator, at its option, may provide and install both the lockbox and placard.

- Operations / Disconnection.  The EDC may temporarily disconnect the Customer-Generator Facility upon occurrence of the following conditions:

  - For scheduled outages upon reasonable notice,

  - For unscheduled outages or emergency conditions,

  - If the EDC determines that the Customer-Generator Facility does not operate in a manner consistent with this Application/Agreement,

  - If the EDC determines that continued operation of the Customer-Generator Facility is a safety hazard to the EDC’s personnel or to the general public,

  - In the event the interconnection equipment used by the Customer-Generator Facility is de-listed by the Nationally Recognized Testing Laboratory that provided the listing at the time the interconnection was approved and the EDC ascertains that the continued operation has the potential to cause a safety, reliability or a power quality problem.

- Indemnification.  The Parties shall at all times indemnify, defend, and save the other Party harmless from, any and all damages, losses, claims, including claims and actions relating to injury to or death of any person or damage to property, demand, suits, recoveries, costs and expenses, court costs, attorney fees, and all other obligations by or to third parties, arising out of or resulting from the other Party's action or inactions of its obligations under these terms and conditions on behalf of the indemnifying Party, except in cases of gross negligence or intentional wrongdoing by the indemnified Party.

- Limitation of Liability.  Each party’s liability to the other party for any loss, cost, claim, injury, liability, or expense, including reasonable attorney’s fees, relating to or arising from any act or omission in its performance of these terms and conditions, shall be limited to the amount of direct damage actually incurred.  In no event shall either party be liable to the other party for any indirect, incidental, special, consequential, or punitive damages of any kind whatsoever.

- Termination.  This Application/Agreement may be terminated under the following conditions:

  - By Customer-Generator.  The Customer-Generator may terminate this Application/Agreement by providing written notice to the EDC.

  - By the EDC. The EDC may terminate this Application/Agreement if the Customer-Generator fails to remedy a violation of terms of this Application/Agreement upon written notice and a reasonable opportunity to cure.

- Permanent Disconnection.  In the event the Application/Agreement is terminated, the EDC shall have the right to disconnect its facilities or direct the Customer-Generator to disconnect its Customer-Generator Facility.

- Survival Rights.  This Application/Agreement shall continue in effect after termination to the extent necessary to allow or require either Party to fulfill its rights or obligations that arose under the Application/Agreement.

- Assignment/Transfer of Ownership of the Customer-Generator Facility: This Application/Agreement shall survive the transfer of ownership of the Customer-Generator Facility to a new owner unless the new owner terminates this Application/Agreement and so notifies the EDC in writing.  The EDC will be responsible for contacting the new customer to execute a new Application/Agreement or assignation agreement, in order for the new owner to be treated as a Net Metering customer.

- No Third Party Beneficiaries - This Agreement is not intended to and does not create rights, remedies, or benefits of any character whatsoever in favor of any persons, corporations, associations, or entities other than the Parties, and the obligations herein assumed are solely for the use and benefit of the Parties, their successors in interest and, where permitted, their assigns.

- No Waiver - The failure of a Party to this Agreement to insist, on any occasion, upon strict performance of any provision of this Agreement will not be considered to waive the obligations, rights, or duties imposed upon the Parties.

- Definitions. The capitalized terms used herein, and the definitions of such terms, are as those used in ANNEX A, TITLE 52. PUBLIC UTILITIES, PART 1. PUBLIC UTILITY COMMISSION, Subpart C., FIXED SERVICE UTILITIES, CHAPTER 75: ALTERNATIVE ENERGY PORTFOLIO STANDARDS, Subchapter C: “INTERCONNECTION STANDARDS.”

- Notice. Unless otherwise provided in this Application/Agreement, any written notice, demand, or request required or authorized in connection with this Application/Agreement (“Notice”) shall be deemed properly given if delivered in person, sent by Electronic Mail (E-mail), sent by recognized national courier service, or sent by first class mail, postage prepaid, to the person specified below:

If to EDC:

The contact listed on the EDC website as the primary contact for the EDC listed in the Customer-Generator’s Facility Information section on Attachment A of this Interconnection Agreement.

If to Customer-Generator:

The contact listed in the Legal Name and Mailing Address of Customer-Generator section on Attachment A of this Interconnection Application.  The Customer-Generator is responsible for notifying the EDC of any change in the contact party information.

In the event the original applicant sells or otherwise transfers ownership of the property listed in the Customer-Generator Facility’s Information section listed on Attachment A of the Interconnection Agreement, the original applicant shall provide the EDC with the appropriate contact information for the new owner of the property.  Upon any subsequent transfer of ownership, the then current owner shall provide the EDC with the new owner’s information.

- Governing Law and Regulatory Authority - This Agreement shall be governed by, interpreted, construed, and enforced in accordance with the laws of the Commonwealth of Pennsylvania.  This Agreement is subject to, and the Parties' obligations hereunder include, operating in full compliance with all valid, applicable federal, state, and local laws or ordinances, and all applicable rules, regulations, orders of, and tariffs approved by, duly constituted regulatory authorities having jurisdiction.

- Multiple Counterparts -- This Agreement may be executed in two counterparts, each of which is deemed an original but all constitute one and the same instrument.

IN WITNESS WHEREOF, the Parties have caused this Agreement to be signed by their respective duly authorized representatives.

Customer-Generator

BY:  		BY:

NAME:       		NAME:

TITLE:       		TITLE:

DATE:       		DATE:

ATTACHMENT A

DESCRIPTION OF FACILITY

For a Level 2, 3 or 4 Review Interconnection Agreement

CUSTOMER-GENERATOR CONTACT INFORMATION

Legal Name and Mailing Address of Customer-Generator: (if an Individual, Individual’s Name)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Contact Person (If other than Above):

Mailing Address (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

Alternative Contact Information: (if different from Customer-Generator above)

Name:

Mailing Address:

City:      		State:      	Zip Code:

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The Customer-Generator Facility’s Information:

Facility Address:

City:      		State: PA	Zip Code:

Account #:      		Meter #:

Do you plan to export power?

If Yes, Estimated Maximum:       kWAC,	Estimated Gross Annual Energy Production:       kWh

One-line Diagram Attached (Required): 	Site Plan Attached (Required):

Energy Source:  		Gross Generator Rating:       kWAC

Utility Accessible Disconnect or Lock Box:

ATTACHMENT B

CERTIFICATE OF COMPLETION

For a Level 2, 3 or 4 Review Interconnection Agreement

Customer-Generator Information

Legal Name and Mailing Address of Customer-Generator (if an Individual, Individual’s Name)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Mailing Address (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The Customer-Generator Facility’s Information:

Facility Address:

City:      		State: PA  Zip Code:

Nearest Crossing Street:

Electric Distribution Company (“EDC”):

Account #:      		Meter #:

Inverter Type;     Energy Source:

Number of Units:       	   Manufacturer:

Model Number of Inverter:       		Inverter Rating:        kWAC

(Attach additional sheets as necessary in the event of multiple units of various types/sizes)

Equipment Installation Contractor:			Check if owner-installed:  ()

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The undersigned asserts that the Equipment has been installed in accordance with of the Interconnection Application as well as all applicable codes and regulations.

Signed: 	  Date:

Printed Name:      		Title:

Electrical Contractor: (if Different from Equipment Installation Contractor)

Name:

Mailing Address:

City:      		State:        Zip Code:

Contact Person (If other than Above):

Telephone (Daytime):      		(Evening):

Facsimile Number:      		E-Mail Address:

The undersigned asserts that the Equipment has been installed in accordance with the Interconnection Application as well as all applicable codes and regulations.

Signed: 	  Date:

Printed Name:      		Title:

Electrical Inspection:

The system has been installed and inspected in compliance with the provisions of the National Electrical Code and other applicable codes and standards as well as the local Building/Electrical Code of:

(Appropriate Governmental Authority)

By:  	  	Date:

Customer-Generator Signature:

The Customer-Generator Facility is complete and ready for interconnected operation in accordance with all of the provisions of the Interconnection Application/Agreement.  The Customer-Generator acknowledges that it shall not operate the Facility until receipt of Final Acceptance (below), or as otherwise provided for by regulation.

Signed: 	  Date:

Printed Name:      		Title:

Final Acceptance to Interconnect Small Generator Facility (for Use by EDC Only)

The requirements for interconnection are complete and interconnection of the Customer-Generator Facility is accepted upon signature and return of this Certificate of Completion or by notification by electronic mail or other acceptable means by the EDC.

Electric Distribution Company waives Witness Test?    (Initial)	Yes	(          )	No	(          )

If no, Successful Witness Test Date:       		Passed: (Initial)   (           )

EDC Signature: 		Date:

Printed Name:      		Title:

# Footnotes

“MADRI” is the acronym for Mid-Atlantic Demand Resource Initiative, a regional group which has been addressing interconnection standards and logistics.  As noted in our Tentative Order, it was determined that the starting point for Pennsylvania’s forms and standards would be the MADRI work product.  Tentative Order at 2.

Completion of local inspections may be designated on inspection forms used by local inspecting authorities.

As a condition of interconnected operation, you are required to send/fax/e-mail a completed signed copy of this Certificate of Completion to your EDC at the address in the Terms & Conditions for Interconnection.

Customers proposing to install generation greater than 2,000 kW are required to contact their EDC for the appropriate application procedures.

Completion of local inspections may be designated on inspection forms used by local inspecting authorities.

As a condition of interconnected operation, you are required to send/fax/e-mail a completed signed copy of this Certificate of Completion to your EDC at the address in the Terms & Conditions for Interconnection.